------------------------------------------------------------------------

		VSN: Volume Serial Number Utility V1.0

		 Copyright (C) 1989 By John F. Stetson

			  All Rights Reserved

------------------------------------------------------------------------

VSN.COM is utility program which is  used  to  manage  DOS  Disk  Volume
Serial Numbers.  It operates on IBM-PC compatible computer systems using
the IBM PC-DOS or Microsoft  MS-DOS  Operating	System	Version  2.0  or
higher.

Disk Volume Serial Numbers were introduced with DOS 4.0.  When a disk is
formatted by FORMAT or copied with  DISKCOPY,  an  8  digit  hexadecimal
Volume Serial Number is automatically placed in the Boot Sector  of  the
disk.  Subsequent execution of the  DOS  CHKDSK, DIR, LABEL, TREE or VOL
command will cause the Volume Serial Number to	be  displayed.	However,
no mechanism is provided for the user to create a specified VSN,  change
an existing VSN, or to delete  an  existing  VSN.  The	VSN.COM  utility
provides these functions.

Perhaps even more useful is its ability to perform these  functions  for
disks formatted under ANY version of DOS from 2.0 through  4.0,  and  it
can be executed under ANY version of DOS  from	2.0  through  4.0.  This
greatly enhances the possible benefits of using Volume Serial Numbers.

The main reason for using Volume Serial Numbers is to establish a unique
means of identifying a disk.  Disks may have identical Volume Labels  or
even identical Directories, but may still contain different data.  Since
DOS 4.0 forces the user to accept the VSN it selects for a disk, and the
method used is based on the current  time,  each  VSN  will  be  unique.
However, this means that the assigned VSN's follow  no  logical  pattern
and are difficult to relate to one another.  The VSN utility retains the
benefits of the concept, but allows the user to  establish  a  numbering
scheme which can be used to form a disk cataloging sequence which  makes
sense, and is compatible with the format used by DOS 4.0.

The DOS command line syntax is as follows:

VSN [drive:] [xxxx-xxxx] [/d]

where all parameters are optional.  If no parameters are specified, help
information is displayed.  If a drive letter is specified,  the  current
Volume Serial Number is displayed, or the user	is  informed  that  none
exists.  If an 8 hexadecimal digit value is specified, the VSN	for  the
specified drive is changed to  the  specified  value.  If  no  drive  is
specified, the current drive is used.  VSN's are  always  specified  and
displayed as 4 hex digits (0-9 or A-F), followed by a dash (-), followed
by 4 hex digits.  The /d switch causes the current VSN for the specified
drive to be deleted.

Error Messages

Unable to Read Disk Boot Sector - an error occurred when trying to  read
the boot sector for the specified drive.

Unable to Locate System Boot Code - there was no jump instruction at the
start of the boot sector for the specified drive.

Insufficient Room for Volume Serial Number - the  data	area  after  the
jump instruction in the boot sector was too small to contain the VSN.

Unable to Write Disk Boot Sector - an  error  occurred	when  trying  to
write the boot sector for the specified drive.

Status Messages

Drive D: Has No Disk Volume Serial Number
Drive D: Old Disk Volume Serial Number is: XXXX-XXXX
Drive D: New Disk Volume Serial Number is: XXXX-XXXX
Drive D: Volume Serial Number Deleted

Examples of Use

VSN C: - display the VSN (if any) for drive C:

VSN C: 0001-0002 - create or change the VSN for drive C:

VSN A: 1989-0001 - create or change the VSN for drive A:

VSN C: /D - delete the VSN for drive C:

------------------------------------------------------------------------