Modifying Modem Programs to Operate at 450 Baud

As you are probably aware,  most 300 Baud  modems will operate at
speeds	greater  then 300 Baud.  Since source code is not  easily
available on most modem programs, below is a method to modify the
ones that do not support 450 Baud. (I haven't found any that do).

The  method  I	use is to modify one of the Baud  rates  that  is
supported to 450 Baud. I picked 1200 in both examples below, if I
had a 1200 Baud modem I would not be doing this.

Each  of the examples are done somewhat differently but the basic
procedure  remains the same.  It is necessary to know the  values
of the various Baud rates used by the hardware. They are:

     9600 BAUD = 000C
     4800 BAUD = 0018
     2400 BAUD = 0030
     1200 BAUD = 0060
      600 BAUD = 00C0
      450 BAUD = 0100
      300 BAUD = 0180
      110 BAUD = 0417

GENERAL PROCEDURE

1.  Make  a  copy of the program to modify and rename it with  an
extension other then COM, EXE, or HEX.

2. Load the program under debug
     Example: A>debug xtalk.mod

3. Use	search	feature of debug to find value of  Baud  rate  to
change.
     Example: -s100 f000 60 00
     Note:  that the value you are looking for will be in  memory
in reverse order from the above table.

4. In most cases debug will report several places where the value
occurs	in  memory,  use the unassemble comand to  determine  the
correct  value	to  change.  If there are several that	might  be
correct my only suggestion would be to change them one at a  time
and test between changes. (Not very fool proof)

5.  After  necessary changes then use the write feature to  store
changes on the disk.
     Example: -w

6. Rename the file back to the correct extension.

7. Run the file to test it and good luck.

Caution:  While in debug do not attemp to run the file.  It  will
not work and the system will get lost.

Modifing Crosstalk

1. Load file under debug

2.  Search for 60 00. There will probably  be  two areas at  B6AA
and C866.  The C866 is the correct area. If you dump the area you
will  see  all the Baud rates followed by the two bytes  for  the
hardware setup.

3. Back up four bytes to where the 1200 starts and enter 0450 and
the 0 , 1
     Example: -ec863
     XXXX:C863 31.30	 32.34	   30.35     30.30     60.0
	       00.1	 36.

     Note:  The  value	to the left of the decimal point  is  the
value in memory, to the right is the value to change it to.

4. Write file back to disk.

     Note:  Since it is known that two	ASCII  zeroes  are before
the hardware value, if the search string is changed to -s100 f000
30  30	60  00, then it should only report one occurance of  that
string.

Modifying Minitel

1. Load file under debug

2. Search for 60 00. There will likely	be several locations. The
area around 1700 is the correct area. If you unassemble this area
you  will see some Mov	 BX instructions with the hardware values
being loaded.

3. Change the 60 00 to 00 01.

4. Write file back to disk.

     Note:  Since  it  is  now known that MOV BX  is  before  the
hardware value, if the search string is changed to -s100 f000  BB
60 00, it should only report one occurrence of that string.

Misc Notes:

     1.  Crosstalk  will  show	0450  Baud  on	the  screen  when
selected.  In Minitel you  have to  select 1200 but  it will work
at 450.
     2.  With both of the systems only the first character  needs
to be input when selecting a Baud rate. A 0 for Crosstalk and a 1
for Minitel.

	    David Paul
he first character  needs
to be input when selecting a Baud rate. A 0 for Crosstalk and a 1
for Minitel.