- ---=-==============================================================-=--- -
--=--======== WAVE - Brainwave Synchronization Voice File maker  ========--=--
 - ---=-==============================================================-=--- -
________               
OVERVIEW  The WAVE program generates Sound Blaster .VOC voice files that,
________  when listened to with stereo headphones, will synchronize your
brainwave patterns into any desired state.  This program is probably unlike
any others in your repetoire, but is well worth having if only to help you
get a good nights sleep!  Scientists have long known that different brainwave
frequencies are associated with different states of mind.  With this program,
you can create files to generate states ranging from deep sleep and medita-
tion, to wide awake and alert.
____________
REQUIREMENTS  * Lots of hard drive space.  Files are always stereo at 22K, 
____________    which take approximately 2.64 megabytes per minute.
              * Patience.  Depending on the machine, files could take anywhere
                from the file's play time to 5 times the playing time. Without 
                a coprocessor, calculations could take 6 times longer still.
                But once the file is generated, it can be archived, or even 
                recorded on tape for future use.
              * Open mind.  Yes, it works better on people who take this
                seriously and give the sounds a chance to "work".  It really
                DOES work!  Within minutes, I can achieve the desired state.
              * Sound Blaster capable of playing 22K stereo .VOC files
              * Stereo headphones, it only works with headphones.
__________
THE AUTHOR  That's me, David Johnston.  I have been working with programs 
__________  like this, and other so called meditation tapes and machines, for
a number of months now, and have found that the sounds this program creates 
are very powerful.  I work at a very well known software company, and have a
Sound Blaster at home.  By the way, this program is absolutely FREE, so please
give it to anyone you like.  The important thing is that more people be able
to experience what these sounds can do for them.  And yes, there are many
uses, which will be explained in more detail later.  But hey, if you WANT to
reward the author in some way, let me know how the program has worked for you,
and any enhancements you'd like to see?  I'll leave my address and an email
route at the end of this document.  Have fun!
______________________________
WHAT AM I GETTING MYSELF INTO?  This program works like many meditation tapes
______________________________  and light/sound devices on the market, which
range in price from $200 to $500.  There's even a board available with plug
in glasses (which have blinking lights) for your PC for $495.  I think the
files this creates are even more powerful, and are definitely more pleasing
to the ears.  Most other devices and tapes have a "humming" sound or some
other tones to induce the write brainwave frequencies.  This program has the
option of tones (which I never use), but also has a waterfall noise, and 
allows you to use your own recordings, and turn them into brainwave syncro-
nization recordings.
  Here's a list of the four major brainwave patterns:
  
  Beta:    > 13 hz    Normal state of alertness, stress and anxiety.
  Alpha:   8-12 hz    State of light relaxation, state of "superlearning",
                      positive thinking
  Theta:   4-7 hz     Deep relaxation, meditation, increased memory and focus
  Delta:   1-3 hz     Deep sleep, lucid dreaming, increased immune functions


______________
USING WAVE.EXE  There are two programs provided, WAVE.EXE for those who do not
______________  have a math coprocessor or 486, or 586, etc., and WAVE87.EXE
for those fortunate enough to own a math coprocessor, or 486, or 586, etc.

Usage:  WAVE <dest-file.VOC> <source-script.WV>
        <dest-file.VOC> is name of the .VOC brainwave file you want to create
        <source-script.WV> is the .WV script file used to describe how to
             generate the .VOC file.

There are many sample .WV files you can look at, or you can create your own
custom file as outlined below.

____________________
SAMPLE THETA.WV FILE
____________________

{Comments can go inside curley braces}  ;Or after a semicolon on the same line
source=noise of 10   ;Nice waterfall noise
source=inverse       ;Sum of left+right channels is 0 (silence)
source=wave of 0.0833hz from -10 to 10  ;Pan source left and right once every
                                        ;12 seconds.  Nice effect!

{  Start from beta and glide down to upper theta 
   The separation is how pronounced the brainwave effect is 
   So start with no effect and end up with an effect of 8     }
wave from 20hz separation 0 to 7.5hz sep 8 in 40 seconds
                                           
{ Now cycle between low theta and high theta about once every 30 seconds }
wave from 7.5hz sep 8
       to 4.5hz sep 12 for 5 minutes 10.5 cycles

{ We ended at 4.5hz (because of the .5 cycles), stay there for a while }
wave of 4.5hz for 3 minutes

{ Now go back up to beta to wake up! }
wave to 20hz sep 0 in 30 seconds



__________________
FORMAT OF .WV FILE  These are just ordinary text files with instructions for
__________________  the wave program.  The file is checked for correct syntax
before the .VOC file is generated.  Here are the main sections, which may
be repeated in any order.  The only restriction is that an input must be
specified before doing the brainwave pattern creation (WAVE...) on it.

 COMMENTS  Comments should be inside curley braces, or after semicolons.

 INPUTS    Choose one of the following:
 
           source=noise of <loudness>
           <loudness> is from 3 to about 30 (I usually use 10).  This produces
           a nice waterfall/rushing river sound which is greate for relaxation

           source=tone of <freq> hz
           <freq> is the frequency in Hertz of the tone to use.  Tones of 90
           to about 300 should work best, although I prefer the noise sounds
           instead

           source=file <filename.VOC>
           <filename.VOC> is the 22K stereo file to use as the source input.
           If you have MONO 22K files, you can use the PHASE utility to convert
           it to stereo (PHASE monofile.VOC stereofile.VOC N).  The file will
           be looped if it is smaller than the destination.  

 PREP      Choose one of the following:
           
           source=mono
           The left and right channels are the input's (L+R)/2.  This just
           sounds like standard mono.

           source=inverse
           The left channel gets (L+R)/2, the right channel gets -(L+R)/2.
           Sounds seem as if they are coming from the center of your head.

           source=stereo
           This leaves the left and right channels untouched.

 SPATIAL   Chose one of the following, or leave out entirely:
           
           source=wave of 0 at <location>
           <location> is the spot where your brain will think the sound is
           coming from.  Negative locations are on the left, while positive
           locations are on the right.  Locations less than -20, or greater
           than 20 have no more effect than just using -20 or 20.

           source=wave of <frequency> hz from <location1> to <location2>
           Cycle the perceived source of the sound from <location1> to 
           <location2> and back again every 1/<frequency> seconds.  This gives
           nice special effects for relaxation by moving the source around,
           which enhances the effects of the brainwave pattern being used.

           source=wave ... theta <degrees>
           End a source=wave line with a starting point.  If <location1> is
           on the left (negative) and <location2> is on the right, a <degrees>
           of 180 will start at the right, a <degrees> of 90 will start in the
           middle, etc.


 WAVES     These are the actual brainwave patterns, and duration of each.

           wave of <frequency> hz for <time-secs> seconds
           wave of <frequency> hz for <time-mins> minutes
           Generate a brainwave frequency of <frequency> hz (frequencies to
           use are described throughout this document, and should be between
           1 and about 20 hz.  This is a Real number, so decimal amounts like
           7.554 are OK).  The duration iw for <time-secs> seconds, or in
           <time-mins> minutes if you prefer minutes.  The <time-mins> may
           also be a decimal value.

           wave from <freq1> hz to <freq2> hz in <time> [minutes/seconds]
           The <time> parameter works the same as above.  Brainwave patterns
           will glide smoothly from <freq1> hz to <freq2> hz.

           wave from <freq1> hz to <freq2> hz in <time> seconds <cyc> cycles
           In this case, the frequency will oscillate between <freq1> and
           <freq2> a number of <cyc> times in <time> seconds.  With whole 
           number values for <cyc>, the ending frequency will be <freq1>,
           for <cyc> ending in .5, the ending frequency will be <freq2>.  This
           is handy to know, so you don't end up suddenly jumping from one
           frequency to another (unless you want to?!?)

           wave from <freq1> hz sep <sep1> to <freq2> hz sep <sep2> in...
           The separation parameter may be added to adjust the intensity of
           the encoded brainwave pattern.  An intensity separation of 0 means
           no pattern, whereas an intensity of about 15 is the maximum.  So
           an intensity of less than 2 will have very little effect on the 
           brain.  Usually, lower intensities are used for higher frequencies.
           I use about 10-12 for frequencies less than 7hz, and 4-10 for those
           above 7hz.

           wave to <freq> hz in...
           If the from section is ignored, the previous frequency and 
           separation values where the last wave ended at are used as the 
           starting point.

           Please look at the sample files if you need more clarity on how
           to define a wave entry.
____________
ENHANCEMENTS  Use the MIX program provided to mix two brainwave .VOC files
____________  together.  I have tried a 4-7hz cycling wave that is spacially
located from -15 to -2 (cycling every 12 seconds) mixed with another 4-7hz 
cycling wave (with slightly different frequencies and cycle times) spacially 
located from 2 to 15 (cycling every 15 seconds).  The MIX program is pretty
self explanitory.  The <proportions> are in percent, so if both files are
mixed at 100, the resultant file could be twice as lound, and may clip.  
Mixing with values that sum to 100 is a good starting place.  You can mix your
own subliminal messages at, say 15 and keep the brainwave file at 100.
The <time> in the MIX command is the time of the resultant mixed file, and
should be the length of the longest of the two files being mixed.



_________
MANY USES  * Relaxation 
_________    Choose between 5hz and 10 hz for different levels of relaxation.
           * Meditation
             Choose between 4hz and 7hz, either cycle between a few, or stay
             at a particular frequency for different results.
           * Induce Sleep
             Choose between 4hz and 6hz for starters, then go into frequencies
             below 3.5hz, settling on about 1.5hz to 2.5hz for sleep.
           * Creative Visualization
             About 6hz for a while, then up to 10hz works well.
           * Stress Reduction
             Any use of frequencies below 11hz will reduce stress.
           * Self Hypnosis
             Choose about 8hz to 10hz while playing any self-hypnosis tape, 
             or guided meditation.
           * Super Learning
             Choose about 7hz to 9hz while playing any learning tapes, like
             foreign language tapes, etc. to increase comprehension.
           * Subliminal Programming
             Choose 5hz to 7hz while playing your favorite subliminal tapes,
             or make your own by recording a .VOC file with your messages,
             and mixing it with your brainwave .VOC file at a bearly audible
             volume.
           * Improve ESP / Intuition
             Theta frequencies help in this area, 4hz to 7hz.
           * Reaching Higher States of Consciousness
             Theta again.
           * Quick Refresher on long days
             Low Alpha 8hz to 10hz works well.
           
________________________
UNSOLICITED TESTIMONIALS
________________________
Note: Any results gained from using Light/Sound devices such as the Voyager, 
      the Brain Machine, MasterMind, the MindsEye, etc. can be gained from 
      listening to these files as well.  Some of these excerpts are from 
      results using flashing light goggles with tones.

This is my own testimonial.  I find that within minutes of listening to a 
thetawave pattern, my thoughts start drifting to really weird stuff that
doesn't make any sense at all.  It is really quite funny some of the things
I find myself thinking of.  Then I start to feel really "good" and relaxed--
at peace if you will.

It has been stated in several places that a half hour a day of the brain
being in the theta state can replace up to 4 hours of sleep.  People find
they need less sleep at night.

Thirty patients had sessions in Theta (5 hz) and experienced relaxation 
states of 80-100% after five minutes as well as improved pain relief.  Eight
patients had blood tests before and after the sessions and showed improved 
beta-endorphin levels of 10-50%.



Using a first-generation prototype light/sound device, one doctor noted,
"these devices produce a distinct relaxation state.  Programming the device
between 3 and 7 hz, it takes about 10 to 15 minutes for the patients to
enter--effortlessly--a state of hypnosis.  They terminate the sessions
relaxed and with a feeling of well-being."  Also, "the device has a calming
effect on the nervous or anxious patients.  In a majority of cases, the 
patients feel relaxed, and calm during a period of three to four days after
the session.  It happnes that the subjects have a reminiscence of childhood
experiences, particularly when in Theta.  The related their experineces which
we incorporated into our psychotherapeutic program."

"The machine works like a tranquilizer and the effect lasts for several days.
Using the machines in Theta frequency, clients are very receptive to 
suggestions on behavioral aspects such as reducing tobacco, alcohol and food 
consumptions."  Many patients "were more creative during the sessions."

"By inducing hemispheric coherence the machine can contribute to improved 
intellectual functioning of the brain.  Like children spending most of their 
time in Theta, the machine allows a reduction in learning time.  With adults
a return into Theta allows them to rediscover childhood experiences.  The
machine is like a 'lost and found office' for the subconscious."

D.J. Anderson, B.Sc., M.B., "The treatment of Migraine with Variable
Frequency Photo-Stimulation," in HEADACHE, March 1989, pp 154-155:
  D.J. Anderson used photo-stimulating goggles with variable frequency using
  red LEDs in order to stimulate the optic nerve, through closed eyes, right 
  and left with frequencies between 0.5 and 50 hz.  The study included
  seven patients who suffered a total of more than 50 migraines during the 
  observation period.  Forty-nine of these migraines were relieved (either
  by reducing the average duration or by increasing the frequency interval
  in between migraine crisis) and 36 other migraines could be stopped while
  using the goggles.

The more these sounds are used, the easier it becomes to produce and maintain
Alpha/Theta rhythms.  As these states of higher awareness become infused into
normal brain activity, the result can lead to what some have called a fifth
state of consciousness, or an "awakened mind."  In this state of illumination
and bliss one sees the world as distinctly as before but with a new mind that
perceives the universe with new meaning.  It's this experience of illumination
that is the seed for all breakthrough scientific theories, literary ideas,
revolutionary inventions, and artistic masterpieces.  The technology used
here induces these states by forcing your brain to focus your mental energies
inward... tapping your own vast reserve of creative genius and eventually
unfolding "an enlightened state of awareness."

  An unusual side benefit of listening to these sounds is a surprising need
for less sleep.  SOme users are able to reduce their sleep requirement by as
much as 3 - 4 hours each night, rising each morning feeling refreshed as if 
they had slept a full 8 hours.  The reason?  It's believed the theta-sounds 
replace the need for extensive dreaming which is the main purpose of sleep.  
  Another interesting side effect, many users report a dramatic increase in
sex drive.  No one knows exactly why, but it may be linked to changes in brain
chemistry.
  But, perhaps the most unusual side effect is the reported increase in
psychic functioning, including episodes of precognition, out-of-body
experiences, and spontaneous channeling events.



When you finish each session your entire body becomes charged with a new energy
and vitality.  Fears and anxieties are gone.  You are renewed, more alert, and
mentally you feel on top of the world.

What causes the euphoria and peak experiences?  The neuroscientists say the
'high' you experience is caused by a release of endorphins in the brain.  A
hundred times more powerful than morphine it makes you feel like you're 
soaring with eagles.

Zen meditators have been found to alter Alpha/Theta frequency according to
their depth of meditation, reports Japan's leading neurophysiologist, Dr.
Tomio Hirai.  he has correlated brain-wave patterns with certain stages of
meditation.  And according to Dr. Hirai, "Meditation is not merely a state
between mental stability and sleep, but a condition in which the mind operates
at the optimum.  In this condition the person is relaxed but ready to accept
and respond positively to any stimulus that may reach him."

Research now confirms that brainwave rhythms correspond to certain states of
consciousness, and this suggests that individuals capable of altering their
brainwave patterns can have significant control over other mental and physio-
logical functioning.  As Elmer and Alyce Green of the famous Menninger
Institute first reported in the mid-70's, "...simply causing your brain to
generate theta activity for a few meinutes each day seems to have enormous
benefits, including boosting the immune system, enhancing creativity, and 
triggering integrative experiences leading to feelings of psychological
well-being."

Biofeedback researchers have found that people who enter the "theta state,"
expande their states of consciousness, acquire super-receptivity to new
information, and demonstrate a greater ability to "rescript" material on a
subconscious level.  Even more astonishing are the findings of a study
conducted on a group of chronic alcoholics at a University in Colorado.  After
13 weeks the group that learned to generate theta and alpha brainwaves, showed
a far greater recover rate, and a complete transformation of personality.
There is a remarkable body of evidence...

Another Note:  I did not do alot of proper citing, I just wanted to present
               some information that is available "out there".

_______________
MAILING ADDRESS  David Johnston
_______________  3702 167th PL NE, H-3025
                 Redmond, WA  98052
                 (please, no mail after 1994... who knows where I'll be then)

email: "beaver.cs.washington.edu!microsoft!davej@beaver.cs.washington.edu"
       (I know it's long, but it works)