Digitized Voice Programmer's Toolkit for the PC
               -----------------------------------------------

                               Version 2.0

             Copyright (c) 1988,1989,1990,1991 Farpoint Software

                 Construction Notes for the Voice Digitizer

------------------------------------------------------------------------------

This document assumes that you are building the digitizer by hand from the
schematic. It will supply details of the circuit that may not be apparent
from the schematic. It will also recommend certain construction and operation
practices for best results. Some portions of this file are duplicated in
the file VOICEKIT.DOC.


Here is a parts list:

     |  Estim. | Estim.|
     |Sgl. Unit| Net   |
Quan |  Cost   | Cost  | Type     | Description                Ref. Des.
========================================================================

  1      .75      .75               MINI PHONO JACK            J1
  1     1.00     1.00               SMALL 3-TERMINAL BLOCK     J2
  1     2.50     2.50               DB25 FEMALE RIGHT ANGLE    J3
                                     P.C. BOARD MOUNT CONN.
  1      .25      .25               MOMENTARY (N.O.)           S1
                                     PUSHBUTTON SWITCH
  1     1.50     1.50               DPDT SWITCH                S2
  1     1.00     1.00   LF347N      QUAD OPAMP                 U1
  1      .50      .50   LM1458N     DUAL OPAMP                 U2
  1      .50      .50   MC1488P     RS232 DRIVER               U3
  1      .75      .75   CD4019BE    QUAD AND/OR SEL            U4
  1     3.50     3.50   LF398N      S/H AMPLIFIER              U5
  1     6.00     6.00   ADC0841CCN  A/D CONVERTER              U6
  1      .75      .75   MC1489A     RS232 RECEIVER             U8
  1      .75      .75   LM78L05ACZ  5-VOLT REGULATOR           U9
  6      .25     1.50   1N4148      SIGNAL DIODE               D1,D2,D3,
                                                                D4,D5,D6
  1      .25      .25               RED LED                    D7
  1      .25      .25               GREEN LED                  D8
  1      .50      .50               100K TRIMPOT               R8
  1      .50      .50               200k TRIMPOT               R24
  2      .25      .50               .0022UF POLYESTER CAP      C8,C9
  2      .25      .50               .0039UF POLYESTER CAP      C6,C7
 12      .25     3.00               .1UF CERAMIC CAP           BP2,BP4,BP6,
                                                                BP8,BP10,BP12,
                                                                BP13,BP14,BP15,
                                                                BP16,C3,C15


  1      .50      .50               .33UF POLYESTER CAP        C14
  2      .75     1.50               1UF POLYESTER CAP          C4,C5
  2      .10      .20               100PF CERAMIC CAP          C1,C2
  1      .75      .75               100PF MICA CAP             C12
  4      .75     3.00               10UF TANTALUM CAP          C10,C11,C13,C16
  8     1.00     8.00               22UF TANTALUM CAP          BP1,BP3,BP5,
                                                                BP7,BP9,BP11,
                                                                BP17,BP18
  2      .15      .30               1K .25W METAL FILM RES.    R5,R6
  2      .06      .12               2.2K .25W CARBON RES.      R17,R19
  1      .06      .06               3.3K .25W CARBON RES.      R15
  2      .06      .12               10K .25W CARBON RES.       R10,R22
  4      .06      .24               12K .25W CARBON RES.       R11,R12,R13,R14
  1      .06      .06               22K .25W CARBON RES.       R7
  2      .06      .12               33K .25W CARBON RES.       R2,R20
  2      .06      .12               39K .25W CARBON RES.       R1,R3
  1      .06      .06               68K .25W CARBON RES.       R4
  2      .06      .12               100K .25W CARBON RES.      R18,R23
  1      .06      .06               220 OHM .25W CARBON RES.   R21
  2      .06      .12               27 OHM .25W CARBON RES.    R25,R26


The costs in this list are ONLY ESTIMATES, based on rounded averages of prices
from several sources. Note that this document was written in December 1991,
and that prices will change over time. Parts cost may vary widely, depending
on the vendor, so consider shopping around. This parts list includes only the
actual circuit components. You will also need a prototype board, a soldering
iron, solder, chip sockets if desired, wire-wrap sockets and tools if wire-
wrap techniques are to be used, and whatever screws and other hardware might
be needed if you intend to mount the device in an enclosure. In addition, you
will need two 9-volt batteries or a split power supply, a microphone, and a
full DB-25 "straight through" cable.

There are two locations in the schematic where redundant components are
shown in order to increase versatility or availability:
    (1) Use EITHER R9 and R16 OR trimpot R24, but not both;
         R24 is recommended.
    (2) Use EITHER U4 OR U7, but not both; selection depends on availability.

The power supply pins for several of the integrated circuits are not shown
on the schematic in order to reduce clutter. This is a list of all the
integrated circuits, their package pin counts, and their power supply and
ground pins. In some cases, the power supply pins may already be shown on
the schematic.

  Ref. Des.      Part Type    Pin Count    Ground    +5       +9       -9
  ---------      ---------    ---------    ------   ----    -----    -----
     U1          LM348N          14          --      --        4       11
     U2          LM1458N          8          --      --        8        4
     U3          MC1488P         14           7      --       14        1
     U4          CD4019BE        16           8      16       --       --
     U5          LF398N           8          --      --        1        4
     U6          ADC0841CCN      20          10      20       --       --
     U8          MC1489A         14           7      14       --       --


All the capacitors shown in parallel groups in the lower left area of the
schematic are power supply bypass capacitors. Their purpose is to provide
each IC with isolation from the noise induced on the power supply rails by
the other parts of the circuit. These capacitors should be distributed around
the board so that each power supply pin of each IC is connected directly to
a bypass capacitor or a pair of bypass capacitors whose other terminal is
solidly connected to ground. Components U1, U2, and U5 should have two bypass
capacitors per power supply pin: one 0.1 uF and one 22 uF tantalum.

This is a list of which bypass capacitors are to be associated with (connected
to the power supply pins of) each IC:

    IC Ref. Des.      Bypass Cap Ref Des.
    -----------       -------------------
        U1            BP1, BP2, BP7, BP8
        U2            BP3, BP4, BP9, BP10
        U3            BP17, BP18
        U4            BP13
        U5            BP5, BP6, BP11, BP12
        U6            BP14
        U8            BP15

Capacitor BP16 would theoretically be associated with U7 if used instead
of U4. Connect capacitors C11 and C13 near the power switch. C14, C15, and
C16 should be connected directly to the leads of regulator U9. Note that the
power pins of U3 are not connected directly to the supply, but draw their
power through R25 and R26 in order to reduce U3's contribution to power
supply noise.

In some cases, depending on the exact board layout, the presence or absence
of a ground plane, and the relative noise level and proximity of the power
source, is may be possible to eliminate some of the bypass capacitors without
any noticeable effect. However, since the factors influencing this are
difficult to calculate, we suggest that you use all of the bypasses shown
when the project is initially constructed. Extra unneeded bypass capacitors
cause no harm, but missing bypasses, in spots where they are needed, can
functionally disable the device.

If a pin on a part is shown connected to nothing, and furthermore if it
shows no "netname" label (pin numbers don't count), then it should in fact
be left unconnected.

Some points in the schematic should be connected together even though there
are no lines joining them. This follows the "netname" convention. Any two
points (wires) on the schematic which possess identical net name labels
are actually interconnected. For example, there are four places showing the
label "VREF". These should all be connected together.

If possible, use a prototype board which has a "ground plane". This is a
continuous metal sheet covering the entire board except for clearances to
allow pins to pass through holes. If your prototype board has a ground plane,
then every pin which requires a ground connection should be connected directly
to the metal ground sheet at the location of the pin.


Try to position the parts on the board to minimize the length of the
interconnecting wires between the parts. Keep all wires as short and direct
as possible. Once all components are wired into the circuit, inspect the
unit carefully, noting in particular that all diodes and polarized capacitors
are oriented correctly. If you used sockets (strongly recommended), remove
all ICs from their sockets. Leave U9 in place, even if it is socketed. Apply
power to the unit, being VERY careful not to connect it backwards. Turn on the
power switch and use a voltmeter to measure the voltages (relative to ground)
on each power supply pin of each empty socket, as shown in the table of power
supply pins above. If your supply is, for example, (+) and (-) 12 volts
instead of 9 volts, then 12 volts should be substituted for 9 in the table.
The pins that are specified as being +5 volt pins are driven by linear
regulator U9, and should read between +4.8 and +5.2 volts as long as the
incoming positive supply is +7.5 volts or higher. Any pin which shows an
incorrect voltage is almost certainly an indication of a wiring error.

After all power supply pins have been verified, disconnect the supply and
install all the ICs into their sockets, being careful to observe the proper
orientation. Reconnect the supply (with the power switch off), plug in a
microphone, and connect a DB-25 "all wires straight through" cable from the
digitizer to a COM port on your PC. Adjust R24 and R8 to their midpoints.
Turn the digitizer power switch on. Run the program ADJUST.EXE, provided
with this toolkit. Press the <F2> key until the display indicates the COM port
number to which the digitizer is connected. Adjust R24 until the DC offset
reading on the screen is zero. The signal level reading should be flickering
slightly, and should be less than about 20. Don't expect zero here. Speak into
the microphone, and the signal level should momentarily jump up to a much
higher value. Adjust R8 so that the "clipping" indicator LED on the digitizer
board flickers on during the loudest peaks of normal speech. The digitizer
should at this point be working correctly.

If the noise level (idle signal level) is too high, one or more of the
following could be the cause: (1) Room background noise; try turning off fans,
air conditioners, etc. Also keep the microphone away from the PC itself.
(2) Local sources of radiated electrical noise. Common culprits are video
monitors, transformers, and particularly desktop fluorescent lamps.
(3) Excessively noisy power supply. (4) U1 is defective or has a bad solder
joint. (5) Improper connection of power supply bypass capacitors.

As a final test, press the <Esc> key to exit from ADJUST, then execute VDFE.
Press the <F2> key until the display indicates the COM port number to which
the digitizer is connected. Then press the <F3> key, wait until VDFE says
"go" (one second later), and say a few words into the microphone. Press the
spacebar to end the recording, then press the <F4> key to play it back. You
should hear the recording played through the PC speaker.