ENABLE READER 4.0         OPERATIONS MANUAL         CHAPTER 5-1

 
          CHAPTER 5  TALKING TUTORIAL PROGRAMMER'S AID 
 
 
5.0  INTRODUCTION 
 
The Talking Tutorial Programmer's Aid is designed for the  
experienced assembly level programmer.  Interfacing between  
higher level lanuguages such as PASCAL and C BASIC are possible,  
yet we do not provide these bridges.  There are ten calls that  
can be accessed through the INT 21 MSDOS Supervisor Call  
structure.  Load the correct registers with the values  
necessary, and then do INT 21.  Enable Reader 4.0 will save all  
registers except the FLAGS, where the ZERO Flag will be set if  
the call was not one of the available Enable Reader 4.0  
Functions.  The Enable Reader Programmer's Aid will check to see  
if the instruction was successfully completed.   
 
When writing tutorials with the Enable Reader 4.0 System, the  
information that is printed to the screen will be spoken.  Most  
of the tutorial will just use this feature.  The Programmer's  
Aid is designed to provide byte I/O to the synthesizer without  
printing the information to the video screen, and to use Help  
Functions in the Enable Reader 4.0 program to enhance the way  
data will be spoken.  For example, if you need to speak  
something in a way that would be confusing to the student if it  
were printed to the screen, such as spelling out a word or line,  
it is possible to send the data through the Enable Reader 4.0  
driver to the synthesizer in Spell Mode.  This can be used to  
great advantage with programs that teach spelling and reading  
skills.   
 
 
5.1  FUNCTION CALLS 
 
The following calls can be made to the INT 21 Call in MSDOS by  
loading the AH Register with FE HEX (254 Decimal), and then  
loading the AL register with the appropriate Ascii Character  
designated to call the function.   
 
The Enable Reader Driver is both Stream Oriented and  
Hierarchical in design.  This means that entry points are  
accumulative, and data passing through the driver's other entry  
points gains the same attributes.  By using byte-stream  
programming, and not using macros and calls to each subroutine,  
the data is processed more rapidly.   
 
The three most used entry points are:  1) DRIVER OUTPUT Call  
that sends a byte through the driver using all the Help  
functions that may be turned on, and the Punctuation routines;  
2) DIRECT OUTPUT Call that sends a byte directly to the  
synthesizer, bypassing the driver and the punctuation filter;  
and 3) MESSAGE OUTPUT Call that turns off the Help functions in  
the driver, and still allows for punctuation filtering.  The  
DIRECT OUTPUT Call will allow 8 bits to be sent, while the other  
two will only allow 7 bits.   
 







ENABLE READER 4.0         OPERATIONS MANUAL         CHAPTER 5-2


It has taken three years and fourteen versions of the program to  
identify speech primitives, assign hierarchy to Help Functions,  
integrate Punctuation Levels, and provide the four Entry Points;  
so that when you drop a byte in the top, it comes out the bottom  
without using look-up tables or macros.   
 
The Enable Reader Driver has a Character Filter and an Ascii  
Sort Routine.  The Character Filter filters out all bytes over  
80 HEX (graphics), and sends all bytes under 20 HEX (Control  
characters) to the Punctuation Level Routines.  This allows no  
graphic characters to pass through the driver.  It is possible  
to send 8 bit bytes to the synthesizer through the DIRECT OUTPUT  
call below.   
 
 
                 TALKING TUTORIAL FUNCTION CALLS 
 
DRIVER OUTPUT                   FUNCTION 01 
 
The DRIVER OUTPUT Call will output the character in DL through  
the Enable Reader driver, without turning off the Help  
Functions.  It will be filtered by the Ascii sort routine in the  
Enable Reader Driver, and if it is punctuation it will be sent  
according to the Level of punctuation selected.   
 
See:  DIRECT OUTPUT to send a byte directly to the synthesizer. 
See:  MESSAGE OUTPUT for sending a byte with Help Functions 
      turned off. 
 
ENTRY CONDITIONS: 
 
AL=01H 
AH=FEH 
DL=Character To Output 
 
 
 
 
DIRECT OUTPUT                   FUNCTION  02 
 
The DIRECT OUTPUT Call will send the byte in DL directly to the  
synthesizer, bypassing the Enable Reader driver and Ascii filter  
sort routine.   
 
ENTRY CONDITIONS: 
 
AL=02H 
AH=FEH 
DL=Character To Output 
 
 
 
 










ENABLE READER 4.0         OPERATIONS MANUAL         CHAPTER 5-3


MESSAGE OUTPUT                  FUNCTION  03 
 
The MESSAGE OUTPUT Call allows character filtration and  
punctuation, but turns off the Help Functions in the driver.   
 
ENTRY CONDITIONS: 
 
AL=03H 
AH=FEH 
DL=Character To Output 
 
 
 
 
AUTO                            FUNCTION  A 
 
The AUTO Call turns on or off the Spell Mode.  Read the  
discussion on AUTO in Chapter 4 Section 4.2 Help Keys.   
 
ENTRY CONDITIONS: 
 
AL=41H (ASCII A) 
AH=FEH 
 
 
 
 
PUNCTUATION LEVELS              FUNCTION  N 
 
The PUNCTUATION LEVELS Call selects one of five Punctuation  
Character Sets that can be accessed.  The fifth level is "Output  
Punctuation", which allows all Ascii characters to be sent to  
the synthesizer without being filtered or translated into the  
Enable Reader 4.0 Punctuation Words.  Read the discussion on  
PUNCTUATION LEVELS in Chapter 4 Section 4.2 Help Keys.   
 
ENTRY CONDITIONS: 
 
AL=4EH (ASCII N) 
AH=FEH 
 
 
 
 
HELP WORD LEVELS                FUNCTION  O 
 
The HELP Call selects one of four levels of Help in Enable  
Reader 4.0.  By selecting "No Help" at the start of your  
program, you can use the other Help Functions without having  
them speak their prompts.  Read the discussion on HELP WORDS in  
Chapter 4 Section 4.2 Help Keys.   
 
ENTRY CONDITIONS: 
 
AL=4FH (ASCII O) 
AH=FEH 
 
 
 
 



ENABLE READER 4.0         OPERATIONS MANUAL         CHAPTER 5-4


QUIT                            FUNCTION  Q 
 
The QUIT Call will stop the synthesizer from speaking.  For a  
discussion on the QUIT Function, read Chapter 4 Section 4.5  
Command Keys.   
 
ENTRY CONDITIONS: 
 
AL=51H (ASCII Q) 
AH=FEH 
 
 
 
 
LETTER-TO-WORD TRANSLATOR       FUNCTION  Z 
 
The TRANSLATOR Call turns on or off the Letter-To-Word  
Translator.  For a discussion on the TRANSLATOR Function, read  
Chapter 4 Section 4.2 Help Keys.   
 
ENTRY CONDITIONS: 
 
AL=5AH (ASCII Z) 
AH=FEH 
 
 
 
 
UPPER CASE IDENTIFICATION       FUNCTION  T 
 
The UPPERCASE IDENTIFICATION Function turns on or off the  
identification of capital letters.  For a discussion on the  
UPCASE Function, read Chapter 4 Section 4.2 Help Keys.   
 
ENTRY CONDITIONS: 
 
AL=54H (ASCII T) 
AH=FEH 
 
 
 
 
VIDEO OUTPUT                    FUNCTION  V 
 
The VIDEO OUTPUT Call turns on or off the output to the  
synthesizer from data that is printed on the video screen.  For  
a discussion on the VIDEO Function, read Chapter 4 Section 4.6  
System Keys.   
 
ENTRY CONDITIONS: 
 
AL=56H (ASCII V) 
AH=FEH 
 
END OF   CHAPTER 5  TALKING TUTORIAL PROGRAMMER'S AID