CAKEWALK TO ENSONIQ VFX TRANSFER ROUTINES

Title: CW--VFX.TXT								    Date: 10/09/89
__________________________________________________________________________
PURPOSE:

1.	To backup VFX presets, Multi setups, and edited programs to
	computer storage media.

2.	To allow edited programs and special Multi setups to be
	downloaded to the VFX during playback of a sequence.

UTILIZATION:

1.	Load the entire contents of the file CW--VFX.TXT into the
	existing CAKEWALK.SXT (see your manual for further details on
	this file) using the Text In function of a word processor or text
	editor.  If you use a word processor, save the modified file as a
	"DOS text file", "ASCII text file", or "non-document file".  Or,

2.	Use a text editor, word processor, or line editor to add the
	necessary lines to CAKEWALK.SXT manually.  The lines you need are
	the ones which begin with quote marks (") instead of double semi-
	colons (;;).  Be sure to type the lines EXACTLY as listed.  I
	suggest that regardless of which method you use, that you place
	the text before or after the entry for the Ensoniq ESQ-1.

PLEASE READ THE COMMENTS IN THE .TXT FILE FOR IMPORTANT INFORMATION!!!

RECEIVING A DUMP:

1.	Select the dump you  wish to request.  You will get the message
	"Waiting for Data"

2.	Press the STORAGE button on the front panel of the VFX.  Choose
	MIDI SYS-EX.

3.	Select the type of dump you want - Programs, Presets, or 
	Multi-A+B.  If you choose Programs or Presets you will proceed to
	another sub-screen which will ask you which data you wish to
	send.

4.	You will see the message "Transfering Data - Please Wait", and
	the byte counter in Cakewalk will increase.  When the counter
	reaches the byte count specified in the comments it will stop,
	and the VFX screen will return to the PROGRAMS screen.

5.	Press any key on your computer keyboard to record the information
	you have transmitted, and then name the slot you have placed it in.

Don't forget to save your Workfile!


SENDING A DUMP:

Sending a dump to the VFX requires you to simply choose the slot you wish
to send to the VFX.  If you send a program to the VFX it will ask you if
you want to write it to memory.  If you send a Preset it will ask you
which area you wish the preset to be stored in.  If you send the Multi it
will replace the current Multi A+B setup.

PRACTICAL USES:

If you use the VFX as a multi-timbral synth with Cakewalk, you can store
your special Multi-A+B settings in the sequence workfile, and have them
automatically download at the beginning of the sequence.

If you have created a special program for a sequence, you can store it in
Cakewalk to be downloaded during playback.

 
SPECIAL NOTES ON VFX BULK DUMPS:

I STRONGLY recommend that you backup the Internal RAM Programs to computer
disk in case you must re-initialize your VFX.  The dump size of this
feature is too large for Cakewalk to handle; therefore you must use a bulk
dump utility such as MIDIEX or QSEND to save it.  This should not be a
problem; it is unlikely that you would need to send the entire RAM
contents to the synth inside a Cakewalk sequence.

SPECIAL NOTES ON USING CAKEWALK WITH THE VFX:

The VFX fully implements Polyphonic Aftertouch and Channel Aftertouch. 
You must explicitly enable the recognition of these features inside
Cakewalk with the <SETTINGS><RECORD FILTER> command.

The VFX does not handle the way Cakewalk sends Note Offs (note with
velocity of 0) properly.  In order to use Cakewalk and the VFX together
you must start Cakewalk with the -O option (the letter O, not 0), i.e. at
the DOS prompt:

	C>CAKEWALK -O

This switch will not adversely affect other synths you may have.

If you have questions or comments I can be reached via the Washington MIDI
Users Group BBS (703-532-7860 - Washington, DC) or the Sound Management
Music BBS (312-949-MIDI - Chicago)

Russ Parker

Happy Sequencing!