Installation Guide for Version 7 of
                                Icon on UNIX Systems*


                                  Ralph E. Griswold




                                      TR 88-6a

























                           Last revised February 22, 1988


                           Department of Computer Science

                              The University of Arizona

                                Tucson, Arizona 85721




          *This work was supported by the National Science Foundation under
          Grant DCR-8502015.













                         Installation Guide for Version 7 of
                                Icon on UNIX Systems




          _1_.___I_n_t_r_o_d_u_c_t_i_o_n

             Version 7 of Icon [1] contains a number of new features and
          improvements to the implementation. Most changes to the language
          are upward compatible with Versions 5 and 6 and users should be
          able to run existing programs under Version 7 with no difficulty.

             This report provides the information necessary to install Ver-
          sion 7 of Icon on computers running UNIX. For other operating
          systems, see [2]. _N_o_t_e: If you previously installed Version 6 of
          Icon, you will find a number of minor changes in the installation
          procedure for Version 7. Be careful, particularly with respect to
          paths as described in this report.

             The implementation of Version 7 of Icon is designed so that it
          can be installed, largely automatically, on a variety of comput-
          ers running different versions of UNIX. This is accomplished by
          providing configuration information that tailors the installation
          to specific computers and versions of UNIX. As of the date given
          on the cover of this report, the following configurations were
          included in the distribution:



























                                       - 1 -








                  _c_o_m_p_u_t_e_r            _U_N_I_X _s_y_s_t_e_m         _n_a_m_e
                  Amdahl 580          UTS                 amdahl_uts
                  AT&T 3B2/5/15       System V            att3b5
                  AT&T 3B20           System V            att3b20
                  Celerity            Berkeley 4.2bsd     celerity_bsd
                  Codata 3400         Unisis              codata
                  DIAB                D-NIX               diab_dnix
                  Gould Powernode     UTX                 gould_pn
                  HP 9000             HP-UX               hp9000
                  IBM XT/AT*          XENIX 286 (LMM)     pc_xenix
                  IBM RT PC           ACIS                rtpc_acis
                  IBM RT PC           AIX                 rtpc_aix
                  Masscomp 5500       System V            masscomp
                  Microport V/AT      System V            microport
                  Motorola 8000/400   System V            mot_8000
                  Plexus P60          System V            plexus
                  Pyramid 90x         Berkeley 4.2bsd     pyramid_bsd
                  Ridge 32            ROS                 ridge
                  Sun-2 Workstation*  UNIX 4.2            sun2
                  Sun-3 Workstation*  UNIX 4.2            sun3
                  Unisys 7000/40      Berkeley 4.3bsd     tahoe_bsd
                  UNIX-PC/3B1*        System III          unixpc
                  VAX-11              Berkeley 4.1bsd     vax_4.1bsd
                  VAX-11*             Berkeley 4.2bsd and 4.3bsdvax_bsd
                  VAX-11              System V            vax_sysv
                  VAX-11              Ultrix              vax_ultrix
                  VAX-11              9th Edition         vax_v9

          These systems are referred to as ``supported'' in this report.
          They worked under Version 6 of Icon, but not all of them have
          been tested yet under Version 7.  The systems marked with an
          asterisk have been tested under Version 7 and are referred to as
          ``tested'' in this report.

             If your system is a tested one, the installation of Version 7
          of Icon should be as simple as issuing a few make commands.  If
          your system is supported but untested, it may install without
          modification, but if problems show up, you may have to make minor
          modifications in configuration files.  If your system is not in
          this list, it may have been added since this report was written.
          See Section 2.1 for information on how to get a current list of
          configurations and their statuses. In some cases, there may be
          partial configuration information. If the configuration informa-
          tion for your system is partial or lacking altogether, you still
          be able to install Version 7 of Icon by providing the information
          yourself, using other configurations are a guide. See Section 3.


          _2_.___T_h_e__I_n_s_t_a_l_l_a_t_i_o_n__P_r_o_c_e_s_s

             There are only a few steps needed to install Icon proper. In
          addition to Icon itself, there are a number of optional com-
          ponents that can be installed: a program library [3], a personal-
          ized interpreter system [4], and a variant translator system [5].



                                       - 2 -








          You may want to review the reports describing these optional com-
          ponents before beginning the installation. In any event, the
          installation of optional components can be done separately after
          Icon itself is installed.

             There are Makefile entries for most steps. Those steps are
          marked by asterisks. Steps that are optional are enclosed in
          brackets.

          _I_c_o_n__P_r_o_p_e_r

               1.    Decide where you want the Icon hierarchy to reside.

               2.    Unload the Icon hierarchy at the selected place.

               [3.*] Check the status of the configuration for your system.

               4.    If you unloaded Icon at a ``nonstandard'' place, edit
                     a configuration file that contains path specifica-
                     tions.

               5.*   Configure the source code for your system.

               6.*   Check the size of a header file; if it is not large
                     enough, adjust a configuration parameter and re-do
                     Step 5.

               7.*   Compile Icon.

               8.*   Install the compiled files.

               9.*   Run some simple tests to be sure Icon is working.

               [10.*]Run a test suite.

          _T_h_e__I_c_o_n__P_r_o_g_r_a_m__L_i_b_r_a_r_y

               [1.*] Compile the Icon program library

               [2.*] Test the Icon program library

               [3.]  Copy the Icon program library to a public place.

          _T_h_e__I_c_o_n__P_e_r_s_o_n_a_l_i_z_e_d__I_n_t_e_r_p_r_e_t_e_r

               [1.*] Build the Icon personalized interpreter system.

               [2.*] Test the Icon personalized interpreter system.

               [3.]  Copy the personalized interpreter system to a public
                     place.






                                       - 3 -








          _T_h_e__I_c_o_n__V_a_r_i_a_n_t__T_r_a_n_s_l_a_t_o_r__S_y_s_t_e_m

               [1.*] Test the Icon variant translator system.

               [2.]  Copy the variant translator system to a public place.

          _F_i_n_i_s_h_i_n_g__U_p

               [1.]  Install UNIX manual pages for the various components
                     of Icon.

               [2.*] Remove files that are no longer needed.

          _2_._1___I_n_s_t_a_l_l_i_n_g__I_c_o_n__P_r_o_p_e_r

          _S_t_e_p__1_:__D_e_c_i_d_i_n_g__W_h_e_r_e__t_o__P_u_t__I_c_o_n

             The standard location for all files, including executable
          binaries, is in the directory /usr/icon/v7|-.  You can chose other
          locations, but if you do, you must edit a file before proceeding.
          Think twice about this: Executable binary files for Icon are
          referenced by full path names, and they cannot be easily moved;
          it is important to select the correct paths at the start.  _N_o_t_e:
          In the balance of this report, relative paths and the location of
          files are given with respect to the location into which the Icon
          hierarchy is unloaded. For example, a reference to make is with
          respect to the Makefile at the top level of this hierarchy
          (/usr/icon/v7/Makefile for the standard location).  Similarly,
          config/unix corresponds to /usr/icon/v7/config/unix for the stan-
          dard location.

          _S_t_e_p__2_:__U_n_l_o_a_d_i_n_g__t_h_e__F_i_l_e_s

             The distribution consists of a hierarchy, which is rooted in
          ``.''.  Icon is distributed in a variety of formats.  The usual
          distribution media is magnetic tape, although it is also avail-
          able on Sun cartridges and on 5-1/4'' diskettes in two formats.

          Tapes: The Icon system is provided on tape in _t_a_r or _c_p_i_o format,
          recorded at 1600 or 6250 bpi.  The format and recording density
          are marked on the label on the tape.

             To unload the tape, cd to the directory that is to hold the
          Icon hierarchy (the standard location is /usr/icon/v7) and mount
          the tape.  The precise _t_a_r or _c_p_i_o command to unload the distri-
          bution tape depends on your local environment.  On a VAX running
          4._nbsd, use the following command for a 1600 bpi _t_a_r distribution
          tape:

                  tar x

          __________________________
          |-For HP-UX, the standard location is /users/icon/v7.




                                       - 4 -








          Similarly, on a VAX running System V with a 6250 bpi _c_p_i_o tape,
          use:

                  cpio -icdB </dev/rmt/0h

          The c (compatibility) and B (blocked) options are essential.

          Cartridges: Data cartridges are functionally equivalent to mag-
          netic tapes, but they are not blocked. For example, on a Sun
          Workstation with a _c_p_i_o cartridge, cd to the directory that is to
          hold the Icon hierarchy and use

                  cpio -icd </dev/rst0


          Diskettes: UNIX Icon is available on diskettes in two formats:
          XENIX _t_a_r and _c_p_i_o on MS-DOS diskettes.

             For XENIX _t_a_r, place the first diskette in drive _n and do

                  tar x_n

          Repeat this process with the remaining diskettes

             For _c_p_i_o on MS-DOS diskettes, copy the *.cpi files on the
          diskettes to the directory that is to hold the Icon hierarchy and
          use a script such as the following:

                  for i in *.cpi
                  do
                     cpio -icd <$i.cpi
                  done


          _S_t_e_p__3_:__C_h_e_c_k_i_n_g__t_h_e__S_t_a_t_u_s__o_f__t_h_e__C_o_n_f_i_g_u_r_a_t_i_o_n__f_o_r__Y_o_u_r__S_y_s_t_e_m

             You may wish to check the status of the configuration for your
          system.  This can be done by

                  make Status name=_n_a_m_e

          where _n_a_m_e is one of those given in the table in Section 1.  For
          example,

                  make Status name=hp9000

          lists the status of the configuration for the HP 9000 operating
          under HP-UX.

             In many cases, the status information was provided by the per-
          son who first installed Icon on the system in question. The
          information may be old and possibly inaccurate; use it as a
          guideline only.




                                       - 5 -








             There are some supported systems for which not all features of
          Version 7 are implemented. If the status information shows this
          for your system, proceed with the installation, but you may wish
          to implement the missing features later. For this, see Section 3
          after completing the basic installation.

          _S_t_e_p__4_:__E_d_i_t_i_n_g__P_a_t_h_s

             If you unloaded Version 7 of Icon at the standard place, skip
          this section.  Otherwise, you need to edit path specifications in
          your configuration directory.  The directory config/unix contains
          a subdirectory for each supported system. For example,
          config/unix/sun3 contains the configuration information for the
          Sun-3 Workstation. To get to the configuration information for
          your system,

                  cd config/unix/_n_a_m_e

          where _n_a_m_e is the name of your system.

             The file paths.h, as distributed, is the same for all systems
          and contains

                  #define RootPath  "/usr/icon/v7"
                  #define IcontPath "/usr/icon/v7/bin/icont"
                  #define TranPath  "/usr/icon/v7/bin/itran"
                  #define LinkPath  "/usr/icon/v7/bin/ilink"
                  #define IconxPath "/usr/icon/v7/bin/iconx"
                  #define HeaderPath"/usr/icon/v7/bin/iconx.hdr"

          RootPath gives the location of the Icon hierarchy; it must be the
          path of the root directory where the distributed files are
          located.

             The five binary files referenced are:

                  icont     Icon command processor - all the typical user knows about
                  itran     Icon translator
                  ilink     Icon linker
                  iconx     Icon run-time system
                  iconx.hdr bootstrap program that gets Icon programs into execution

          The command processor icont calls the other programs.

             There are two reasons for changing these paths:

               1.  If the Icon hierarchy is unloaded in an area other than
                   /usr/icon/v7, you probably want the binary files
                   installed in that area instead of /usr/icon/v7.

               2.  You may want to install some or all of the binary files
                   in a public area.

          For example, if you want to unload Icon in /usr/irving/v7 and



                                       - 6 -








          have the binaries in /usr/local/icon, edit paths.h to be

                  #define RootPath  "/usr/irving/v7"
                  #define IcontPath "/usr/local/icon/icont"
                  #define TranPath  "/usr/local/icon/itran"
                  #define LinkPath  "/usr/local/icon/ilink"
                  #define IconxPath "/usr/local/icon/iconx"
                  #define HeaderPath"/usr/local/icon/iconx.hdr"

          _C_a_u_t_i_o_n: If you are using a previous version of Icon, do not put
          iconx where it is - iconx for Version 7 is incompatible with
          iconx for previous versions and replacing a previous iconx by
          Version 7 iconx will invalidate all previously compiled Icon pro-
          grams.

          _S_t_e_p__5_:__C_o_n_f_i_g_u_r_i_n_g__I_c_o_n__f_o_r__Y_o_u_r__S_y_s_t_e_m

             To configure Icon for your system, do

                  make Configure name=_n_a_m_e

          where _n_a_m_e is the name of your system as described above.  For
          example,

                  make Configure name=vax_bsd

          configures Version 7 of Icon for a VAX running Berkeley 4._nbsd.

          _S_t_e_p__6_:__C_h_e_c_k_i_n_g__t_h_e__S_i_z_e__o_f__a__H_e_a_d_e_r__F_i_l_e

             Translating and linking an Icon program produces an _i_c_o_d_e
          file, which can then be run. In order to make icode files execut-
          able, a bootstrap header, iconx.hdr, is provided. The size of
          iconx.hdr varies from system to system and is determined by the
          defined constant MaxHdr, which is given in a configuration file.
          If value of MaxHdr is not large enough, icode files fail to exe-
          cute. To be sure that MaxHdr is large enough for your system, do

                  make Header

          This compiles the header file and lists its size, followed by the
          value of MaxHdr. For example, on a VAX BSD system, typical output
          from this make is

                  cc -O -c ixhdr.c
                  cc -O -N ixhdr.o -o iconx.hdr
                  strip iconx.hdr
                  -rwxrwxr-x  1 icon         1492 Jan 13 08:32 iconx.hdr
                  #define MaxHdr  1500

          The last two lines are what are important. In this example,
          MaxHdr is 1500 and the size of the header file is 1492 - that is,
          MaxHdr is large enough.




                                       - 7 -








             If you find MaxHdr is not large enough for your system (or if
          it is excessively large), edit config/unix/_n_a_m_e/define.h and
          change the value of MaxHdr there to an appropriate value (where
          _n_a_m_e is the name of your system as given above). It's advisable
          to leave a little spare room; some systems even require the value
          of MaxHdr to be rounded up. Don't worry about that at this point,
          but if icode files fail to execute, come back to this step and
          increase MaxHdr.

             If you change MaxHdr, you must go back and re-do Step 5.

          _S_t_e_p__7_:__C_o_m_p_i_l_i_n_g__I_c_o_n

             Next, compile Icon by

                  make Icon

          This takes a while. There may be warning messages on some sys-
          tems, but there should be no fatal errors.

          _S_t_e_p__8_:__I_n_s_t_a_l_l_i_n_g__I_c_o_n

             To install Icon, do

                  make Install


          _S_t_e_p__9_:__D_o_i_n_g__S_o_m_e__S_i_m_p_l_e__T_e_s_t_s

             For supported systems that compile and install without
          apparent difficulty, a few simple tests usually are sufficient to
          confirm that Icon is running properly. The following does the
          job:

                  make Samples

          This test compares local program output with the expected output.
          There should be no differences.  If there are none, you presum-
          ably have a running Version 7 Icon.

          _S_t_e_p__1_0_:__E_x_t_e_n_s_i_v_e__T_e_s_t_i_n_g

             If you want to runs more extensive tests, do

                  make Test-all

          This takes quite a while and does a lot of work. Some differences
          are to be expected, since tests include date, time, and local
          host information. There also sometimes are insignificant differ-
          ences in the format of floating-point numbers, the order of ran-
          dom numbers, and the results of sorting (relating to stability).
          See the main Makefile for more information if you want to run
          these tests.




                                       - 8 -








          _2_._2___I_c_o_n__P_r_o_g_r_a_m__L_i_b_r_a_r_y

             The Icon program library contains a variety of programs and
          procedures.  This library not only is useful it its own right,
          but it provides numerous examples of programming techniques which
          may be useful to novice Icon programmers. While this library is
          not necessary for the running of Icon programs, most sites
          install it.

             _N_o_t_e: The present Icon program library is still Version 6.  It
          runs properly under Version 7, however.

          _S_t_e_p__1_:__B_u_i_l_d_i_n_g__t_h_e__I_c_o_n__P_r_o_g_r_a_m__L_i_b_r_a_r_y

             To build the Icon program library, do

                  make Ipl

          This puts compiled programs in ipl/progs and translated pro-
          cedures in ipl/procs.

          _S_t_e_p__2_:__T_e_s_t_i_n_g__t_h_e__I_c_o_n__P_r_o_g_r_a_m__L_i_b_r_a_r_y

             To test the library, do

                  make Test-ipl

          No differences should show.

          _S_t_e_p__3_:__I_n_s_t_a_l_l_i_n_g__t_h_e__I_c_o_n__P_r_o_g_r_a_m__L_i_b_r_a_r_y

             You can copy the executable programs in ipl/progs and the
          translated procedures in ipl/procs to public locations to make
          them more accessible, although they can be used from any location
          that is readable by the user.

          _2_._3___P_e_r_s_o_n_a_l_i_z_e_d__I_n_t_e_r_p_r_e_t_e_r_s

             The personalized interpreter system allows an individual to
          build a private copy of Icon's run-time system, which then can be
          modified.

             Personalized interpreters are somewhat specialized and the
          typical Icon programmer has no need for them. However, if your
          site has a need for tailored versions of Icon, this system may be
          useful.

          _S_t_e_p__1_:__B_u_i_l_d_i_n_g__t_h_e__P_e_r_s_o_n_a_l_i_z_e_d__I_n_t_e_r_p_r_e_t_e_r__S_y_s_t_e_m

             To build the personalized interpreter system, do

                  make PI





                                       - 9 -








          _S_t_e_p__2_:__T_e_s_t_i_n_g__t_h_e__P_e_r_s_o_n_a_l_i_z_e_d__I_n_t_e_r_p_r_e_t_e_r__S_y_s_t_e_m

             For testing, do

                  make Test-pi

          There may be some warning messages during compilation, but there
          should be no fatal errors.

          _S_t_e_p__3_:__I_n_s_t_a_l_l_i_n_g__t_h_e__P_e_r_s_o_n_a_l_i_z_e_d__I_n_t_e_r_p_r_e_t_e_r__S_y_s_t_e_m

             Personalized interpreter directories are constructed by the
          shell script icon_pi. You therefore may wish to place it in a
          public location:

                  cp icon_pi _l_o_c_a_t_i_o_n


          _2_._4___V_a_r_i_a_n_t__T_r_a_n_s_l_a_t_o_r_s

             The variant translator system facilitates the construction of
          preprocessors for variants of the Icon programming language.
          This facility is even more specialized than the personalized
          interpreter system, but some forthcoming tools related to measur-
          ing the performance and behavior of Icon programs use the variant
          translator system.

             The variant translator system requires a version of _y_a_c_c(_1)
          with large regions. You may have to tailor your version of
          _y_a_c_c(_1) for this. See [5]. On systems with a limited amount of
          memory, this may not work at all. If there is a problem, it will
          show up during testing.

             There is no separate step for building the variant translator
          system.  However, Icon must be installed before testing the vari-
          ant translator system.

          _S_t_e_p__1_:__T_e_s_t_i_n_g__t_h_e__V_a_r_i_a_n_t__T_r_a_n_s_l_a_t_o_r__S_y_s_t_e_m

             For testing, do

                  make Test-vt

          There may be warning messages during compilation, but there
          should be no fatal errors.

          _S_t_e_p__3_:__I_n_s_t_a_l_l_i_n_g__t_h_e__V_a_r_i_a_n_t__T_r_a_n_s_l_a_t_o_r__S_y_s_t_e_m

             To put icon_vt, the shell script that builds variant transla-
          tor directories into a public place, do

                  cp icon_vt _l_o_c_a_t_i_o_n





                                       - 10 -








          _2_._5___F_i_n_i_s_h_i_n_g__U_p

          _S_t_e_p__1_:__I_n_s_t_a_l_l_i_n_g__M_a_n_u_a_l__P_a_g_e_s

             After Icon and any optional components have be installed, you
          may wish to install the appropriate manual pages in the standard
          location on your system. The manual pages are in the docs direc-
          tory:

                  icont.1   manual page for Icon proper
                  icon_pi.1 manual page for the Icon personalized interpreter system
                  icon_vt.1 manual page for the Icon variant translator system


          _S_t_e_p__2_:__C_l_e_a_n_i_n_g__U_p

             You can remove object files and test results by

                  make Clean

          You also can remove source files, but think twice about this,
          since source files may be useful to persons using personalized
          interpreters and variant translators.  In addition, you can
          remove files related to optional components of the Icon system
          that you do not need, and if you are tight on space you may wish
          to remove documents and the directory containing the programs
          from the Icon language book. See Appendix A, which shows the Icon
          hierarchy.


          _3_.___C_o_n_f_i_g_u_r_i_n_g__V_e_r_s_i_o_n__7__f_o_r__a__N_e_w__S_y_s_t_e_m

             Version 7 of Icon assumes that C _i_n_ts are 16, 32, or 64 bits
          long.  (Icon has not yet been installed on a computer with 64-bit
          _i_n_ts.) If your system violates this assumption, don't try to go
          on - but check back with us, since we are may be able to provide
          some advice on how to proceed.

             There are eleven steps in installing Icon for a new system:

               1.*   Build a configuration directory.

               2.    Edit a configuration file to provide appropriate
                     definitions for your system.

               3.    Edit Makefile headers.

               4.*   Perform the installation as described in Section 2.

               5.*   Perform extensive tests.

               6.    Make any necessary corrections, repeating previous
                     steps as necessary.




                                       - 11 -








               [7.]  Implement and test co-expressions.

               [8.]  Implement and test arithmetic overflow checking.

               [9.]  Implement the personalized interpreter system.

               10.   Provide status information in your configuration
                     directory.

               11.   Send the contents of your configuration directory to
                     the Icon Project so that your configuration can be
                     added to the system there for future availability.

          _S_t_e_p__1_:__B_u_i_l_d_i_n_g__a__N_e_w__C_o_n_f_i_g_u_r_a_t_i_o_n__D_i_r_e_c_t_o_r_y

             First you need to select a name for your system.  The name
          should consist of a mnemonic for the computer, which may be fol-
          lowed by an underscore and a mnemonic for the operating system,
          in case there may be more than one operating system for the com-
          puter.  Examples are vax_bsd and vax_sysv.

             To build and initialize a new configuration directory,

                  make System name=_n_a_m_e

          where _n_a_m_e is the name of your system.

             As a result, the subdirectory _n_a_m_e will contain the following
          files:

                  define.h    main configuration file
                  paths.h     paths
                  icont.hdr   flags for command processor Makefile
                  iconx.hdr   flags and other definitions for the run-time system Makefile
                  ilink.hdr   flags for the linker Makefile
                  itran.hdr   flags for the translator Makefile
                  pi.hdr      flags for the personalized interpreter Makefile
                  vt.hdr      flags for the variant translator Makefile
                  rlocal.c    placeholder for possible assembly-language routines
                  rover.c     arithmetic overflow checks
                  rswitch.c   co-expression context switch
                  Ranlib      library randomizer for personalized interpreters

          To work on these files,

                  cd unix/config/_n_a_m_e


          _S_t_e_p__2_:__E_d_i_t_i_n_g__t_h_e__M_a_i_n__C_o_n_f_i_g_u_r_a_t_i_o_n__F_i_l_e_,_define.h

             There are many constants in the source code for Icon that vary
          from system to system. Default values are provided so that the
          usual cases are handled automatically.  The file define.h con-
          tains C preprocessor definitions for parameters that differ from



                                       - 12 -








          the defaults or that must be provided on an individual basis. The
          initial contents of this file as produced in Step 1 above are for
          a ``vanilla'' system with the commonest values for parameters. If
          your system closely approximates a ``vanilla'' system, you will
          have few changes to make to define.h. Over the range of possible
          systems, there are many possibilities as described below.

             The definitions are grouped into categories so that any neces-
          sary changes to define.h can be approached in a logical way.

          C preprocessor: Icon preprocessor directives use string concate-
          nation and substitution of arguments within quotation marks. By
          default, the ``standard'' method of accomplishing this in UNIX
          preprocessors is used.  A different method is specified in the C
          draft standard [6]. If your C compiler supports the draft stan-
          dard, add

                  #define Standard

          to define.h.

          C sizing and alignment: There are four constants that relate to
          the size of C data and alignment:

                  IntBits     (default: 32)
                  WordBits    (default: 32)
                  Double      (default: undefined)

          IntBits is the number of bits in a C _i_n_t. It may be 16, 32, or
          64. WordBits is the number of bits in a C _l_o_n_g (Icon's ``word'').
          It may be 32 or 64.  If your C library expects _d_o_u_b_l_es to be
          aligned at double-word boundaries, add

                  #define Double

          to define.h.

          Floating-point arithmetic: There are four optional definitions
          related to floating-point arithmetic:

                  Big         (default: 9007199254740092.)
                  LogHuge     (default: 309)
                  Precision   (default: 10)
                  ZeroDivide  (default: undefined)

          The values of Big, LogHuge, and Precision give, respectively, the
          largest floating-point number that does not loose precision, the
          maximum base-10 exponent + 1 of a floating-point number, and the
          number of digits provided in the string representation of a
          floating-point number. If the default values given above do not
          suit the floating-point arithmetic on your system, add appropri-
          ate definitions to define.h. If your system needs a software
          check for division by floating-point zero, add




                                       - 13 -








                  #define ZeroDivide

          to  define.h.

          Include file location: The location of the include file time.h
          varies from system to system. Its default location is <time.h>.
          If it resides at a different location on your system (usually
          <sys/time.h>), add an appropriate definition of SysTime to
          define.h, as in

                  #define SysTime <sys/time.h>

          If the location is incorrect, a fatal error will occur during the
          compilation of src/iconx/lmisc.c.  The use of this definition
          also depends on your C preprocessor making macro substitutions in
          #include directives. Most preprocessors do, but if yours does
          not, edit src/iconx/lmisc.c and replace SysTime there by the
          appropriate value. If you have to do this, make a note to come
          back later and place the definition under the control of condi-
          tional compilation as described in Step 4.

          Run-time routines: The support for some run-time routines varies
          from system to system.  The related constants are:

                  Fork        (default: fork)
                  IconGcvt    (default: undefined)
                  IconQsort   (default: undefined)
                  NoAtof      (default: undefined)
                  SysMem      (default: undefined)
                  index       (default: undefined)
                  rindex      (default: undefined)

          If your system supports _v_f_o_r_k(_2), add

                  #define Fork vfork

          to define.h.

          If IconGcvt and IconQsort are defined, versions of _g_c_v_t(_3) and
          _q_s_o_r_t(_3) in the Icon system are used in place of the routines
          normally provided in the C run-time system. These constants only
          need to be defined if the versions of these routines in your
          run-time system are defective or missing.

          The C run-time routine _a_t_o_f(_3) normally is used in the Icon
          linker to convert strings for real literals to corresponding
          floating-point numbers.  If the version of _a_t_o_f on your system
          does not work properly, add

                  #define NoAtof

          to define.h.  This replaces the use of _a_t_o_f by in-line conversion
          code.




                                       - 14 -








          If your run-time system includes _m_e_m_c_p_y(_3) and _m_e_m_s_e_t(_3), add

                  #define SysMem

          to define.h.  Otherwise, versions of these routines in the Icon
          system are used.

          Different versions of UNIX use different names for the routines
          for locating substrings within strings. The source code for Icon
          uses index and rindex. The other possibilities are strchr and
          strrchr. If your system uses the latter names, add

                  #define index strchr
                  #define rindex strrchr

          to define.h.

          Host identification: The identification of the host computer as
          given by the Icon keyword &host needs to be specified in
          define.h.  The definition

                  #define HostStr "unknown host"

          is provided in define.h initially.  This definition should be
          changed to an appropriate value for your system.

          Alternatively, some systems provide direct mechanisms for speci-
          fying the host in a standard way. In this case, remove the defin-
          ition of HostStr and provide an alternative as follows:

          On some versions of UNIX, notably Version 7 and 4.1bsd, the file
          /usr/include/whoami.h contains the host name. If your system has
          this file and you want to use this name, add

                  #define WhoHost

          to define.h.

          Some versions of UNIX, notably 4.2bsd and 4.3bsd, provide the
          host name via the _g_e_t_h_o_s_t_n_a_m_e(_2) system call. If your system sup-
          ports this system call and you want to use this name,

                  #define GetHost

          to define.h.

          Some versions of UNIX, such as System V, provide the host name
          via the _u_n_a_m_e(_2) system call. If your system supports this call
          and you want to use this name,

                  #define UtsName

          to define.h.




                                       - 15 -








          _N_o_t_e: Only one of these methods of specifying the host name can
          be used.

          Storage management: Icon includes its own versions of _m_a_l_l_o_c(_3),
          _c_a_l_l_o_c(_3), _r_e_a_l_l_o_c(_3), and _f_r_e_e(_3) so that it can manage its
          storage region without interference from allocation by the
          operating system. Normally, Icon's versions of these routines are
          loaded instead of the system library routines.

          Leave things are they are in the initial configuration, but if
          your system insists on loading its own library routines, multiple
          definitions will occur as a result of the _l_d in src/iconx.  If
          multiple definitions occur, go back and add

                  #define IconAlloc

          to define.h. This definition causes Icon's routines to be named
          differently to avoid collision with the system routine names.

          One possible effect of this definition is to interfere with
          Icon's expansion of its memory region in case the initial values
          for allocated storage are not large enough to accommodate a pro-
          gram that produces a lot of data.  This problem appears in the
          form of run-time errors 305-307. Users can get around this prob-
          lem on a case-by-case basis by increasing the initial values for
          allocated storage by setting environment variables [7].

          Icon's dynamic storage allocation system uses three contiguous
          memory regions that it expands if necessary. This method relies
          on the use of _b_r_k(_2) and _s_b_r_k(_2) and the system treatment of user
          memory space as one logically contiguous region. This may not
          work on some systems that treat memory as segmented or do not
          support _b_r_k and _s_b_r_k. On such systems, it may be necessary to add

                  #define FixedRegions

          to define.h.  The effect of this definition is to assign fixed-
          sized regions for Icon's use. They may not be shared or expanded
          and all of available memory may not be used. This option should
          be used only if necessary.

          The header file: As described In Section 2.1, Step 6, a bootstrap
          header file is used to make icode files executable.  On some sys-
          tems, particularly UNIX emulators, many routines may be included
          in the header file by the loader, even if they are not needed.

          Start by assuming this is not a problem, but if iconx.hdr is
          impractically large, you can eliminate the header file by adding

                  #define NoHeader

          to define.h.  _N_o_t_e: If NoHeader is defined, the value of MaxHdr
          is irrelevant.




                                       - 16 -








          The effect of this definition is to render Icon programs non-
          executable. Instead, they must be run by using the -x option
          after the program name when icont is used, as in

                  icont prog.icn -x

          Such a program also can be run as an argument of iconx, as in

                  iconx prog

          where prog is the result of translating and linking prog.icn as
          in the previous example.

          Miscellaneous: There are two other definitions that may be needed
          in some cases:

                  Hz          (default: 60)
                  UpStack     (default: undefined)

          If you are running in a 50-hz environment, add

                  #define Hz 50

          to define.h.

          Most computers have downward-growing C stacks, for which stack
          addresses decrease as values are pushed. If you have an upward-
          growing stack, for which stack addresses increase as values are
          pushed, add

                  #define UpStack

          to define.h.

          Executable Images: If you have a 4._nbsd UNIX system and want to
          enable the function save(s), which allows an executable image of
          a running Icon program to be saved [1], add

                  #define ExecImages

          to define.h.

          Optional features: The implementation of co-expressions and
          arithmetic overflow checking require assembly language routines.
          Initially, define.h contains

                  #define NoCoexpr
                  #define NoOver

          These definitions disable co-expressions and arithmetic overflow
          checks.  Leave these definitions in for the first round, although
          you may want to remove them later and implement these features
          (see Steps 7 and 8).




                                       - 17 -








          _S_t_e_p__3_:_Makefile Headers

             The files icont.hdr, iconx.hdr, ilink.hdr, and itran.hdr pro-
          vide headers for Makefiles in the source directories src/icont,
          src/iconx, and so on. These headers are prepended to the standard
          bodies for the Makefiles during configuration.

             Except for iconx.hdr, these headers serve only to specify
          flags for _c_c(_1) and _l_d(_1) via CFLAGS and LDFLAGS.  If your C
          optimizer is robust, you may wish to start with

                  CFLAGS= -O

          in all these headers.  If you encounter problems during testing,
          suspect your optimizer first and try compiling Icon without the
          -O flag.

             Other _c_c and _l_d flags vary considerably from system to system.
          You may want to review your local manual pages for these proces-
          sors and look at the header files in the other configuration
          areas.

             There are two other definitions in iconx.hdr, RSWITCH and
          ROVER, which depend on whether the local co-expression context
          switch and arithmetic overflow checks are written in C or assem-
          bly language. The initial values of these definitions are
          rswitch.c and rover.c, and dummy C routines are provided. To
          start out, leave these definitions as they are; the default rou-
          tines can be replaced later. See Steps 7 and 8.

             The file pi.hdr provides a header for the personalized inter-
          preter Makefile (which is named Pimakefile). In addition to the
          usual _c_c and _l_d flags, you should provide definitions for XCFLAGS
          and XLDFLAGS that are the same as those for CFLAGS and LDFLAGS in
          icont.hdr. This assures that the header file in the personalized
          interpreter is the same size as the one in the regular version of
          Icon.

             The file vt.hdr provides a header for the variant translator
          Makefile (which is named Vtmake2). It should have the same _c_c and
          _l_d flags as itran.hdr.

          _S_t_e_p__4_:__I_n_s_t_a_l_l_a_t_i_o_n

             Once you have edited the files as described in the previous
          steps, proceed with the installation as described in Steps 5
          through 9 at the beginning of Section 2.  You may need to iterate
          if problems show up.  If you make a change in a configuration
          file after a compilation, be sure to perform the configuration
          step again; some aspects of the configuration are far-reaching
          and not obvious.

             _N_o_t_e: The configuration system is designed to avoid modifica-
          tions to the distributed source code for Version 7.  However, you



                                       - 18 -








          may run into problems that require modifications to the source
          code itself.  If you need to modify the source code, do it under
          the control of conditional compilation keyed to the name of your
          system. Add

                  #define _N_A_M_E

          to define.h, where _N_A_M_E is an all-uppercase name that identifies
          your system.  For example, the define.h for Sun Workstations con-
          tains

                  #define SUN


          Then use

                  #ifdef _N_A_M_E
                       .
                       .
                       .
                  #endif /* _N_A_M_E */

          or similar constructions where you need local source-code modifi-
          cations.  For example, this technique can be used to handle the
          problem that may arise with SysTime, described in Step 2. Note
          that nested #ifdefs may be needed in places where there are
          several different local modifications.

             It is important to be consistent and careful about the use of
          such conditional compilations; if done properly, your modifica-
          tions can be backed into the central version of the source code
          at the Icon Project and will be in place for you when subsequent
          versions are released.  See Step 11.

             Occasionally, it is necessary to add code that cannot be writ-
          ten in C.  The file rlocal.s is provided for such contingencies.
          It initially is a placeholder that is copied from the configura-
          tion file to src/iconx and is compiled and linked when the run-
          time system is built. This placeholder can be replaced by any
          necessary assembly-language routines.

          _S_t_e_p__5_:__T_e_s_t_i_n_g

             More testing is recommended for a new installation than for
          one that has been successfully installed elsewhere. You should do
          Step 10 at the beginning of Section 2:

                  make Test-all

          See Makefile for more detailed information about the tests.







                                       - 19 -








          _S_t_e_p__7_:__C_o_-_E_x_p_r_e_s_s_i_o_n_s

             Once Icon is working properly, you may wish to implement co-
          expressions.  _N_o_t_e: If your system does not allow the C stack to
          be at an arbitrary place in memory, there is probably little hope
          of implementing co-expressions.  If you do not implement co-
          expressions, the only effect will be that Icon programs that
          attempt to use a co-expression will terminate with an error mes-
          sage.

             All aspects of co-expression creation and activation are writ-
          ten in C in Version 7 except for a routine, coswitch, that is
          needed for context switching. This routine requires assembly
          language, since it must manipulate hardware registers.  It either
          can be written as a C routine with asm directives or as an assem-
          bly language routine.

             When a new configuration directory is set up, a file rswitch.c
          is provided with a version of coswitch that results in error ter-
          mination if an Icon program attempts to activate a co-expression.
          If you implement coswitch in C, replace the version of this file
          in your configuration directory. Alternatively, if you implement
          coswitch in assembly language, place it in a file named
          rswitch.s.

             Calls to the context switch have the form
          coswitch(old_cs,new_cs,first), where old_cs is a pointer to an
          array of words that contain C state information for the current
          co-expression, new_cs is a pointer to an array of words that hold
          C state information for a co-expression to be activated, and
          first is 1 or 0, depending on whether or not the new co-
          expression has or has not been activated before.  The zeroth ele-
          ment of a C state array always contains the hardware stack
          pointer (_s_p) for that co-expression. The other elements can be
          used to save any C frame pointers and any other registers your C
          compiler expects to be preserved across calls.

             The default number of elements for saving the C state is 15.
          This number may be changed by adding

                  #define CStateSize _n

          to define.h, where _n is the number of elements needed.

             The first thing coswitch does is to save the current pointers
          and registers in the old_cs array. Then it tests first.  If first
          is zero, coswitch sets _s_p from new_cs[0], clears the C frame
          pointers, and _c_a_l_l_s interp. If first is not zero, it loads the
          (previously saved) _s_p, C frame pointers, and registers from
          new_cs and returns.

             Written in C, coswitch has the form:





                                       - 20 -








                  /*
                   * coswitch
                   */
                  coswitch(old_cs, new_cs, first)
                  int *old_cs, *new_cs;
                  int first;
                  {
                                      .
                                      .
                                      .
                              /* save sp, frame pointers, and other registers in old_cs */
                                      .
                                      .
                                      .
                     if (first == 0) {/* this is first activation */
                                      .
                                      .
                                      .
                              /* load sp from new_cs[0] and clear frame pointers */
                                      .
                                      .
                                      .
                        interp(0, 0);
                        syserr("interp() returned in coswitch");
                        }
                     else {
                                      .
                                      .
                                      .
                              /* load sp, frame pointers, and other registers from new_cs */
                                      .
                                      .
                                      .
                        }
                  }

          Appendix B contains coswitch for the VAX.  Other examples are
          contained in the configuration directories in config/unix.

             After you implement rswitch, remove the #define NoCoexpr from
          define.h and replace rswitch.c in your configuration directory by
          either a new rswitch.c or an assembly language file named
          rswitch.s. The configuration process will copy your file to the
          appropriate place prior to compilation. If you use rswitch.s,
          change the definition of RSWITCH in iconx.hdr to

                  RSWITCH=rswitch.s

          If your assembler requires special flags, add an appropriate
          definition for OFLAGS to iconx.hdr.

             To test your context switch,





                                       - 21 -








                  make Test-coexpr

          Ideally, there should be no differences in the comparison of out-
          puts.

             If you have trouble with your context switch, the first thing
          to do is double-check the registers that your C compiler expects
          to be preserved across calls - different C compilers on the same
          computer may have different requirements.

             Another possible source of problems is built-in stack check-
          ing.  Co-expressions rely on being able to specify an arbitrary
          region of memory for the C stack. If your C compiler generates
          code for stack probes that expects the C stack to be at a
          specific location, you may need to disable this code or replace
          it with something more appropriate.

          _S_t_e_p__8_:__O_v_e_r_f_l_o_w__C_h_e_c_k_i_n_g

             C does not provide overflow checking for integer addition,
          subtraction, or multiplication. Icon, on the other hand, is sup-
          posed to check for overflow. This usually requires assembly-
          language code.

             Initially, define.h contains the definition

                  #define NoOver

          which causes overflow checking to be bypassed.

             If you do not want to implement overflow checking, you need do
          nothing.  The only effect will be that overflow will not be
          detected.

             If you want to implement overflow checking, remove the defini-
          tion of NoOver from your define.h and write routines ckadd,
          cksub, and ckmul that call fatalerr(-203,0) in the case of over-
          flow. Appendix C contains the overflow checking routine for the
          VAX.  Other examples are contained in the configuration direc-
          tories in config/unix.

             _N_o_t_e: It often is harder to test for overflow for multiplica-
          tion than for addition and subtraction. A dummy routine that sim-
          ply returns can be provided for multiplication if this is the
          case on your system.

             If you supply overflow checking routines, put them in the file
          rover.s in your configuration directory and replace

                  ROVER=rswitch.c

          by





                                       - 22 -








                  ROVER=rswitch.s

          in iconx.hdr in your configuration directory. The configuration
          process then will copy this file to the appropriate place prior
          to compilation.

             To test overflow checking,

                  make Test-over

          There should be no differences in the comparison of outputs if
          overflow checking is working properly.

             You should also rerun previous tests at this point to make
          sure that arithmetic still works properly.

          _S_t_e_p__9_:__P_e_r_s_o_n_a_l_i_z_e_d__I_n_t_e_r_p_r_e_t_e_r_s

             The personalized interpreter system uses _a_r(_1). On most UNIX
          systems, it is necessary to use _r_a_n_l_i_b(_1) so that the loader can
          access the archive. The script Ranlib that is provided when a new
          configuration directory is initialized contains calls of _r_a_n_l_i_b
          for this purpose.

             Some UNIX systems, notably System V, handle this problem
          directly in _a_r(_1) and do not have _r_a_n_l_i_b(_1). If your system does
          not use _r_a_n_l_i_b(_1), change Ranlib to an empty script by

                  echo "" >Ranlib

          in your configuration directory.

             Test your personalized interpreter system as described in Sec-
          tion 2.3. If the test programs fail to execute, suspect the size
          of tests/pi/piconx.hdr, the personalized interpreter version of
          iconx.hdr. If it is larger than MaxHdr, something is wrong. Check
          the file pi.hdr in your configuration directory as described in
          Section 2.1.

          _S_t_e_p__1_0_:__S_t_a_t_u_s__I_n_f_o_r_m_a_t_i_o_n

             Each configuration directory contains a file named status that
          describes the state of the configuration. A placeholder is pro-
          vided when a new configuration directory is set up.  When your
          configuration is complete, edit status appropriately, using the
          status files in other configuration directories as models.

          _S_t_e_p__1_1_:__S_e_n_d_i_n_g__Y_o_u_r__C_o_n_f_i_g_u_r_a_t_i_o_n__I_n_f_o_r_m_a_t_i_o_n__t_o__t_h_e__I_c_o_n__P_r_o_j_e_c_t

             When your newly installed system is complete, send a copy of
          any files you modified (both in your configuration directory and
          in the source code, if changes there were necessary) to the Icon
          Project as given in Section 4.




                                       - 23 -








             In turn, your changes will be added to the central Icon system
          and will be available to others (as well as to you in future
          releases of Icon).

             Files can be sent on any convenient media, such as magnetic
          tape in _t_a_r or _c_p_i_o format. Electronic mail also can be used.


          _4_.___C_o_m_m_u_n_i_c_a_t_i_n_g__w_i_t_h__t_h_e__I_c_o_n__P_r_o_j_e_c_t

             If you run into problems with the installation of Version 7 of
          Icon, contact the Icon Project:

                  Icon Project
                  Gould-Simpson Building
                  Department of Computer Science
                  The University of Arizona
                  Tucson, AZ   85721
                  (602) 621-6613
                  icon-project@arizona.edu
                  {ihnp4,noao,mcnc,allegra}!arizona!icon-project


             Please also let us know if you have any suggestions for
          improvements to the installation process or corrections or
          refinements to configuration files for supported systems.

          _R_e_f_e_r_e_n_c_e_s

          1. Griswold, Ralph E., Gregg M. Townsend, and Kenneth Walker,
          _V_e_r_s_i_o_n _7 _o_f _I_c_o_n, Technical Report TR 88-5, Department of Com-
          puter Science, The University of Arizona. 1988.

          2. Griswold, Ralph E. _T_r_a_n_s_p_o_r_t_i_n_g _V_e_r_s_i_o_n _7 _o_f _I_c_o_n, Technical
          Report TR 88-9, Department of Computer Science, The University of
          Arizona. 1988.

          3. Griswold, Ralph E. _T_h_e _I_c_o_n _P_r_o_g_r_a_m _L_i_b_r_a_r_y; _V_e_r_s_i_o_n _6,
          _R_e_l_e_a_s_e _1, Technical Report TR 86-13, Department of Computer Sci-
          ence, The University of Arizona. 1986.

          4. Griswold, Ralph E. _P_e_r_s_o_n_a_l_i_z_e_d _I_n_t_e_r_p_r_e_t_e_r_s _f_o_r _V_e_r_s_i_o_n _7 _o_f
          _I_c_o_n, Technical Report TR 88-7, Department of Computer Science,
          The University of Arizona. 1988.

          5. Griswold, Ralph E. and Kenneth Walker.  _B_u_i_l_d_i_n_g _V_a_r_i_a_n_t
          _T_r_a_n_s_l_a_t_o_r_s _f_o_r _V_e_r_s_i_o_n _7 _o_f _I_c_o_n, Technical Report TR 88-8,
          Department of Computer Science, The University of Arizona. 1988.

          6. Technical Committee X3J11, _D_r_a_f_t _P_r_o_p_o_s_e_d _A_m_e_r_i_c_a_n _N_a_t_i_o_n_a_l
          _S_t_a_n_d_a_r_d _f_o_r _I_n_f_o_r_m_a_t_i_o_n _S_y_s_t_e_m_s - _P_r_o_g_r_a_m_m_i_n_g _L_a_n_g_u_a_g_e _C. 1986.

          7. Griswold, Ralph E. _I_C_O_N_T(_1), manual page for _U_N_I_X _P_r_o_g_r_a_m_m_e_r'_s
          _M_a_n_u_a_l, Department of Computer Science, The University of



                                       - 24 -








          Arizona. 1988.
























































                                       - 25 -








                       Appendix A - The Distribution Hierarchy





             The main directories in the Version 7 hierarchy are:

                  v7                  root of the Version 7 hierarchy
                            /bin      standard location for binary files
                            /book     programs from the Icon book
                            /config/unix        configuration files for UNIX systems
                            /docs     source text for documents
                            /ipl      Icon program library
                            /pi       personalized interpreter system
                            /samples  sample programs
                            /src      source code for the Icon system
                            /tests    test programs
                            /vt       variant translator system

          A complete directory tree is contained in docs/v7.dtree.




































                                       - 26 -








                 Appendix B - A Sample Co-Expression Context Switch





          rswitch.c for the VAX under Berkeley UNIX:


                  coswitch(old_cs, new_cs, first)
                  int *old_cs, *new_cs;
                  int first;


                  {
                     asm("  movl 4(ap),r0");
                     asm("  movl 8(ap),r1");
                     asm("  movl sp,0(r0)");
                     asm("  movl fp,4(r0)");
                     asm("  movl ap,8(r0)");
                     asm("  movl r11,16(r0)");
                     asm("  movl r10,20(r0)");
                     asm("  movl r9,24(r0)");
                     asm("  movl r8,28(r0)");
                     asm("  movl r7,32(r0)");
                     asm("  movl r6,36(r0)");


                     if (first == 0) {    /* this is first activation */
                        asm("  movl 0(r1),sp");
                        asm("  clrl fp");
                        asm("  clrl ap");
                        interp(0, 0);
                        syserr("interp() returned in coswitch");
                        }


                     else {
                        asm(" movl 0(r1),sp");
                        asm(" movl 4(r1),fp");
                        asm(" movl 8(r1),ap");
                        asm(" movl 16(r1),r11");
                        asm(" movl 20(r1),r10");
                        asm(" movl 24(r1),r9");
                        asm(" movl 28(r1),r8");
                        asm(" movl 32(r1),r7");
                        asm(" movl 36(r1),r6");
                        }
                  }








                                       - 27 -








             Appendix C - A Sample Arithmetic Overflow Checking Routine





          rover.s for the VAX under Berkeley UNIX:


                  _ckadd: .word   0
                          addl3   4(ap),8(ap),r0  # Perform addition
                          jvs     oflow           # Branch if overflow
                          ret                     # Return result in r0

                  _cksub: .word   0
                          subl3   8(ap),4(ap),r0  # Perform subtraction
                          jvs     oflow           # Branch if overflow
                          ret                     # Return result in r0

                  _ckmul: .word   0
                          mull3   4(ap),8(ap),r0  # Perform multiplication
                          jvs     oflow           # Branch if overflow
                          ret                     # Return result in r0

                  oflow:                          # Got overflow on an operation
                          pushl   $0
                          pushl   $-203
                          calls   $1,_fatalerr            # fatalerr(-203,0)





























                                       - 28 -