*******************************************
* MJGEM10X.DOC              Documentation *
* Mandelbrot/Julia Plotter     gemini-10X *
* Todd Redden                  Sept. 1993 *
******************************************* "Mandelbrot/Julia Plotter
gemini-10X" for Atari ST uses the gemini-10X printer as a graphic device for
plotting the Mandelbrot set and quadratic Julia fractals with several options.
Double clicking on MJGEM10X.TOS then prompts the user for keyboard input, and
channels required information based on previous entries.  Following is a
description of the program's parameters and capabilities:

*******************
* New or Continue *
******************* Enter new data to begin a fractal from scratch, or continue
an aborted fractal previously saved to disk.  If continuing, enter a descriptor
using up to eight text characters.  This is used to determine the filename of
the fractal and of the data file which holds its interim parameters.  The files
must be in the root directory of the diskette in drive A.  If creating a new
fractal, the program requests the following data:

****************************
* Mandelbrot or Julia plot *
**************************** Choose whether to print any window within the
Mandelbrot set or one of its associated Julia fractals, with magnification
limited only by 16 digit double-precision coordinates.  (Default window
coordinates: The Mandelbrot set [x(min)=-2.4, x(max)=0.8, y(min)=-1.2,
y(max)=1.2.],  Complete Julia sets [x(min)=y(min)=-1.5, x(max)=y(max)=1.5.]

********************
* Complete or Zoom *
******************** The program can automatically enter parameters for the
complete Mandelbrot or Julia set, or you can magnify any area of the fractal by
entering window coordinates manually.  If complete is selected, the plotted
fractal will be proportional to its default window coordinates (see above.)  If
you want to distort a fractal, you must enter your own coordinates with Zoom.
This is true, for example, if you wish to stretch a Julia curve to fit a
rectangular page area.

********************************
* Centered or Top of page area *
******************************** Complete fractals may be centered in the
middle of the page area.  This function makes it easy to print full page,
centered, Julia curves without having to calculate window dimensions, and also
allows full page centering of the complete Mandelbrot set (the vertical
Mandelbrot plot is already proportional to the rectangular page area.)

*************************
* Square or Rectangular *
************************* If you choose to enter your own coordinates by
selecting Zoom, you can specify a square or rectangular plot.  Square plots
print to the upper portion of the rectangular page area.  (Complete Julia sets
are already proportional to the square page area.)

***********************************
* Distort or Maintain pixel ratio *
*********************************** If entering your own coordinates, the
program can also calculate the bottom window coordinate automatically in order
to make the fractal dimensions proportional to the page area in which the
fractal is mapped.  Otherwise, you may distort the map by entering all four
coordinates, in which case it is stretched or squeezed into the page area.

***********************************
* Proximity bands or Fractal only *
*********************************** Select whether to print only the points
which never escape to infinity (Fractal only), or to include alternating bands
showing how quickly other points escape the basin of attraction (Proximity
bands.)

**************************************
* Horizontal or Vertical orientation *
************************************** Fractals can be oriented either
horizontally or vertically.  Orientation refers to the real coordinate axis, so
that a horizontal plot has the real axis parallel to the sweep of the print
head and the imaginary axis perpendicular to it, while the vertical plot is the
reverse.

*************
* Page size *
************* Printing may be restricted to a full, half, quarter, eighth,
sixteenth, thirty-secondth, or sixty-fourth of a page (the selections only
suggest a rough estimate of the actual area.)  All page subdivisions are
proportional to the full page, and start in the upper left corner.  All
fractals are printed one-per-page.

**********************
* Graphic resolution *
********************** gemini-10X horizontal graphic resolution may be set to
low (60 dpi), high (120 dpi), or ultra-high (240 dpi), providing 480, 960, or
1920 dots going across an 8 inch full page.

*************
* Linefeeds *
************* To alter gemini-10X vertical graphic resolution, select either
full (1/72 inch) or half (1/144 inch) linefeeds, providing 768 or 1536 dots
going down a 10-2/3 inch full page.

*****************************************
* Maximum number of iterations (colors) *
***************************************** Enter the maximum number of
iterations before the program assumes that the current point will never escape
the basin of attraction.  The higher the number, the more chances each point
has of going off to infinity, and the thinner the fractal appears.  The counter
approaching this value also determines the rate at which points do escape the
set, which is used to map color bands if "Proximity bands" is set.  Setting the
number of iterations low saves on plotting time, but the closer to the fractal
you are (ie- deep magnifications) the more likely that a low iteration setting
will select too many points.  50-300 is a good range to start experimenting.

******************************************
* Maximum value of iterations (infinity) *
****************************************** The higher that virtual infinity is
set, the longer it may take to determine whether a given point will escape, and
the greater the chance that the point will be plotted (ie- does not escape)
within a given number of iterations.  Since any iteration resulting in a value
greater than 4 will go off to infinity, there is no good reason to use any
value other than 4, but since the proof eludes me, you can enter any value of
your choice.

*********************
* Enter coordinates *
********************* The program may ask for some or all of the minimum or
maximum, real or imaginary coordinates which define the fractal window,
depending on previous selections.  Be certain to read carefully which
coordinate the program is looking for, as it may skip what you might expect is
to be entered next.

*******************
* Enter constants *
******************* Julia sets require that you enter a real and an imaginary
constant which define the fractal.

**********************
* gemini-10X or Disk *
********************** Output may go directly to the printer, in which case you
will keep the neighbors awake late at night on long printouts.  Another
disadvantage of printing output directly is that the data can be printed only
once.  A better way to direct output is to a file on diskette, which is
quieter, and which enables you to print your fractal whenever you want.  The
file contains the gemini-10X graphics commands embedded within the data (ending
with a printer reset,) so that all you have to do is print the file from the
desktop.  The program automatically assigns an *.MJG (Mandelbrot/Julia/Gemini)
extender to the fractal file.  An *.DAT file is also created so that aborted
fractals may be continued at another time (this data file is automatically
deleted when the fractal is finished.)  All files are written to the root
directory of drive A.

*******************
* Parameter check *
******************* If all information has been entered correctly, type Y to
proceed.  If any entry was made incorrectly, you will have to type N and enter
everything again, so type carefully.

*******************
* List parameters *
******************* You can elect to save to disk (or to print) a list of
parameters so that you can keep track of previous output without having to
write it manually.  The output device is chosen when selecting where to output
the fractal.  The parameter file has the same name as the fractal, with an
*.TXT extender.

******************
* Fractal output *
****************** The fractal will then be printed to the selected device.  No
check is made to ensure that your printer is on-line or that a diskette with
adequate room is in the assigned drive.  Remember to set up everything properly
before running the program.  The number of print blocks remaining to be
calculated appears in the bottom right corner of the screen.  Each time a print
block is completed, the bell will sound.  Also, pressing <?> will display the
percentage of the current print block which has been completed.  To stop output
in mid-stream, type Control-C, in which case the program will stop running and
you will return immediately to the desktop or shell. It is best to do this near
the beginning of a print block as the current unwritten block will have to be
recalculated. The system may be powered down (such as an unexpected power
outage) without fear of losing data as long as the disk is not being written
to.

***************************
* More about resolution...*
*************************** Dot matrix printer dots are not true picture
elements (pixels) as they are not rectangular, and are not perfectly space
filling.  If you want a printout where the dots just touch tangentially in both
directions, then select low resolution/full linefeeds, which gives a light and
grid-like printout using up to 480 x 768 = 368,640 dots.  If you want the dots
to overlap by 1/2 dot in both directions, select high resolution/half linefeeds
which uses up to 960 x 1536 = 1,474,560 dots for a nice, dark final printout
which has 23 times as many pixels as an ST low resolution color monitor.
Ultra-high resolution gives twice as many pixels, but since they overlap, the
result is not substantially different than high resolution but takes twice as
long, so I recommend using only the two combination settings above.

***********************
* Time Considerations *
*********************** These fractals take a long time to finish.  Anyone who
has created fractals on screen has an idea of what I mean.  To be more
specific, if a low resolution screen (320 x 200 = 64,000 pixels) fractal takes
1 hour, then the high resolution, full page gemini-10X plot with 1,474,560 dots
(see above) would take 1,474,560/64,000 = 23 hours.  That is just about how
long a high resolution, full page, square Julia fractal with low iteration
settings takes to complete.

Nearly every parameter can have an effect on the amount of time to print out a
fractal.  The higher the resolution, the larger the page size, the higher the
iteration parameters, the deeper the magnification into the set, and the more
points that are in the set; the longer the fractal will take to output.  I
started an ultra-high resolution Mandelbrot zoom of about 1,000,000 x
magnification with iterations=300 to a full page.  After 10 hours, 2 of 96
print blocks had occurred.  If I had allowed this fractal to finish, it would
have taken 10 x 48 = 480 hours = about 20 days to finish.

**************
* Data Entry *
************** One of the best ways to find areas of interest within the
Mandelbrot set, as well as aesthetically appealing Julia sets, is to experiment
with programs which create these fractals on screen.  "Fractal Fantasy 2.0" is
especially nice because of its locate function which provides Julia constants
close to the Mandelbrot set just by clicking on it, as well as its "small"
feature which makes rapid investigation possible.  Many public domain fractal
generators are also available (Fractal Mayhem, Fractal Zoom, Mandel Show, etc.)
The best sources of information about fractals are interesting books on the
subject:

****************
* Bibliography *
****************

"The Fractal Geometry of Nature" by Benoit B. Mandelbrot

"CHAOS: Making a New Science" by James Gleick

"Fractals Everywhere" by Michael Barnsley

"Chaos, Fractals, and Dynamics: Computer Experiments in Mathematics"
 by Robert L. Devaney

"Fractals: Endlessly Repeated Geometrical Figures" by Hans Lauwerier

"The Beauty of Fractals: Images of Complex Dynamical Systems"
Ed. Heinz-Otto Peitgen & P.H. Richter

"The Science of Fractal Images" Ed. Heinz-Otto Peitgen & Dietmar Saupe

"Fractals: The Patterns of Chaos (Discovering a New Aesthetic of Art, Science,
and Nature)" by John Briggs

*******
* End *
*******