Addendum to QRT Version 1.4
        
        
        
        The following are changes to QRT made since version 1.3
        
        Additions and Enhancements
        
           Transmission
               
               Transmission of light through surfaces now works, allowing
               one to  model  glass  surfaces.   Some  additions  to  and
               changes  from  the  original  grammar  were  necessary  to
               provide  the  desired   functionality.    A  new  keyword,
               "DENSITY", has been  added,  and  the  function of the old
               "TRANS" keyword has  been  changed.   Also,  a "THRESHOLD"
               parameter has been added to the  default structure.  Since
               transmission is a complex operation,  this entire Addendum
               will discuss aspects of modeling glass surfaces.
               
           The DENSITY keyword
               
               It was my previous  intent  that  the  TRANS keyword would
               specify  the  percent  transmission  of  light  though the
               surface.  After thinking a little more about the nature of
               light  transmission,  it   was   clear  that  this  wasn't
               adequate.  The amount  of  light  transmitted  depends not
               only on a fixed  coefficient  of  the  surface, but on the
               thickness of the  surface.   For  example,  a hollow glass
               sphere will appear darker  (transmit  less light) near the
               edges, where the glass is  thickest.   To account for this
               effect,  the  "DENSITY"   keyword   was  added.    Density
               specifies what  percentage  of  transmitted  light will be
               removed per unit  distance  travelled  though  the object.
               For example, the following density  attribute would remove
               2 percent of all light per unit distance:
               
                    DENSITY = (.02, .02, .02);
               
               If a sphere, at its widest  point,  was 10 units thick, 20
               percent of the light would  be  removed.  Near the edge of
               the sphere, less light would be removed.
               
               Since density is a function of  distance, the same density
               factor will have different effects on objects of different
               sizes.  To remove the  same  percentage  of  light from an
               object half as thick, double the density factor.
               


        QRT Ray Tracer               Page 1               Addendum to 1.4












           Shadows from Transparent Surfaces
               
               The old "TRANS" keyword  still  exists,  but it performs a
               different function.  It does not  affect the appearance of
               the object, but rather, the  attenuation  of  light passed
               through the surface.  QRT  knows  how  glass surfaces bend
               light, and so it  can  model  the  magnifying  effects  of
               looking through  curved  glass,  etc.   But  for computing
               shadows, it cannot  properly  bend  the  light from lamps.
               This means that you  can  model  lenses  that the observer
               looks through, but  not  lenses  used  to focus light.  In
               order to provide  some attenuation effects, use "TRANS" to
               tell QRT how much light  is  passed  through  the surface.
               This information is ONLY used  for computing shadows.  For
               example,  blue  glass  should  cast  a  blue  shadow.  Use
               something similar to:
               
                        TRANS = (0, 0, .7)
               
               to cast a blue shadow (this  lets  70  percent of the blue
               light pass).  Note that by  using  strange combinations of
               DENSITY and TRANS, you can  model  illogical objects which
               appear, for example, blue,  but  cast a red shadow.  These
               shadows will be entirely of  one  intensity,  and will not
               vary with the thickness of the glass.
               
           Using MIRROR with Transparent surfaces
               
               Glass surfaces not only refract  light, but also reflect a
               percentage of it.  This means  that to realistically model
               glass, the glass should reflect  a small percentage of the
               light.   Try starting with  20  to  25 percent reflection.
               Note that all glass objects  reflect  light  from both the
               outside and the inside surfaces of the glass.
               
           Index of Refraction
               
               The index of refraction for an object governs how much the
               light is bent  upon  entering  or  exiting  the object.  A
               higher index will  bend  the  light  more.   The  index of
               refraction of air is 1.00, and  for glass is roughly 1.33.
               Some substances, such as diamond, have a higher index.
               
           Modeling Hollow Objects
               
               When designing the QRT transmission  routines, I wanted to
               be able  to  model  both  solid  glass  and  hollow  glass
               objects.  To understand how this  is done, it is necessary
               to understand a little about how  QRT's transmission model
               works.
               


        QRT Ray Tracer               Page 2               Addendum to 1.4












               A ray, after leaving the observer,  has two states: either
               it is inside a glass  object,  or  it is outside.  The ray
               starts out outside.   When  it  first  encounters  a glass
               surface, it is bent, and its state is toggled from OUTSIDE
               to INSIDE.  It continues  on  until  encountering  another
               surface, whereupon it is bent again, and its state is once
               more toggled.  This has several  implications for modeling
               glass.  The first is that ALL glass surfaces MUST have two
               sides - that is, once the ray enters the glass, there must
               be no way for it to exit  without  again passing through a
               surface.  The second is that  a  ray must go from glass to
               air, or air to glass,  but  not  from  glass with index of
               refraction A to glass with index of refraction B; i.e, the
               two glass surfaces cannot  touch  each  other, even though
               they may be placed very close together.
               
               As an example of how this  works,  consider  a solid glass
               sphere.  The ray encounters  the  sphere,  and is bent (in
               this case, towards the normal  vector).  QRT now remembers
               that  the  ray  is  INSIDE  a  glass  surface.    The  ray
               continues on until it hits  the  back  side of the sphere,
               whereupon it is bent (away  from  the  normal vector), and
               its  state  is  toggled  to   OUTSIDE.   In  summary,  the
               INSIDE/OUTSIDE flag tells QRT how to bend the ray.
               
               Consider now the case of a  hollow  glass sphere.  This is
               modeled using two concentric  spheres,  one with a smaller
               radius.  The ray will  first  hit  the  outside sphere, be
               bent, and have its state toggled  to INSIDE. There are now
               two possible cases.  First,  the  ray  may miss the inside
               sphere, in which case the  simulation  proceeds  as in the
               above paragraph.  Second,  it  may  hit the inside sphere.
               In this case, it is  bent,  and  its  state  is toggled to
               OUTSIDE.  The ray is now considered  to be back in air, so
               that the inside sphere has  modeled  the hollow portion of
               the glass.  In a similar manner, the ray reaches the other
               side of the inside  sphere,  enters  the  glass again, and
               finally leaves the outside sphere.   Note that even though
               the inside sphere is thought of as the "air" in the center
               of the object, it MUST have  the  same index of refraction
               as the outside sphere.  This is  necessary so that QRT can
               correctly bend the light when it exits the glass.
               
           Chromatic Aberration
               
               In QRT,  all  rays,  regardless  of  color,  are refracted
               exactly the same.  This is contrast  to the real world, in
               which  the  amount  the  light  is  bent  depends  on  its
               wavelength.  This appears,  so  far as I can tell, to be a
               bug in the real world, and I  saw  no reason to include it
               in a ray tracer.


        QRT Ray Tracer               Page 3               Addendum to 1.4












               
           Threshold attribute
               
               A new keyword, THRESHOLD,  has  been  added to the default
               structure.   In  previous  versions  of  QRT,  there was a
               mechanism for detecting  infinite  recursion provided that
               objects  reflected  less  that  100  percent  of the light
               reaching  them.   QRT   stopped  the  recursion  when  the
               intensity of the light  reached  1 percent of its original
               value.  When  transmission  was  added,  I made this value
               adjustable.  With  glass  objects,  both  surfaces reflect
               light, and if QRT waits  until  the  1 percent mark before
               stopping recursion,  the  time  necessary  to complete the
               image is greatly increased  with  little or no increase in
               image quality.   The  default  is  now  10 percent, and is
               changeable as follows:
               
                    DEFAULT ( threshold = .05
                            )
               
               This would stop  recursion  when  the  intensity reaches 5
               percent of the original value.  An added effect is that if
               the objects surface reflects (or  transmits) less than the
               threshold amount of light, the  reflection or transmission
               will be ignored completely.
               
           Affect of Glass on Speed
               
               Unfortunately, the presence of any glass objects will slow
               the ray tracer down.  This  effect  may  range from barely
               noticeable,  for  few,  small  objects  to  excruciatingly
               miserably slow, for many, large  objects.  Sorry, there is
               nothing I can do to speed it  up  - the 68000 simply won't
               go any faster.  The reason for the 
               slowdown is that for every ray/glass surface intersection,
               TWO additional rays must be  sent  out (as opposed to one,
               for reflection).   And  remember,  each  ray  intersects a
               glass object twice: once on  the  way  in, and once on the
               way out.  Also, the two  generated  rays may intersect the
               glass, as well.  You can  see  how  this process could get
               very slow.
               
        Notes, etc.
           
           Watch for control  characters  in  the  QRT input file.  I had
           accidentally imbedded an invisible control character in a file
           I was working on, and  the  QRT  parser  refused  to parse the
           file.  After closely checking the  file, I began to look for a
           bug in the parser  code.   Finally,  I  discovered the control
           character, but only after spending  1 hour checking the parser
           code.  The QRT parser will  generate  a SYNTAX ERROR, CODE 207


        QRT Ray Tracer               Page 4               Addendum to 1.4












           upon encountering any special characters in the input file.
           
           Since transmission involves  heavy  recursion, don't forget to
           set the default  stack  size  to  something  larger  than  the
           default 4000 bytes.  A  stack  size  of  40000  to 50000 bytes
           seems safe for most images.
           
        Notes on Multitasking
           
           The following discussion is not at all QRT specific, but it is
           here just to clear up some  confusion  many  people have about
           multitasking. 
           
           There has been some discussion to the effect that multitasking
           is either: a) not  useful  at  all  (just  ask  Apple/Mac type
           folks), or b) useful only as a mechanism for loading more than
           one interactive program  at  once  and  switching between them
           (said/believed by many Amiga  folks).   While  for some people
           this may be true, for anyone who  runs ray tracers, mandelbrot
           set program, or down/uploads programs from a BBS, multitasking
           holds great benefits.  Try this:  run QRT on the Amiga, in the
           background, with a low task  priority.   Now  forget about it,
           and  do  whatever  else   you   wanted   to  do  (run  a  text
           editor/spreadsheet/terminal prog, etc).  Now, run a ray tracer
           on an IBM or MAC II, and  you'll  very quickly tire of staring
           at the machine while it thinks.  
           
           The key to getting the maximum benefit from multitasking, (and
           this is what many  people  don't  realize),  is  being able to
           specify task priorities.  Non  interactive,  number  crunching
           tasks should be given a low priority (try -5).  This will give
           any interactive tasks all the CPU time they want.  By lowering
           the  priority  of  the   background   tasks,   the  editor  or
           spreadsheet or compiler will run just as fast as it would have
           without the background task.   If  the  background task is run
           with the SAME priority as the  foreground  task (editor, etc),
           the foreground task will run  noticeably  slower.   Don't ever
           run a task such as a ray tracer  with a HIGHER priority as the
           CLI or interactive task.  Doing  so will cause the interactive
           task to stop dead until the ray tracer has finished.
           
           One more note on multitasking for programmers: do try to write
           nice, friendly programs that  give  up the CPU when they don't
           need it.  Number crunching programs typically need all the CPU
           time they can get; however,  interactive  programs do not.  If
           you wish to wait, use the timer  device, not a for loop.  This
           has two advantages: 1)  it  doesn't  hog  the  CPU, and 2) the
           elapsed time will be  relatively  independent  of how busy the
           CPU is.  There  is  nothing  more  annoying  than  some little
           calculator or notepad  program  that  wants  ALL the CPU time,
           causing low priority  tasks  to  stop.   Even  some commercial


        QRT Ray Tracer               Page 5               Addendum to 1.4












           software  houses  have  committed  this  fault  (witness  some
           popular paint programs or terminal programs).
           
           OK, enough preaching  about  multitasking.   I  hope  this has
           cleared up the issue for anyone who was confused.
















































        QRT Ray Tracer               Page 6               Addendum to 1.4