MIDIBoard(tm)

                        Version 1.05
                     Copyright (c) 1991
                       by Jeff Beeghly

                    Released September 1, 1991


Table of Contents
	Introduction..................................p 1
	Disclaimer of Warranty........................p 1
	Credits.......................................p 2
	About MIDIBoard(tm)...........................p 2
	Bugs..........................................p 3
	Shareware.....................................p 3


                       INTRODUCTION 

	Announcing MIDIBoard, the desk accessory that graphically
represents incoming MIDI data.  The program serves several
purposes:

	* Invaluable source to test MIDI configuration (helps to
	  determine why a particular instrument isn't playing, e.g.
	  if a synth module isn't responding, is there something
	  wrong with the master keyboard, the module, or the MIDI
	  cable?)

	* Quick reference of MIDI note number (for devices that
	  don't list the corresponding note and MIDI note number,
	  such as drum machines and MIDI percussion controllers)

	* Tool to determine if a keyboard is sending note on/off
	  messages, system exclusive messages, pitch bend messages,
	  and MIDI clock start/stop commands


                      DISCLAIMER OF WARRANTY


	This software is sold "as is" and without warranties as to
performance of merchantability or any other warranties whether
expressed or implied.  Because of the various hardware and
software environments into which this program may be put, no
warranty of fitness for a particular purpose is offered.

	Good data processing procedure dictates that any program be
thoroughly tested with non-critical data before relying on it.
The user must assume the entire risk of using the program.  Any
liability of the seller will be limited exclusively to product
replacement or refund of purchase price. 


                             CREDITS

	This desk accessory was created and inspired from the
article, "Accessorize Your Programs" by Samuel  Streeper
(STart, October 1989), and the book, "C-Manship Complete," by
Clayton Walnum.


                         ABOUT MIDIBOARD(tm)

	MIDIBoard is a desk accessory that will graphically display
incoming MIDI data.  It will run in medium or high resolution on
an Atari ST, and features a modifiable window area, variable
note range (from C-2 to C8), selectable channel, and MIDI thru
options.  The following files should be contained in the
archieved file, MDB_1_05.ARC:

		COMMENTS.DOC    A text file that will help me to
		                determine bugs and effectiveness of my
		                program
		MIDIBRD.ACC     The desk accessory
		MIDIBRD.DOC     The text file that you are reading now
		MIDIBRD.NIC     A NeoDesk icon for midibrd.ac*


	The following is a run down of the options found in the top
portion of MIDIBoard:

		Thru			(Default is off) When selected,
					incoming data is sent out of the Atari
					MIDI out port

		Channel		(Default is Omni) Use the up and down
					arrows located next to the channel box
					to select the MIDI channel(1 - 16, omni)

		About		Clicking on this box will display the
					information about this program

		SysEx		This box is highlighted when the program
					receives a system exclusive ON message,
					and turns to its normal state when the
					program receives a system exclusive OFF
					message

		STart/STop	This box is highlighted when the program
					receives a MIDI START message, and turns
					to its normal state when the program
					receives a MIDI STOP message

		P Bend		This box is highlighted when there is
					pitch bend information being transmitted


                                BUGS

	Well, the first point I want to bring up really isn't a bug. 
Every reference I have (which includes books, musical
instruments, and other software programs) states that MIDI note
number 60 is C3.  The exception to this are Roland musical
products, which reference MIDI note number 60 as C4.  So, if you
are using Roland products, subtract one from the octave on
MIDIBoard.

	The other bug (which is a very serious problem) is that this
desk accessory does not work with most MIDI sequencing and
scoring software.  It turns out that these software programs
perform an interrupt on the MIDI port and are always inputing
data.  Although my desk accessory doesn't crash when operated
with sequencing programs, it acts as if it doesn't receive any
MIDI information.  On the other hand, it does work at the desktop
level, with non-MIDI programs, and MIDI programs that don't
continuously input MIDI data (like librarians and editors).

	If anybody knows of a fix for this program, I sure would
appreciate some help.  This desk accessory has been written in C
and uses the standard Bconin(3) command to input MIDI data.  I
believe that I need to create my own interrupt routine, but I
don't know very much about machine language programming so if
anyone can shed some light on the subject, I sure would
appreciate it.



                            SHAREWARE 
 
	Save $395!!!  ACT NOW!!!  Well, okay.....here's the deal.
Roland has a one space rack device out called the A-110.  It
displays MIDI data (like my desk accessory), but only displays
signals from MIDI note number 21 to number 108, and costs $400.
If you send me $5 for use of my desk accessory (which is your
legal obligation), you save $395!  BUT WAIT, THERE'S MORE!!!
MIDIBoard monitors a larger range of notes, incoming system
exclusive messages, MIDI clock start/stop, and pitch bend.

	If there is enough interest (read: registered users) in
version 1.05 of MIDIBoard, I will continue to invest my resources
in developing a routine to be able to use MIDIBoard with all MIDI
programs.  Some of the benefits of shareware you should consider
are: 
 
	*	You may try the software before you buy it.

	*	Generally, software authors are able to be implement
		and release revised editions of their program faster
		than software companies can.

	*	Shareware programs are often cheaper (in price) than
		comparable retail software.


	Thank you for taking the time to read this instruction file.
I would also appreciate it if you could take the time to print
out and answer the question in the file, COMMENTS.DOC. 


                          Thank you,

                          Jeff Beeghly
                          10552 14th N.W.
                          Seattle, WA   98177