PLAYBACK.ACC, PLAYBACK.PRG, and the associated documentation are 
     (C)opyright 1988, 1989 by Ric Clayton.  The Sound Tables and Replay 
     interrupt routines were provided by 2-Bit Systems REPLAY and are under 
     copyright held by 2-Bit Systems.  Used by permission.

          All versions of PlayBack (hereinafter referred to as "the 
     software") are copyrighted by the author.  The author reserves all 
     rights with respect to the copyright, including, but not limited to, 
     ownership, sale, and distribution of any and all versions of the 
     software.  No version of the software may be sold or included in a 
     commercial package without written permission from the author.

          The current version of the software is being distributed as 
     "Shareware".  It is not free.  You may upload it to information 
     services and networks (like GEnie, CompuServe, USEnet, etc.) or give it 
     to friends for evaluation.

          You may use the software for a limited time to evaluate it.  If 
     you like it and wish to continue using it, you should become a 
     registered user.  You become a registered user by sending $15.00 (US) 
     to the author.  (Be sure to include a note that you are registering as 
     a user of the software.)  Registered users will receive notices when 
     new versions are available.  Registered users may also obtain the 
     latest version of the software, when available, by sending a 3.5" 
     Floppy Disk and $5.00 (US) to the author.  (The more registrations I 
     receive, the more motivated I will be to enhance and maintain this 
     software and produce more Shareware.)

          PlayBack was designed and programmed by Ric Clayton using the 
     Megamax Laser-C development system.

          Inquiries, comments, suggestions, registrations, donations, etc. 
     are welcome and should be addressed to:

               Ric Clayton
               1000 Escalon Ave.  #1126
               Sunnyvale, CA.  94086  USA

               GEnie:    RIC
               Portal:   Ric Clayton
               USEnet:   ric.i.clayton@portal.com
               CompuServe:[73317,1350]


     1.0  What it is

          PlayBack is a GEM application to play back sound samples created 
     with Replay4 (formerly ST-Replay), distributed by MicroDeal.  Two 
     versions are included; a standard GEM application and a GEM Desk 
     Accessory.  Both versions operate identically and will operate in any 
     resolution.

          The Desk Accessory version also provides the capability for other 
     GEM applications to load and play sound samples.  This is accomplished 
     by sending GEM Pipeline Messages [i.e. appl_write()] to the PlayBack 
     Desk Accessory.  The advantage is that the application does not have to 
     have the sound routines built into it.  It need only load the sample 
     into memory and then instruct PlayBack to play it.

          Both versions also include a function optionally play back a 
     sample on startup.  A text string in the file PLAYBACK.INF tells 
     PlayBack the name of the startup sample.

          Sample playback may be stopped at any time with a single press of 
     the right mouse button.  (Since I feel this is something the user 
     should always be in control of, this feature cannot be disabled.)


     2.0  Installation

     2.1  Application Version

          The only requirement for the application version is that the 
     startup file, PLAYBACK.INF, must be in the "current directory" if you 
     want it to play a startup sample.  If you run it from the GEM Desktop, 
     this will be the same directory (folder) PLAYBACK.PRG is in.  Other 
     than this, there are no installation requirements for the application 
     version.  Just double-click on PLAYBACK.PRG.  When you're finished 
     reading the info box, left-click anywhere on the screen.  The startup 
     sample, if any, will be played and the main control panel will be 
     displayed.


     2.2  Desk Accessory Version

          To install the Desk Accessory version of PlayBack simply copy the 
     file PLAYBACK.ACC to your boot disk.  This should be the same place you 
     normally put the Desk Accessories you want to load when you boot your 
     computer.

          If you want PlayBack to play a startup sample, copy the file 
     PLAYBACK.INF to your boot disk as well.  It should go in the same place 
     you normally find the file DESKTOP.INF.  The sample will be played 
     after the GEM Desktop has been displayed.

          To use PlayBack, select "PlayBack" from the Desk Accessory menu.  
     The first time you select PlayBack, it will display its information 
     box.  Left-click anywhere on the screen and PlayBack will display its 
     control panel.  Thereafter, PlayBack will display its control panel 
     directly when selected.  (That is, until you change resolutions, reset, 
     or reboot your computer.)


     3.0  The Control Panel

          The control panel is where you control PlayBack from the Desktop.  
     It provides functions to allow you to select sample to play back, set 
     the playback speed, and start the PlayBack.  As always, play-back may 
     be stopped by clicking the right mouse button.

          The control panel is divided into three sub-panels.  Just below 
     the title box is the Selection Display panel.  On the lower-left is a 
     panel containing the speed select buttons.  On the lower-right is a 
     panel containing buttons used to operate PlayBack's functions.


     3.1  Selection Display

          When a sample is loaded into memory, the name of the sample file 
     will be displayed in this panel.  While a sample is playing, the word 
     "Selection" changes to "Now Playing".


     3.2  PlayBack Speed Buttons

          The left-hand panel on the lower portion of the control panel 
     contains 6 buttons arranged vertically.  These are the speed select 
     buttons.  The button labeled "5 Khz" selects the slowest speed and the 
     button labeled "31 Khz" selects the fastest.

          Initially, the speed will be set at 15 Khz.  This seems to be the 
     best compromise between sound quality and sample size for the Replay4 
     sampler.  You select another speed by clicking on the appropriate 
     button.


     3.3  Play Once

          After loading a sample, clicking on this button will play the 
     sample one time and then stop.  Clicking on this button does nothing if 
     a sample has not been loaded.


     3.4  Play Loop

          After loading a sample, clicking on this button will play the 
     sample repeatedly until the right mouse button is pressed.  Clicking on 
     this button does nothing if a sample has not been loaded.


     3.5  Load Sample

          Click on this button to load a sample into PlayBack's sample 
     buffer.  The sample is selected using the standard file selector 
     dialog.  After loading a sample, click on "Play Once" or "Play Loop" to 
     play it back.

          Once a sample is loaded, it will remain in PlayBack's sample 
     buffer until another sample is loaded or you exit the control panel.


     3.6  Exit

          Clicking on this button exits the control panel.  When you exit 
     the control panel, PlayBack releases all memory it was using to hold 
     samples.


     4.0  The Startup File

          PlayBack allows you to have a sample played when your computer has 
     finished booting up.  (It's kinda neat to hear HAL's voice informing 
     you that your computer is "fully functional.")

          When PlayBack starts up, it looks for a file named PLAYBACK.INF, 
     in the root directory of the boot drive for the Desk Accessory version, 
     in the current directory for the program version.  It expects this file 
     to contain a single line of text in the following format:

          <speed> <times> <path\filename>

          <speed> is a number that tells PlayBack the speed at which the 
     sample is to be played.  The numbers correspond to the buttons on 
     PlayBack's control panel.

               0 - 5 Khz
               1 - 7.5 Khz
               2 - 10 Khz
               3 - 15 Khz
               4 - 20 Khz
               5 - 31 Khz

          <times> is a number from 0 to 255 which tells PlayBack how many 
     times to repeat the sample.  0 means don't repeat, play it once.  255 
     means repeat it 255 times after playing it once.  (That is, play it 256 
     times.)

          <path/filename> is the name of the sample file to be played, 
     optionally including a drive and path specification.

          For example, if PLAYBACK.INF contained the line:

               3 0 D:\REPLAY\SAMPLES\HAL.SPL

     it would load the sample file named 'HAL.SPL' from the folder 
     'REPLAY\SAMPLES' on drive D and play it once at a speed of 15 Khz.

          The PLAYBACK.INF file include on the PlayBack distribution disk 
     contains the line:

               3 0 C:\PERFECT.SPL

     which will play the included sample file "PERFECT.SPL" from the root of 
     drive C:  when PlayBack is started, or booted as an accessory.  Edit 
     this with any text editor or word processor (save as an ASCII file) if 
     you want to change it, or just create a PLAYBACK.INF file of your own.  
     Remember to put it in the same place you put PLAYBACK.ACC, or run 
     PLAYBACK.PRG from.


     5.0  The Communications Pipeline

          PlayBack provides the capability for another GEM application to 
     request it to play back a sample.  This means that other GEM 
     applications can use sampled sound for prompting, sound effects, etc., 
     without having to know how to play back sound samples.  This is 
     accomplished by sending PlayBack messages through the GEM Message 
     Pipeline.  (Such messages are commonly known as "Inter-Process 
     Messages" or IPM's for short.)

          The messages you send to PlayBack, called "requests", consist of a 
     message code representing the PlayBack command, followed by one or more 
     parameters.  You send a message to PlayBack with GEM's appl_write() 
     function.

          PlayBack responds to each message with a message called the 
     "response".  You receive responses from PlayBack with GEM's 
     evnt_mesag() or evnt_multi() functions.

          C-language definitions for PlayBack's messages are included in the 
     file "PIPECMD.H" on the distribution disk.

          Note: All PlayBack messages are 16 bytes long.


     5.1  Message Headers

          PlayBack request and response messages begin with a standard 
     header.  This header identifies the PlayBack command and the ID of the 
     application sending the request.  The C-language definition of the 
     standard header is:

     typedef struct
             {
             int     msgcode;
             int     sender_id;
             int     unused;         /* Must be Zero */
             } IPMHDR;


     5.2  The HELLO command

          The HELLO command is used to check if the PlayBack Desk Accessory 
     is installed and active without having to do any real work, like 
     loading a sample.  It consists of a single parameter, "magic", which 
     must be set to 0x31415927.  When PlayBack receives this message with 
     the proper magic number, it will respond with a HELLO message in which 
     "magic" will be set to 0x72961413.  The C-language definitions for 
     HELLO are:

     #define HELLO_CMD       0x0101  /* msgcode for HELLO */

     #define HELLO_REQUEST   0x31415927L  /* Send this in HELLO request */
     #define HELLO_REPLY     0x72951413L  /* PlayBack replies with this */

     typedef struct          /* Hello command request/response definition */
             {
             IPMHDR  hdr;
             long    magic;
             int     unused[3];
             } HELLO;


     5.3  The PLAY Command

          The PLAY command is used to request PlayBack to play a sample.  It 
     consists of a separate request and response structure.  The request 
     contains several parameters used to control the playback of the sample.  
     The C-language definitions for the PLAY command are:

     #define PLAY_CMD        0x0102  /* msgcode used for PLAY */

     typedef struct                  /* Play command request definition */
             {
             IPMHDR  hdr;
             struct             /* Note: Megamax bit assignment may not */
                     {          /*       be the same as other compilers.*/
                     unsigned times:8;     /* Number of times to repeat */
                     unsigned freq:3;          /* Play back speed (0-7) */
                     unsigned unused:3;                 /* Must be Zero */
                     unsigned loop:1;  /* If True, repeat until stopped */
                     unsigned intext:1;    /* 0=monitor, 1=Replay cart. */
                     }control;       /* Playback controls */
             int     *data;          /* pointer to sample data */
             long    length;         /* length of sample */
             } PLAYREQ;

     typedef struct                  /* Play command response definition*/
             {
             IPMHDR  hdr;
             int     error;          /* 0 if no error, else error code */
             int     unused[4];
             } PLAYRSP;


          PLAYREQ contains several parameters:

          control - bit fields that control the playback
               times -   number of times to play the sample.  Range is 0 to
     255 for 1 to 256 times. Ignored when control.loop == 1.
               freq  - Specifies the playback frequency.
                           0 = 5 Khz
                           1 = 7.5 Khz
                           2 = 10 Khz
                           3 = 15 Khz
                           4 = 20 Khz
                           5 = 31 Khz
                           6 = 40 Khz  (external mode only)
                           7 = 50 Khz  (external mode only)
               unused -  reserved for future use (must be 0)
               loop   -  1=loop until stopped, 0=loop for 'times'.
               intext -  0=internal playback, 1=external (Replay4 cart.)

          data   -  is an integer pointer to the sample in memory. 
                    It is up to the sender to load the sample into memory.

         length  -  is the byte-length of the sample data.


         PLAYRSP is the response returned to the PLAYREQ request.  If the 
     error parameter is zero, then the request was honored and the sample 
     has finished playing.  Otherwise, the request was rejected, nothing was 
     played, and 'error' contains an error code as follows:

               -1   The frequency selection was out of range for internal 
                    mode playback.

               -2   Reserved bits not zero.


     5.4  C-language example

          Here is an example for communication with PlayBack.  This was 
     extracted from the file PLAYACC.C on the distribution disk, which 
     contains the C-language source code for a working program that sends 
     messages to PlayBack.  Examine it for a more thorough example.


          #include "pipecmd.h"

          int     *data;
          long    length;
          int     freq;
          int     myapplid;
          int     playback;

          HELLO   hello;
          PLAYREQ play_req;
          PLAYRSP play_rsp;

          main()
             {
             int event, zz;

             if ( (playback=appl_find("PLAYBACK")) < 0 )
                     {
                     puts("Can't find PlayBack!");
                     goto done;
                     }

             hello.hdr.msgcode = HELLO_CMD;
             hello.hdr.sender_id = myapplid;
             hello.hdr.unused = 0;
             hello.magic = HELLO_REQUEST;
             appl_write( playback, 16, &hello );

             event = evnt_multi( MU_TIMER|MU_MESAG,
                                     0, 0, 0,
                                     0, 0, 0, 0, 0,
                                     0, 0, 0, 0, 0,
                                     &hello, 2000, 0, &z, &z,
                                     &z, &z, &z, &z );

             if ( event & MU_TIMER )
                     {
                     puts("PlayBack did not respond to HELLO.");
                     goto done;
                     }

             if ( hello.magic != HELLO_REPLY )
                     {
                     puts("Bad Magic in HELLO response.");
                     goto done;
                     }
             puts("PlayBack says, \"Hello, you.\"");

          done:
            appl_exit();
            exit( 0 );
            }