Here is something that will test the number crunching ability of
your ST. There are some fairly extensive trigonometric calculations
in places.

This program computes data for the sun and moon. It was made with the
intent of printing monthly tables of sunrise and sunset or moon rise
and moon set. The program is based on several articles published in
Weatherwise magazine and expanded upon to add an easy to use user
interface. The program was first written on a Prime computer using
Fortran 77. It was then converted to Megamax C for the Atari ST. Finally
after discovering the floating point calculations were fairly slow,
it was converted to GFA basic which was about 5 times faster.

The rise and set computations are valid for a flat horizon at sea level.
Adjustments would have to be made for the actual times and angles
where there are hills on the horizon or where the location is at
a higher elevation. Care has been made to insure accuracy at high
latitudes (don't try the north pole). The program will perform
calculations for both northern and southern hemispheres. Times of
daylight savings time are set to the standard starting and ending
times in the United States. (First Sunday in April advances clock,
last Sunday in October set back clock.) For locations outside the
U.S. it is advisable to specify the clock advance as "NO" and adjust
the tables accordingly when summer time is in effect.

In order to run the program a file called LATLON.DAT is required.
This file contains data for specific locations including latitude,
longitude, number of hours from UTC meridian, and whether daylight
savings time is used. This enables fast access by locating file
data when required by the program. The LATLON file can be added to
through the program. It also can be added to or modified through a
file editor or word processor (The file must be resaved in ASCII,
not in word processing mode.) LATLON city names should be in capital
letters, the latitudes and longitudes are entered (in the file only)
without a decimal point. Hour differences from the 0 degree meridian
are positive for west longitudes and negative for east longitudes.
About two cities from each state some foreign locations are included
in the LATLON.DAT file. The maximum entries allowable in LATLON.DAT
is 500.

Medium or high resolution is required. When the program begins the
first location in the file is displayed in the status line at the
bottom of the screen. To change this start up location you have to edit
the LATLON file. To change the month of computation select the data
entry in the menu bar or the F1 key. Enter the month in number or
three letter format. Similarly the year can be changed using the data
entry menu or the F2 key. Years require 4 number format. To change the
location for the computation use the data entry menu or the F3 key. It
is not necessary to type the entire city name. The location with the
first characters in the LATLON file that match your entry will be
selected. For example to call up Los Angeles you would only need to
type L if it was the first L location in the file. If not Lo or Los
would probably work. Changes you make are displayed in the status line
at the screen bottom.

The F4 key or compute in the data entry menu will start computation.
Listing to the screen may be stopped at any time by pressing a key.
Another key press will resume the computation.

The options menu in the menu bar enables computation change from the
sun to the moon. Click on your choice. Default is the sun on program
start up. Also through the options menu you may display the entire
list of locations available. Another option enables you to enter data
for a new place. For instance you could type data for your own residence.
Follow the prompts. Latitudes and longitudes are entered in degrees and
hundredths, not minutes.

Output to the printer may be selected through the options menu or the
F5 key. When the printer is selected all computed output goes to the
printer instead of the monitor screen. Make sure you have the printer
turned on in advance.
 
Quit in the options menu or the F6 key is the only way to gracefully
exit the program.

In addition there is a choice of 3 different types of twilight for
the sun computations. The default is civil twilight which begins or
ends when the sun is 6 degrees below the horizon. You may also
select nautical twilight, when the sun is 12 degrees below the
horizon or astronomical twilight when the sun is 18 degrees below
the horizon.

Output shows rise and set times and day lengths in hours and minutes.
Times should be accurate to less than 1 minute for the sun and within a
few minutes for the moon, probably better at low latitudes than at high
latitudes. Change in day length is in minutes and seconds. Azimuth
angles of rise and set on the horizon are measured from true north and
are in degrees and tenths. Maximum elevations are also measured in
degrees and tenths. Transit or solar noon is the time that the sun
or moon is on the horizon due south. It is given to the nearest second
for the sun. This enables an observer to determine the location of
due south. Full moon occurs when the phase is shown to be .99.

There are centain conditions where there are no rise or set times for
a day. It is also possible to have two sunsets on the same day! 
The following conventions are used in the times showing these conditions:

..:.. Indicates there is no rise or set for this day, it occurs on the
      following day.
--:-- Indicates there is no rise or set for this day because the sun
      or moon stays below the horizon.
**:** Indicates there is no rise or set for this day because the sun
      or moon remains above the horizon.

Revision 1.1 added the following...
Through a line editor or word processor you may add elevation after the
UTC/local time difference in columns 33 through 37. Normally this is not
used but in the case where the observer is on a high mountain and
the horizon is near sea level it will make several minutes difference
in sunrise and sunset. This elevation is not computation is not done
for moonrise and moonset.

The status display line at the screen bottom was fixed to show correct
latitude and longitude.

Tests were inserted for screen resolution and printer status.

A file called DATLOC.DAT was added which remembers the last location,
month, and year used so when the program is rerun the same data
will be used.

Rev 1.2 added...
A delete function to the menu bar. A location can be deleted from
the LATLON.DAT file using this function.

Program was adjusted to allow locations in the southern hemisphere.

Suggestions for improvements are welcome. Write:

                      Dave Henry
                      1720 Wickersham Drive
                      Anchorage, Alaska 99507