08/13/91
Re: LVAPRN use; key maps; LVAFONTE output & fix; overview

LVAPRN works in conjuction with LVAFONT and allows you to print out your
special foreign or custom characters on an Epson 9 pin printer without using
GDOS. I've tested it on an Epson FX100 but it should work on most printers
claiming to be Epson FX compatible and possibly the RX and MX models. It uses
the downloadable font feature on this printer.  One exception is the Citizen
120D, which can only download to the range 0x20 to 0x40 which isn't enough for
all the characters.

LVAPRN is specially written to download to printer those fonts created with
EPSFNTED.PRG, a PD/sharewared Epson 9 pin font editor. I created one printer
font which is meant to be used in conjuction with the Cyrillic font that comes
with LVAFONTE. 

I'll attempt an overview of how all these programs work together. LVAFONTE.PRG
lets you create the ST system font that you see on your screen. EPSFNTED lets
you create a matching font for the printer. LVAPRN bridges the two fonts,
allowing you to print on your printer the fonts you see on your screen.

LVAFONT.ACC takes the characters stored in the ST character set locations 0xC0
to 0xFF and sends them to the editor you're using. It only seems to work with
some GEM editors. I've used FLASH and Word Writer with success but don't know
which others will work. You can switch between these special characters,
created with LVAFONTE .PRG, and the regular characters with Left-Shift + Alt.
When you're thru writing your text, save it as a plain ASCII file. That file
will now contain characters in the 0x20 (or 0x00) to 0x7F range, which are the
normal characters, and those in the 0xC0 to 0xFF range, which are the special
characters. 

There is also an accessory called EXTRAKEY which allows access to the special
characters and should work with all GEM editors that display the menu bar.

To print out the text run LVAPRN. It asks which printer font you'd like to
download to your printer. This will be the font you've created with EPSFNTED,
or in case of the Cyrillic font, enter CYRILLIC.PFT. If you have one printer
font you use a lot, you can rename it LVA.PFT and it will load automatically.
I included LVA.PFT, which is the same font as CYRILLIC.PFT, just so you don't
miss this feature. Next you'll be asked which text file you'd like printed.
Enter the name of the text file you created above. If you save your text under
the name LVA.TXT, LVAPRN won't ask which text file to print but print it
directly. I included a couple of text files as samples.

As the text file prints, LVAPRN checks each character to see if it's in the
normal range 0x00 to 0x7F, in which case it switches the printer to the normal
font and sends it directly to the printer; or in the special range 0xC0 to
0xFF, in which case it subtracts 0x80 and switches the printer to the download
font before sending the character to the printer. LVAFONT.ACC treats spacebar
as a normal character so switching between normal and special fonts usually
takes place between words. You may or may not notice the printer head go thru
some extra motion at such points. This is a feature of the printer.

As a guide to those who'd like to create their own printer fonts here's what I
did. Install LAVFONT.ACC and then run LVAFONTE.PRG. Notice that the desired
characters are in the range 0xC0 to 0xFF. Let's say you want to create a
character for your printer font that corresponds to the character you see at
0xC6. Subtract 0x80 (128 decimal) and get 0x46. This is the ASCII value you
need to edit. So, now run EPSFNTED, pick edit on the drop-down menu, enter
0x46 (70 decimal), and  'draw' the equivalent printer character. The only
exception is the character you see at 0xFF (in the LVAFONTE.PRG grid), it does
not become 0x7f as expected. Instead edit 0x31 (0xB1-0x80) in the EPSFNTED
program. 

The following table, barring any typos, shows how LVAFONT.ACC translates your
keypress into the code for the special character. When you're typing with the
special characters switched on and you press the the key in the CHAR column 
(with its ASCII value in the ASCII column), LVAFONT.ACC generates the value in
the BECOMES column + 0x80. LVAPRN later takes that value and subtracts 0x80 
(128 decimal), creating the value in the BECOMES column, and sends it to the
printer. It is the value in the BECOMES column that you use for selecting the
character to edit when using EPSFNTED.

Where there is a character in the 4th column, the BECOMES column is the actual
value generated by LVAFONT.ACC, not 0x80 less. These particular characters are
printed from the normal character set and are not to be edited by EPSFNTED.
Numerals and their symbols are also printed from the normal set but you get
numbers when you hold the shift key down and symbols otherwise. That's the way
the Cyrillic keyboard is and I'm not sure what changes you can make with
LVAFONTE.PRG to 'Americanize' it.

One other note about LVAFONTE. It seem that once you have it loaded, you lose
your backslash (\) in the English mode. I've found that if I change byte 0x2B
of LVARUSS.KBD from a '$' to a '\' the problem is corrected. I don't know what
else this change affects so I don't make any guaranties. I included this
'corrected' version in this archive. 

CHAR   ASCII  BECOMES
       (HEX)  (HEX)

q      71      69
w      77      76
e      65      73
r      72      6a
t      75      65
y      79      6d
u      75      63
i      69      78
o      6f      79
p      70      67
[      5b      75
]      5d      7a
a      61      74
s      72      7b
d      64      62
f      66      60
g      67      6f
h      68      70
j      6a      6e
k      6b      6b
l      6c      64
;      3b      66
'      27      7d
\      5c      7c (|)
z      7a      31
x      78      77
c      63      71
v      76      6c
b      62      68
n      6e      72      
m      6d      7c
,      2c      61
.      2e      7e
/      2f      3f (?)
====================
upper case:

Q      51      49
W      57      56
E      45      53
R      52      4a
T      54      45
Y      59      4d
U      55      43
I      49      58
O      4f      59
P      50      47
{      70      55
}      7d      5a
A      41      54
S      53      5b
D      44      42
F      46      40
G      67      6f
H      48      50
J      4a      4e
K      4b      4b
L      4c      44
:      3a      46
"      22      5d
|      7c      7c (|)
Z      5a      5f
X      58      57
C      43      51
V      56      4c
B      42      48
N      43      52
M      4d      5c
<      3c      41
>      3e      5e
?      3f      5f (_)

==============================================================================

Please keep this file together with the program. Additons and corrections are
permitted, deletions are not. Hopefully, others will benefit from the info and
be encouraged to contribute to expanding and improving these useful programs.
Those who have looked for an alternative to GDOS for printing special
characters and symbols should appreciate such efforts.

Alex Fetesoff
P.O.Box 163681
Sacramento, CA 95816

CIS: 72277,1607
GENIE: ALEX.F
DELPHI: ALEXF
UUCP: ...ames!pacbell!sactoh0!alexf
INTERNET: alexf@sactoh0.SAC.CA.US