======================================================================
 A memory test program for the Atari ST (tm) and Mega (tm) computers.
======================================================================
                                              Version 1.0, 02-jan-1990

OVERVIEW

This text comes to you with a program to test the random access memory
of Atari ST and Mega computers. The text consists of a discussion of
state-of-the-art random access memory testing in general followed by
some considerations about memory testing on the Atari ST and Mega
computers in particular and a description of the program. The program
and this text are NOT in the public domain. A modest shareware fee is
requested from those who find this program useful. We encourage you
to spread copies of this text and the program to your friends and to
electronic bulletin board systems. However, we insist that this text
and the program are NOT CHANGED IN ANY WAY and are always DISTRIBUTED
TOGETHER.

                                        Peter Knoppers, Harm Salomons.


WHY MEMORY TESTING ?

Some defects in computer memories result in immediate failure of the
computer system. Others are more subtle and can remain unnoticed for
a long time. Defects in computer memories can indeed be very hard to
find and the effects of a defect can be very expensive. In recent
years memory testing has transformed from an art into a science. Many
computers do not execute a memory test after power-on, or use one with
very questionable fault detection capabilities.


WHEN SHOULD YOU TEST MEMORY ?

Memory testing is performed to identify a failing memory chip or to
prove that there are no faults present. (As will be explained below,
absolute proof of absence of faults is unattainable.) In general, when
something about the memory configuration of a computer has been
changed it is advisable to test all memory of that computer. If a
computer system has sporadic malfunctions, the memory is usually a
good place to start looking for the cause. Subtle faults in the memory
of your computer can damage the integrity of your files which may be
very expensive. In the absence of parity check (or a similar hardware
mechanism), you should test memory as often as you should make backups
of your files.

If your computer has parity check or a similar mechanism that checks
for errors on every read operation, you have in effect a continuous
memory test running in your computer. All professional computer
systems use such a mechanism. In this sense the Atari ST and Mega
computers are not professional computers...


WHAT IS MEMORY TESTING ?

In general, testing is performed to verify that a system performs as
specified. A specification for a computer memory could be:
    A system capable of storing all conceivable patterns consisting
    of a fixed number (called the capacity) of ones and zeros for a
    certain length of time and which allows for retrieval and update
    of any part of the pattern of ones and zeros without affecting the
    remainder of the stored pattern.

The definition suggests that to test a memory with a capacity of n
bits, one has to write all the 2**n different patterns in it, and for
each such pattern apply all possible transitions to other patterns.
Assuming that the memory is written with one bit at a time, there are
n possible transitions to be tested for each pattern, which results in
a total of n*2**n transitions that must be verified in order to prove
that the memory is free of defects. After each transition, the
contents of the entire memory must be verified (hoping that a read
operation does not influence the stored pattern). Clearly, this would
result in an astronomical number of read and write operations (taking
up excessive test time) even for very small values of n.

REDUCTION OF THE TEST TIME

When implementation aspects of computer memories are considered, it is
possible to identify large classes of faults that are extremely
unlikely to occur. For instance, if a memory is constructed from a
number of identical chips, it is unlikely that the contents of one of
these chips influences the behaviour of another. On a smaller scale,
one can argue that the contents of one cell on a memory chip can not
influence the behaviour of other cells on that memory chip, provided
that those other cells are separated from the first cell by a certain
minimum distance. All the cells that lie within this minimum distance
constitute the neighbourhood of the cell. Because the cells are
usually arranged in a rectangular grid, the neighbourhood of a cell
usually consists of the four or eight cells that lie adjacent to the
cell.

TESTING FOR NEIGHBOURHOOD PATTERN SENSITIVE FAULTS

There are known algorithms that can test for neighbourhood pattern
sensitive faults. Unfortunately, these tests are not generally
applicable, because the arrangement of the cells on most chips is not
very straightforward, it varies between different manufacturers and
sometimes even within the chips of one manufacturer. This is further
complicated by the fact that real memory chips are manufactured with a
few redundant rows or columns in the cell matrix. When a defect is
found during the manufacturing process, the wiring pattern on the chip
can be altered with a laser beam, so that one of the spare rows or
columns is used instead of the one containing the defective cell(s).
This means that even chips from the same batch can have different cell
array orderings and only the manufacturer can test with confidence for
neighbourhood pattern sensitive faults.

Normally the cell array is covered with a grid of row-select, column-
select and data lines. This means that a myriad of different shorts
are possible. Many of these cause pattern sensitive faults.

When the layout of the cells on the chips is unknown it is not
practical to test for pattern sensitive faults.

TESTING WHEN THE NEIGHBOURHOOD IS UNKNOWN

The next best thing (as testing for neighbourhood pattern sensitive
faults in general is unachievable) is to test for 2-coupling faults.
    A 2-coupling fault between two cells A and B is a fault where a
    transition in cell A causes a transition in cell B, irrespective
    of the contents of all other cells in the memory.
(The last part of this definition is the clever bit.) Each transition
can be up, or down, resulting in 4 possible types of 2-coupling faults
(up -> up, up -> down, down -> up, down -> down). The first published
algorithm designed for testing 2-coupling faults is (to our knowledge)
the SACO (Stuck At and COupling) algorithm published in [Na79]. The
SACO algorithm uses 14 writes and 16 reads per memory location. In
[Su81] the march-B algorithm was published. This algorithm detects the
same faults as the SACO algorithm, but needs only 11 writes and 6
reads per memory location.

OTHER TYPES OF FAULTS

In addition to any number of 2-coupling faults, SACO and march-B will
detect stuck-at and transition faults and address decoder faults.

    A stuck-at fault is a fault where a memory cell has a fixed value.
(This fixed value is either 0, or 1).
Stuck at faults faults can simply be detected by writing and reading
all addresses with the value 0 and with the value 1.

    A transition fault is a fault where a memory cell fails to make
    a certain transition.
(The failing transition can be either up or down.) This fault is very
similar to the stuck-at fault, however it is possible that after
powering up the system, the cell with the transition fault is in the
state that it can not reach via a transition.
Transition faults can be detected by writing and reading all addresses
with the values 0, 1 and 0 in succession.

    An address decoder fault is a fault where different addresses
    access the same memory cell, or one address accesses no cell at
    all.
It can be shown that SACO and March-B detect all address decoder
faults (this is not very difficult to prove).

WHAT IS MARCH-B ?

March-B can best be described in a pseudo programming language. In the
program below every read operation is assumed to signal an error when
the value read differs from the expected value. Statement grouping is
indicated by indenting (like in OCCAM).

   FOR address = lowest TO highest STEP 1
       write(address, 0)               # initialize all locations to 0
   FOR address = lowest TO highest STEP 1
       read(address)                   # if not 0: error
       write(address, 1)
       read(address)                   # if not 1: error
       write(address, 0)
       read(address)                   # if not 0: error
       write(address, 1)
   FOR address is lowest TO highest STEP 1
       read(address)                   # if not 1: error
       write(address, 0)
       write(address, 1)
   FOR address is highest TO lowest STEP -1
       read(address)                   # if not 1: error
       write(address, 0)
       write(address, 1)
       write(address, 0)
   FOR address is highest TO lowest STEP -1
       read(address)                   # if not 0: error
       write(address, 1)
       write(address, 0)

Each FOR loop is called a march-element.

Under the assumption that read operations do not alter the contents of
any memory cell it can be proven that there is no combination of
stuck-at faults, transition faults, coupling faults and address
decoder faults) that is not detected by this sequence of accesses.
However, the march-B test algorithm does not determine the type of
each fault and some faults may be obscured by others. (For example a
stuck-at fault in a cell that is inaccessible due to an address
decoder fault is undetectable.) Finally, one fault may be detected
(and reported) several times.

March-B is currently (1989) the state-of-the-art memory test for all
cases where the physical layout of the chips is unknown. There is no
known algorithm that can test for the more complex pattern sensitive
faults without this knowledge in reasonable time. Also, there is no
known test algorithm that achieves the fault coverage of march-B in
less time.

OTHER TYPES OF MEMORY FAULTS

There are other classes of faults that can be present in memories that
have been neglected so far. These faults are sensitive for timing,
heat, humidity, vibrations, electrical discharges, noise on the power
lines, etc. Some of these faults can only be detected when memory is
accessed at very high (or very low) speed or under special (stressed)
environmental conditions. Many of these faults are intermittent, that
is, they can not be reproduced on demand.

The reason for testing memory repeatedly for a long time is usually
the hope that an intermittent fault will be caught given enough test
time. Sometimes the environmental conditions are stressed, so the
intermittent fault may become permanent (as long as the stressed
environmental conditions last). The following table suggest some ways
to stress the environmental conditions of your computer while running
a memory test. For some conditions you may have to partly disassemble
your computer. As always, be very careful with the high voltages which
are present in and around the power supply while the computer is
switched on. All tests which involve opening your computer should only
be attempted if you are experienced in the repair of computer systems.

Stressing environmental conditions is not entirely without risk to
your computer either. If you cause damage to your computer it is your
problem, you may have stressed it too hard, or you may have had a
latent fault waiting to become permanent. The damage may or may not
covered by your warranty. We can not assume any responsibility.

condition              low budget stress method
high temperature       Use a hair drier to heat up the memory chips.
                       Temperatures above 100 degrees Celcius should
                       be avoided. You will have to open your computer
                       for this test to get the heat on the memory
                       chips. Take care, as plastic parts may not be
                       able to withstand much heat.
low temperature        Use a freeze spray. You will have to open your
                       computer for this test to get the cold right
                       on the chips and not in the power supply, the
                       floppy disk drive or the keyboard.
noise on power lines   Use a variac to vary the mains voltage of the
                       computer by NO MORE THAN 20 %. Disconnect your
                       hard disk and other peripherals that are not
                       necessary for this test and remove any floppy
                       disks from their drives. The strangest things
                       can happen when the supply voltage drops too
                       low.
other electrical noise Use a piezo electric gas lighter close to the
                       computer. This causes a tremendous amount of
                       electrical noise. If the computer stops working
                       immediately, you have probably disturbed the
                       operation of the MC68000. If a short while
                       after your spark a fault is reported, you may
                       have discovered a memory problem. If the faults
                       are reproducible or most of them apply to a
                       single bit, you have probably a fault in a
                       memory chip. Do not open the computer for this
                       test. If you have other electrical equipment
                       that interferes with radio reception, or a
                       cordless phone you could also try to operate
                       this equipment near your computer.
vibrations             Drop your computer (excluding any hard disks)
                       from one inch height onto the table
high humidity          This condition is very hard to control. You
                       could run the memory test program on hot, moist
                       days to determine if this influences the
                       performance of your computer.


MEMORY TESTING WITH MARCH-B FOR THE ATARI ST COMPUTER

The march-B memory test for Atari ST computer is carried out by the
MC68000 processor. This has a number of consequences:
- The test program itself must be stored somewhere in the memory;
  therefore it is not possible to test all the memory at once.
- The test program must have some way to report any detected errors to
  the user. If the BIOS of the Atari ST computer is to be used, some
  interrupt vectors and other data in low memory locations may not be
  disturbed. The screen is memory mapped; if this memory must be
  tested, the screen cannot be used for output.
- Some events such as address errors, bus errors, illegal opcodes,
  privilege violations, cause immediate transfer of control to an
  exception service routine whose address is stored in low memory
  locations. While these locations are being tested, these events will
  cause the system to hang. In unmodified Atari ST computers a bus
  error is generated when the processor attempts to access memory
  above 4 Mega bytes. Addresses below 8 are mapped to Read-Only-
  Memory. On reset the MC68000 loads the initial values for the PC and
  the SSP (supervisor stack pointer) from these addresses. A write to
  these addresses causes a bus error (even in supervisor mode). While
  in user mode any access to addresses from 0 to 2047 causes a bus
  error.
- Some memory locations can be modified by interrupt routines (for
  instance mouse movement interrupts modify the contents of the screen
  and keyboard interrupts add characters to a keyboard input buffer).
- When the Atari ST computer or Mega is reset, the BIOS determines
  the size of the memory chips present in bank 0 and bank 1. This
  information is used to program the MMU chip. A defective memory chip
  may cause the BIOS to program the MMU incorrectly. This means that
  the amount of memory in your system is effectively reduced by some
  amount.

HOW DOES THE PROGRAM WORK ?

The approach that is used in this memory test program is to use a
menu-driven part written in C to select memory limits, etc. and a part
written in MC68000 assembler that takes complete control over the
computer to test the memory. This part disables all interrupts and
directly accesses the parallel port or the RS232 serial port to output
progress reports and detected faults. If the memory from which the
memory test program is running is defective, there is an unavoidable
chance that address errors or other violations cause the system to
hang. The only way to cope with this possibility is to output progress
reports at regular intervals.

The memory test program knows which addresses it occupies and
automatically skips these addresses when testing memory. The program
has an option to run the test for a specified number of times,
changing position in memory after each run. It actually makes sense to
run this program from different addresses, because the memory where
the program itself is positioned is accessed at the highest frequency
that can be obtained under software control. Frequent accesses to one
(or a few) addresses can cause a small part of a memory chip to heat
up which may reveal a temperature dependent problem. The user of the
program will observe that the system hangs when such a fault occurs.
To cope with this problem the program can report its position before
each run.

The program accesses 16 memory chips at once, each chip belonging to a
different data line. The march-B program in pseudo code is written for
a 1 bit wide memory. March-B can be extended for 16 bit wide memories
by replacing the values 0 and 1 in the algorithm by any 16 bit word
and the one's complement value of that word. (The one's complement of
a word is obtained by replacing all ones by zeros and vice versa.)
There is not much reason for using patterns other than 00.....00 and
11.....11, except that some faults in the data line buffers and shorts
between data lines might be detected when more exotic patterns are
used. (Real shorts between data lines would probably prevent start up
of the system.) The memory test program has the option to use a few
other patterns than 00.....00 and 11.....11, it can even select a
pseudo-random value for each successive run.


HOW TO USE THE MEMORY TEST PROGRAM

The program is started from the desktop or from your favourite command
line interpreter. A menu is presented which allows selection of the
memory range to test and many other parameters. The use of the menu is
intended to be self-explanatory.

The entries "start address" and "end address" determine the address
range that will be tested. The highest address accessed is JUST BELOW
the "end address". Both addresses must be entered as hexadecimal
numbers. The table below may help you to translate a decimal number of
bytes, Kilo bytes or Mega bytes to a hexadecimal number of bytes.

  decimal  hexadecimal  Mega bytes  Kilo bytes   which Atari computer
        0           0       0             0
   524288       80000       0.5         512            520 ST
  1048576      100000       1          1024       1024 ST or Mega 1
  2097152      200000       2          2048            Mega 2
  2621440      280000       2.5        2560     user-upgraded 1024 ST
  4194304      400000       4          4096            Mega 4

Above the menu, the program displays the amount of memory that your
system appears to have as determined by the BIOS at startup. The MMU
chip limits access to memory above the 4 Mega byte limit. Some memory
extensions circumvent this limit. The program displays the address
where the MMU chip generates a bus error. If you select a higher value
for "end address" the memory test will be aborted by a bus error and
your computer may hang. No bombs will be displayed if the trap vectors
in low memory are overwritten.

The program displays how the MMU was programmed at boot time when the
BIOS determined the memory configuration. The BIOS tries to read and
and write specific patterns to certain addresses to determine the
amount of memory chips in bank 0 and bank 1. Some faults in the memory
chips may cause the BIOS to decide that less memory is installed than
is actually true, or it may even decide that no memory is installed in
bank 1. If bank 1 contains no chips, the MMU is (probably) programmed
for 2 Mega byte. Writes to this nonexistent memory have no effect,
reads yield amazingly reproducible values which seem to depend on the
instruction used to read them.

The "maximum run count" entry in the menu determines the number of
runs that the memory test program performs, unless the "maximum error
count" (see below) is reached. When the memory test program exits
(either because the "maximum run count" or the "maximum error count"
is reached), the system is rebooted. If the "maximum run count" value
is 0, the program will run forever, or until the "maximum error count"
is exceeded.

The entry "first execution address" determines the address to which
the memory test program is moved before it starts. The routine that
moves the test program to its destination cannot handle overlapping
moves. (The target and the source areas must be disjunct.) Therefore,
some values for the "first execution address" are not allowed.
It is informative to let the program run in the screen memory, where
you see a few pixels change as the program goes from one march element
to the next. The changes are small because the most used counters and
variables are kept in the registers of the microprocessor. If you have
no RAM disks or other resident programs that change the screen address
when they are installed, the screen memory ranges from the top of
memory in the computer minus 8000 (hexadecimal) to the top of the
memory.

The entry "relocation distance" determines how far the program is
moved in memory between successive runs. (If the "maximum run count"
is 1, the value of the "relocation distance" is irrelevant.) Certain
small values for the "relocation distance" are not allowed, because
the relocation routine cannot handle overlapping moves. Therefore the
"relocation distance" must be bigger than the amount of memory that is
occupied by the test program. If the program is about to be moved over
the "end address", it is moved to the "start address" instead.

The entry "patterns to use" selects the combinations of ones and zeros
to use as test patterns. There are four standard patterns, but the
program can also select a pseudo random pattern for each run.

The entry "output device" allows selection of the parallel port or the
RS232 serial port of the Atari ST computer for progress and error
reports. If the serial port is to be used, the baud rate and other
parameters must have been set before the memory test program was
started. The control panel accessory supplied by Atari can do this. If
not set explicitly, the baud rate will be 9600 baud, 8 databits, no
parity, one stopbit. The X-on/X-off option of the serial port will not
work with the memory test program.
If the parallel port is used, the memory test program will wait
forever for the printer to be put on-line. After about 30 seconds, it
will however use the sound generator of the Atari to summon attention.

The entry "report frequency" controls the amount of output generated
by the program (apart from reports about detected errors). Progress
reports can be generated once per run, once per march element (5 march
elements per run), or only when the program starts and exits.

All error reports contain the address where the error occurred, the
value that was actually read from that address and the value that the
program expected to read.

The "maximum error count" entry limits the maximum number of errors
reported by the program. Setting this limit is highly desirable when
you want to limit the amount of paper that might otherwise be filled
with error reports. When the "maximum error count" value is set to 0,
there is no limit.

With the last entry of the menu the memory test can be started, or the
parameters of the memory test can be saved on disk (the filename is
always MEMTEST.DAT), or recalled from disk. Once started, the memory
test program can only be stopped by pressing the reset button.

The memory test itself takes about 18.3 seconds per Mega byte per run.
This is quite good. The 8 MHz MC68000 can access memory no more often
than every 500 nano seconds. (Times were measured on an 8 MHz machine
with an ordinary stopwatch.)


DISCLAIMER

This program is provided `as is' without warranty of any kind. We will
not be liable to anyone for any damages or losses arising from the
use, or inability to use this program or this document.

This memory test has been written and tested with great care and we do
believe that it implements the march-B algorithm in an efficient
manner. As explained before, theory suggests that there are some kinds
of faults for which it is not possible to create a program or an
algorithm that detects these faults within a reasonable amount of
time.

Summarizing:

    We can not guarantee that the memory in your Atari ST computer is
    fault free, even when this memory test program reports no errors.
    On the other hand, there may be faults in your Atari ST computer
    that exhibit themselves as memory faults, but which are actually
    faults in other components.


SHAREWARE FEE

If you find this program useful, we would like you to pay a shareware
fee. We suggest DFL 20.-- (20 Dutch Guilders, about US $ 10.--). For
commercial users (who repair Atari ST computers for a living) a higher
fee seems more appropriate, but we leave the decision to you (the
commercial user).

Our names and addresses are:
   Peter Knoppers                     Harm Salomons
   W. Bilderdijkhof 59                W. Bilderdijkhof 116
   2624 ZG  Delft                     2624 ZK  Delft
   The Netherlands                    The Netherlands

   Email: knop@duteca.tudelft.nl


REFERENCES

Na78:   Nair, R., Thattle, S.M., and Abraham, J.A., "Efficient
        Algorithms for Testing Semiconductor Random-Access Memories",
        IEEE Transactions on Computers vol. C-27, no. 6, pp. 572-576,
        June 1978.
Su81:   Suk, D.S. and Reddy, S.M., "A March Test for Functional Faults
        in Semiconductor Random Access Memories", IEEE Transactions on
        Computers, vol. C-30, no. 12, pp. 982-985, December 1981.