UNEEKIT.TOS
				===========

	UNEEKIT.TOS is a programme to overcome a problem that strikes most
Atari ST users from time to time -- the lack of a unique serial number on disk-
ettes formatted on MS-DOS systems.  This problem gets re-discovered from time
to time and many fixes get suggested -- e.g. using different formatting
programmes, or a sector editor to patch the boot sector, etc. -- but so far I
have not seen a simple programme to fix a disk, so here is a little hack to do
the job.

The Problem:  When TOS wants to check if a diskette has been changed, it looks
at a sequence of 3 bytes in the boot sector, which get written with a random
24-bit number (i.e. pretty likely to be unique) when TOS formats the diskette.
If it sees the same number there as the last time it looked, it assumes (quite
reasonably) that the same diskette is in the drive and that the directory and
file allocation table (FAT) data it has in memory are valid for that diskette.
However, the field used by TOS to store this "serial number" is within the
field specified by Microsoft to hold a name given by the OEM supplying any
particular version of MS-DOS.  Since this name is always the same, TOS then
considers such diskettes all to have the same serial number.  Hence the problem
(which also obtains if you use a disk copy programme to duplicate a diskette --
the copy has the same serial number as the original!): TOS does not detect when
an MS-DOS diskette has been changed for another, and proceeds to write
directory and FAT information from the previous diskette onto the new one, with
usually disastrous results.

The Cure: You can circumvent the problem is several ways.  The simplest is to
put a TOS formatted diskette in the drive and press <Esc> before putting a
second MS-DOS diskette in the drive, so that TOS sees a diskette change.  You
can also close the diskette window and re-open it.  However these are "active"
measures that require you to remember which system each diskette was formatted
under.  Far better to eliminate the problem by ensuring that each diskette does
have a truly unique serial number.  Hence UNEEKIT.TOS, which reads in the
diskette's boot sector, provides it with a random serial number, and then
writes it back onto the diskette.  Now you only have to remember to UNEEK
each diskette the first time you bring it home from work...  UNEEKed diskettes
are still entirely usable under MS-DOS.

		Ivan D Reid,  Untersiggenthal CH  9/12/1990
 ivan@cageir5a.bitnet		20550::ivan	ivan@cvax.psi.ch
also close the disk