ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
               º  ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±  º
               º  ±                                             ±  º
               º  ±  DTMF Real-Time Decoder -- 486 DEMO Version ±  º
               º  ±                                             ±  º
               º  ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±  º
               º                                                   º
               ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
               º    Shima-nized Advanced Utilities - J.M. Shima    º
               º         Copyright (c) 1994-95 by James Shima      º
               º                 All Rights Reserved               º
               º                                                   º
               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


                   ÞÞÞÞ   R E F E R E N C E   M A N U A L   ÞÞÞÞ





             ¯ Type DTMF486D at the DOS prompt for a summary of options ®




INTRODUCTION
ßßßßßßßßßßßß

* This program functions as a real-time DTMF decoder.  One application
  where DTMF tones are used is in the standard American telephone dialing
  system.  The standard DTMF tones represent the numbers 1,2,3,4,5,6,7,
  8,9,0,*,# on a standard keypad interface.  The four reserved DTMF tones
  representing A,B,C,D are supported in the REGISTERED version.

* This program is capable of decoding DTMF tones from a Soundblaster
  Version 1.0 - 2.0, Soundblaster Pro, or TRUE Soundblaster compatible
  (16-bit or 8-bit) sound card in real-time.  Soundblaster 16 support
  has been reported to work but is fully untested at this point.

* This 486 version is geared toward persons with a 486DX PC or better.
  This version can be used by slower machines, but results will
  be error prone due to the non real-time processing.

* If your PC DOES NOT perform equivalent to a 486DX-25 or better,
  a quasi real-time switch is supported.  However, due to the nature
  of real-time processing, this means data will be lost and results
  may vary from system to system.

* The Soundblaster or compatible sound card MUST be connected to port
  address 220h and using DMA 1 (the factory settings).

* The input to the Soundblaster mic or line input can originate
  from any external communication device that supplies DTMF tones
  to the sound card.

* This program accepts COMMAND-LINE ARGUMENTS that are passed to the
  DTMF decoder.

* For a list of the arguments, type DTMF486D at the DOS prompt.

* The DEMO only decodes a maximum of 5 numbers.  Interested
  persons can receive the REGISTERED version with no limitations.


SOFTWARE LICENSE
ßßßßßßßßßßßßßßßß

The 486 DEMO version of the DTMF real-time decoder is shareware, and is free
for personal use only.  This is true as long as the DEMO is not alterted
in any fashion.  Registered users will receive the REGISTERED version of
the DTMF decoder and will receive documentation stating such.



The author offers no warranties on this program.  This program is provided
as is.  Use this program at your own risk.  I assume no responsibility in your
actions while you are using this program.  The author is not liable for any
damage caused to your computer while you are using this program.  Using
the program is your compliance to this statement and the license.


COMMAND-LINE ARGUMENT SCREEN
ßßßßßßßßßßßßßßßßßßßßßßßßßßßß

The program argument screen should look as follows:

Real-Time Dual-Tone Multi-Frequency Decoder, 486 DEMO Version
Shima-nized Advanced Utilities (c) 1994-95 - J.M. Shima

USAGE: DTMF486D  <sample_rate>  switches:[ <-t>number <-r>]

Notes:  <sample_rate> = rate of incoming samples in Hz. The range
                        is 4000 < fs < 12000 for DTMF decoding.
                        The RECOMMENDED value is 4000 Hz for real-time
                        decoding.

** Sound card must be Soundblaster 1.0 - 2.0, Pro, or Soundblaster
** compatible connected to port 220h using DMA 1 (The factory settings).

Switches: -t = Defines the S/N threshold value (in dB) that DTMF tones
               must surpass for proper detection.
               The threshold S/N value can be any real, non-negative number.
               DEFAULT value is 20 dB.
          -r = Enable real-time mode.  Use this for a 486DX-25 machine or up.
               Otherwise, use quasi real-time mode which is probable to
               give inconsistent results.  Real-time mode is OFF by DEFAULT.


EXPLANATION OF COMMAND-LINE ARGUMENTS
ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

<sample_rate>   -->  Input sample rate.  Must be in the range of 4000 to
                     12000 Hertz (Hz).  For DTMF detection, it is HIGHLY
                     RECOMMENDED THAT YOU USE 4000 Hz for real-time
                     processing.  However, testing indicated that a
                     486DX-66 could perform real time processing with a
                     8000 Hz sample rate.

Switches:
ÍÍÍÍÍÍÍÍ

 -t<number>    -->  The threshold that the DTMF tones must exceed over the
                    noise floor for detection (in dB).  Typically, strong
                    DTMF tones will be 20-40 dB stronger than the noise
                    in the signal.  However, noisy signals lower this
                    signal-to-noise (S/N) ratio.  The threshold parameter
                    allows the user to set the S/N threshold for detection
                    of noisier or corrupted DTMF tones.

                    * NOTE:  If nothing is entered, then the DEFAULT S/N
                             threshold value is 20dB, which is a figure
                             of merit for normal tones.


                    One must realize that dB is a logarithmic scale
                    of signal gain through the equation:
                    dB = 20 * log(signal gain).
                    Thus, a large signal gain represents a small
                    increase in the dB number (i.e. 40dB is a 100x
                    signal gain, while 20dB is a 10x signal gain).

 -r            -->  Enables TRUE real-time processing mode.  Include this
                    switch if your system is capable of handling the
                    flow rate of data.  Rule of thumb:  A 486DX-33 can
                    probably handle real-time.

                    ** NOTE:  Results will VARY from system to system.

                    By default, a quasi real-time process is included
                    for slower machines.  Obviously, this means data will
                    be lost due to computational overhead, put I have
                    tried to STRATEGICALLY MINIMIZE the effects of this.



EXAMPLES OF RUNNING DTMF486D
ßßßßßßßßßßßßßßßßßßßßßßßßßßßß

* Program start:  Run the program by typing the executable name.
* Program end:  The program ENDS when ANY key is hit during decoding!

 
DTMF486D 4000            -->   Input sample rate is 4000 Hz.  Quasi real-time
                               mode is enabled by default.  Input S/N
                               threshold defaults to 20dB.

DTMF486D 4000 -t25       -->   Input sample rate is 4000 Hz.  The input
                               S/N threshold is set to 25dB.  Quasi real-time
                               mode is enabled.

DTMF486D 4000 -r -t15    -->   Input sample rate is 4000 Hz.  The S/N
                               threshold is set to 15dB.  Real-time mode
                               for fast machines is enabled.


IMPORTANT NOTES
ßßßßßßßßßßßßßßß

Since this is a real-time piece of software, certain rules must be followed
for proper use.

Sampling rate:
                Increasing the sampling rate means that samples are ready
                faster.  Thus, the computer has less time to do what
                is has to before it has to fetch more samples.  So,
                one must make the sample rate as low as it can go
                and still represent the maximum frequency in the signal.
                For DTMF tones, this minimum sampling rate is 4000 Hz,
                (due to Nyquist theorem).  IT BEHOOVES YOU to use this rate.
                Sampling at a rate higher than necessary gains you
                nothing, but INCREASES your computational overhead. For real-
                time operation, make your sampling rate as low as you can

               without violating Nyquist theorem (2x the maximum freq.
                in the signal).  So, for all practical purposes, use
                4000 Hz as your sampling rate.

Real-time processing:
                If your system cannot handle real-time processing, that
                means data will be lost.  While your system is processing
                the old data, it doesn't have time to retrieve the new
                data coming in.  This new data is discarded and the
                computer picks up fresh data when it's done with its
                current task.  Thus, results are inconsistent when real-time
                processing cannot be done.  The probability of detecting
                a given tone depends on where your computer is in its
                processing stage.  You can see that its nearly impossible
                to debug whether or not real-time processing is happening
                or not.  On top of this, your CPU takes care of many other
                housekeeping tasks.  Therefore, I have deemed "real-time"
                on the fact that a DTMF tone does not go undetected as given
                in the DTMF standards.  Closely spaced tones will be detected
                in real-time if your system can run the code in real time.

                However, you can also decode all DTMF tones if there
                is enough time between tones and your computer works
                fast enough so to extract some data from each tone.
                In this case, the decoder is not working in real time
                but is able to extract data since a tone exists for
                a longer amount of time than it takes to perform a detection.
                In other words, longer DTMF tones are better detected
                in quasi real-time mode.  DTMF tones invoked by humans
                are very long compared to the time it takes your computer
                to detect them, so in quasi-real time mode you should
                be able to get good results.  This is why probability
                governs the detection process in the quasi real-time case.

                Noisy DTMF tones are also error ridden since the processing
                window is so small no noise immunity algorithm can be
                implemented.  Note that non-pure tones may not be detected
                properly!



INCLUDED FILES
ßßßßßßßßßßßßßß

DTMF486D.EXE   -->  DTMF real-time decoder, DEMO version.
DTMF486D.DOC   -->  This file.
REGISTER.DOC   -->  Registration form.
 


REGISTRATION
ßßßßßßßßßßßß

** For registration, please fill out REGISTER.DOC and see the DEMO screen.
   Specify media dispersement.

The REGISTERED version of this program allows unlimited decoding of numbers,
and offers other features including:




1) Automatic logging of the resulting decoded numbers to a log file.
   The session is also time and date stamped.

2) Time monitoring switch.  Allows deciphering of incoming streams of
   numbers if tone activity is not detected for a set number of seconds.

3) Supports the extended DTMF tones A,B,C,D.

4) REGISTERED users will also receive a DTMF generator program.  This is
   a DTMF tone generator which allows you to create any DTMF sequence
   you wish.  The program allows you to specify a DTMF number sequence,
   the sampling rate, and how long you want the pulses to be (in samples).



TESTING
ßßßßßßß

I have thoroughly tested this code and I am not responsible for any mishaps
that may happen when run on your computer.

SOUND CARDS TESTED:

Aztec Sound Galaxy 16 bit
Sound Blaster 8 bit
Sound Blaster ASP 16
Generic SB fully compatible 16 bit
Sound Blaster 16 VE *

* Some problems with the SB 16 VE have been reported and verified.
  Mic and line inputs for the SB 16 VE gave spurious results.  No
  explanation for this hardware problem has been determined.


TESTING PLATFORMS:

1)  The code was tested on an IBM compatible 25MHz 486DX Cyrix upgrade PC
    with a Soundblaster Version 1.5 sound card running DOS 5.0.  Tones
    were recorded onto a cassette tape and played into a microphone which
    was connected to the mic input of the Soundblaster card.  It was able
    to run in quasi real-time mode with a 4000 Hz sample rate and decoded
    numbers with approximately 90% accuracy.  Real-time mode was
    unachievable but gave similar results.  Using this test vector data,
    normal dialing was decoded 95% of the time.  Burst dialing was
    decoded 95% of the time.  Noisy tones gave inconsistent results.

    ** NOTE: All captured numbers were correctly decoded, the errors
    stemmed from the fact that real-time decoding was not possible!




2)  The code was also tested on a 486DX2-66 with an Aztec Sound
    Galaxy 16-bit Soundblaster compatible sound card.  The code was ABLE
    to run in REAL-TIoder is 2-6 you n card.  ThThem    be ablster Vers  Tnrin ng L-Thiser is 2-6 you n card.  ThThem  Tith aRMTn igram allnwas Acer Iodonsibn 2-6 you n whisnu n carany mishe errors
f al    E AcEr Iodonsibn 2-6sibu nonsn% accuracycareu can

  rEBris 2-quencn errong was noibnibn nonsn% acc ASklersn% accOiSse fills 2-6 Cncns erong was noibnibn nonsnranyC AS you patible souTncncomputeracycon rmng  smen reibnrd.s lo sequenceacc ASout REnfncnTncnuteracycon rmibn smen reibnrd.s.s  sen rpuredacctection
 onsibn 2-6sibIracyc imp

 s wn re.s.s  ebn C AS yrrmng  snibn nonsnranyCecoded, the ep

 s s wnsis.sE ebn C AS yrrmnAS snibn cFesnrec          nsnranyC AS yIeibncxI 2-n   C AS yon 1.n sncen cnsnArec