xiii

                           THE 8086 INSTRUCTION SET


             Before I go through the instructions I need to say something
             about the structure of the instructions. For the majority of
             instructions, two bits in the first instruction byte and the
             whole second byte determine whether it is a byte or word
             instruction and whether it is:

                 1. register, register
                 2. register, memory
                 3. memory, register

             These refer to the 8 arithmetic registers, not the segment
             registers. "Memory" is any allowable addressing mode. Therefore,
             it is simpler to abbreviate this as:

                 reg/mem, reg/mem

             This will always mean:

                 1. either a byte or word operation is allowed
                 2. any of the above 3 possibilities is allowed

             unless specifically stated otherwise. Another possibility is the
             operations with constants:

                 add  ax, 7
                 xor  sign_flag, 80h

             These follow the same form. There are two possibilities:

                 1. register, constant
                 2. memory, constant

             where this may be a byte or a word, "register" is any arithmetic
             register, and "memory" is any allowable addressing mode. These
             will be abbreviated:

                 reg/mem, constant

             If we are taliking about a segment register, they will be
             abbreviated:

                 segreg

             If anything does not follow this pattern, it will be explicitly
             stated.


             DESTINATION,SOURCE

             The standard way of writing instructions is with the destination
             on the left and the source on the right:

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             The PC Assembler Tutor                                        xiv
             ______________________


                 add  destination, source

             The register or memory location on the left ALWAYS gets the
             result of the operation. The thing on the right is the second
             operand (if any).

             ADDRESSING MODES

             These are the natural (default) segments of all addressing modes:

                 (1) DS

                      variable + (constant)
                      [bx] + (constant)
                      [si] + (constant)
                      [di] + (constant)
                      [bx+si] + (constant)
                      [bx+di] + (constant)


                 (2) SS

                      [bp] + (constant)
                      [bp+si] + (constant)
                      [bp+di] + (constant)

             Where the constant is optional. Segment overrides may be used.
             The segment overrides are:

                 SEGMENT OVERRIDE         MACHINE CODE (hex)
                      CS:                      2E
                      DS:                      3E
                      ES:                      26
                      SS:                      36


             These default segments apply to all instructions except the
             string instructions, which will be explained individually.



             THE INSTRUCTION SET

             AAA  (ascii adjust for addition) adjusts AL, assuming that it
             contains the result of a legitimate unpacked BCD addition. If the
             lower half-byte has generated a result 10 or over, it subtracts
             10, carries 1 to AH, and sets the carry flag. If the result is 9
             or less, it clears CF. In either case it zeroes the upper
             half-byte of AL.


             AAD (ascii adjust for division) PREPARES AL and AH for division.
             It assumes that AH contains the 10's digit and AL contains the
             1's digit of a two byte unpacked BCD number. It multiplies AH by
             10 and adds it to AL, thus making a single integer between 0 and
             99. It zeroes AH in preparation for unsigned division.





             Appendix II - The 8086 Instruction Set                         xv
             ______________________________________



             AAM (ascii adjust for multiplication) adjusts AL, assuming that
             it contains the result of a legitimate BCD multiplication. It
             divides the result by 10, putting the quotient in AH and the
             remainder in AL. If AL contains 73 before AAM, then afterwards AH
             will contain 7 and AL will contain 3


             AAS  (ascii adjust for subtraction) adjusts AL, assuming that it
             contains the result of a legitimate unpacked BCD subtraction. If
             the lower half-byte has generated a result -1 or less, it borrows
             1 from AH, adds 10 to AL, and sets the carry flag. If the result
             is 0 or more, it clears CF. In either case it zeroes the upper
             half-byte of AL.


             ADC (add with carry) adds two integers, either signed or
             unsigned, and adds in the carry from the previous arithmetic
             operation. It is used for multiple word (byte) addition.

                 adc  reg/mem, reg/mem
                 adc  reg/mem, constant


             ADD adds two integers, either signed or unsigned.

                 add  reg/mem, reg/mem
                 add  reg/mem, constant


             AND ands two bytes or words. A bit remains set only if both its
             respective source and destination bits were set.

                 and  reg/mem, reg/mem
                 and  reg/mem, constant



             CALL calls a procedure. The two forms we have used are NEAR and
             FAR calls.

                 call set_regs
                 call FAR PTR calculate_array

             There are two other forms where the addresses of the subprograms
             are in memory and changable. You should only use these forms if
             you are writing an operating system or a compiler, since they are
             an invitation to disaster.



             CBW sign extends the signed byte in AL to AH:AL in preparation
             for signed division. It is used alone without any register
             specification.

                 cbw





             The PC Assembler Tutor                                        xvi
             ______________________




             CLC clears the carry flag (CF = 0).


             CLD clears the direction flag (increments string pointers).


             CLI clears the interrupt flag (disables interrupts). All maskable
             interrupts must wait till the flag is set again before they will
             be processed.


             CMC changes the value of the carry flag. If CF =1, then CF = 0;
             if CF = 0, then CF = 1.


             CMP compares two values. It is the same as SUB except it does not
             alter the "destination" variable. Its job is to set the flags as
             if a subtraction had been performed, in preparation for a
             conditional jump instruction.

                 cmp  reg/mem, reg/mem
                 cmp  reg/mem, constant



             CMPS compares the byte (or word) at DS:[si] with the one at
             ES:[di], (calculating [si] - [di]) and sets the flags
             accordingly. It increments (or decrements) SI and DI depending on
             the setting of DF, the direction flag (by 1 for bytes and by 2
             for words). You may use CS:[si], SS:[si] or ES:[si], but you MAY
             NOT OVERRIDE ES:[di]. Notice that SI and DI are reversed from
             their position in the other string instructions.

                 cmpsb
                 cmpsw
                 cmps BYTE PTR SS:[si], ES:[di]     ;or CS, DS, ES:[si]
                 cmps WORD PTR SS:[si], ES:[di]     ;or CS, DS, ES:[si]



             CWD sign extends the signed integer in AX to DX:AX in preparation
             for signed word division. No register specification is used.

                 cwd



             DAA (decimal adjust for addition) adjusts AL, assuming that it
             contains the result of a legitimate packed BCD addition. It
             treats AL as two independent half-bytes. If the result of the
             lower half-byte is 10 or over, it subtracts 10 from the lower
             half-byte and adds the carry to the upper half byte. It then
             looks at the upper half byte. If its result is 10 or over, DAA
             subtracts 10 from the upper half byte and sets the carry flag.





             Appendix II - The 8086 Instruction Set                       xvii
             ______________________________________

             Otherwise the carry flag is cleared.



             DAS (decimal adjust for subtraction) adjusts AL, assuming that it
             contains the result of a legitimate packed BCD subtraction.It
             treats AL as two independent half-bytes. If the result of the
             lower half-byte is -1 or less, it adds 10 to the lower half-byte
             and borrows 1 from the upper half byte. It then looks at the
             upper half byte. If its result is -1 or less, DAA adds 10 to the
             upper half byte and sets the carry flag to indicate a borrow.
             Otherwise the carry flag is cleared.



             DEC decrements the byte or word by 1. It does not alter CF.

                 dec  reg/mem



             DIV performs unsigned division. If byte division, the unsigned
             double byte must be in AH:AL. Afterwards, AL has the quotient and
             AH has the remainder. If word division, the unsigned word must be
             in DX:AX. Afterwards, AX has the quotient, and DX the remainder.
             Division by a constant is not allowed. The DIV instruction does
             not mention DX:AX or AH:AL. They are understood.

                 div  reg/mem



             ESC (escape) signals to the 8086 that the bytes starting with the
             ESC byte are a coprocessor instruction. The 8086 will calculate a
             memory address (if appropriate) and give it to the coprocessor.
             The 8086 will then go on to the next instruction.  



             HLT (halt) halts the machine. It can be restarted with a reset, a
             non-maskable interrupt, or (if IEF is set) with a maskable
             interrupt.



             IDIV performs signed integer division. For byte division, the
             value in AL must be sign extended to AH (with CBW), giving the
             double signed byte AH:AL, after division, AL contains the
             quotient and AH contains the remainder. For word division, the
             value in AX must be sign extended to DX (with CWD), giving the
             double signed word DX:AX, after division, AX contains the
             quotient and DX contains the remainder. Division by a constant is
             not allowed. IDIV cannot perform multiple word division. To do
             that, you need to make the numbers positive and use DIV,
             adjusting the signs afterwards. IDIV does not mention the AL or
             AX register, it is understood.






             The PC Assembler Tutor                                      xviii
             ______________________

                 idiv reg/mem



             IMUL performs signed integer multiplication. The multiplicand
             must be in AX (or AL for bytes). After the multiplication, the
             result is in DX:AX for words and AH:AL for bytes. If DX (or AH
             for bytes) contains significant information, then CF is set (=1).
             If all the information is in AX (or AL for bytes) then CF = 0.
             Multiplication by a constant is not allowed. The IMUL instruction
             does not mention AX (or AL); it is understood.

                 imul mem/reg



             IN allows you to move data from a port address to AX (for a word)
             or AL (for a byte). There are two forms:

                 IN   al, port_number
                 IN   al, dx

             Where 'port_number' is a CONSTANT that is hard coded into the
             machine instruction and is from 0 - 255. The port address in DX
             may be from 0-65535. It must be the DX register.



             INC increments a register or a variable by 1. It does not effect
             CF. 
                 inc  reg/mem



             INT (interrupt) sends the program to a subprogram whose address
             is located in the interrupt vector table in low memory. For any
             interrupt number I, the 8086 goes to segment 0000, offset
             (I X 4). It loads IP with the first two bytes, then loads CS from
             the next two bytes. The next instruction executed will be at the
             new CS:IP. Before loading the new CS and IP, it pushes (1) the
             flags, (2) the old CS and (3) the old IP in that order.

                 int  3
                 int  21h



             INTO checks OF. If OF = 1, INTO generates interrupt 4. Otherwise
             it does nothing. It is used for error handling of signed numbers.

                 into



             IRET (interrupt return) is a special return instruction for
             interrupt routines. It pops (1) the old IP, (2) the old CS, and
             (3) the old flags in that order.





             Appendix II - The 8086 Instruction Set                        xix
             ______________________________________


                 iret



             JUMPS ---------------------------------------------------------

             There are two kinds of jumps. JMP is unconditional and can jump
             anywhere in the segment. All other jumps are conditional and are
             limited jumps from -128 to +127 bytes from the END of the jump
             instruction.{1}


             THESE ARE THE JUMP INSTRUCTIONS FOR SIGNED NUMBERS

                 jg        ; jump if greater
                 jnle      ; jump if not (less or equal) 

                 jl        ; jump if less
                 jnge      ; jump if not (greater or equal) 

                 je        ; jump if equal
                 jz        ; jump if zero 

                 jge       ; jump if greater or equal
                 jnl       ; jump if not less

                 jle       ; jump if less or equal
                 jng       ; jump if not greater

                 jne       ; jump if not equal
                 jnz       ; jump if not zero 



             THESE ARE THE JUMP INSTRUCTIONS FOR UNSIGNED NUMBERS

                 ja        ; jump if above
                 jnbe      ; jump if not (below or equal) 

                 jb        ; jump if below
                 jnae      ; jump if not (above or equal) 

                 je        ; jump if equal
                 jz        ; jump if zero 

                 jae       ; jump if above or equal
                 jnb       ; jump if not below 

                 jbe       ; jump if below or equal
                 jna       ; jump if not above
             ____________________

                1 There is also a long jump which can jump anywhere in memory
             (from 00000 to FFFFF). Except under special circumstances, using
             this is truly lousy programming practice. The long jump is for
             the Olympics, not for quality programming. 





             The PC Assembler Tutor                                         xx
             ______________________


                 jne       ; jump if not equal
                 jnz       ; jump if not zero 


             THESE JUMPS CHECK A SINGLE FLAG 

             These come in opposite pairs

                 jc        ; jump if the carry flag is set
                 jnc       ; jump if the carry flag is not set

                 jo        ; jump if the overflow flag is set
                 jno       ; jump if the overflow flag is not set

                 jp or jpe ; jump if parity flag is set (parity is even)
                 jnp or jpo  ;jump if parity flag is not set (parity is odd)


                 js        ; jump if the sign flag is set (negative )
                 jns       ; jump if the sign flag is not set (positive or 0)


             THIS CHECKS THE CX REGISTER

                 jcxz      ; jump if cx is zero

             This is used before entry to a loop to make sure the loop counter
             is not set to 0.


             INDIRECT JUMPS are jumps where the information for the jump is
             stored in memory (or in a register for an in-segment jump). These
             forms are dangerous and should be used only when writing things
             like multi-tasking operating systems. Have you written one
             lately?

             END OF JUMPS  - - - - - - - - - - - - - - - - - - - - - - -


             LAHF (load AH from flags) loads the lower half of the flags
             register into AH.



             LDS (load DS) loads the first two bytes of the memory address
             into the named arithmetic register and the next two bytes into
             DS. The register may be any arithmetic register, but this is
             designed for the 4 addressing registers: BX, SI, DI and BP.

                      lds  reg, memory_address



             LEA calculates an offset address and puts it in the named
             register.






             Appendix II - The 8086 Instruction Set                        xxi
             ______________________________________

                      lea  ax, [bp+si]+145



             LES (load ES) loads the first two bytes into the named arithmetic
             register and the next two bytes into ES. The register may be any
             arithmetic register, but this is designed for the 4 addressing
             registers: BX, SI, DI and BP.

                      les  reg, memory_address



             LOCK is for use if there is more than one 8086 operating in a
             computer. LOCK allows one 8086 to be the only one which can read
             from or write to memory during the following instruction. 



             LODS moves a byte or word from DS:[si] to AL or AX, and
             increments (or decrements) SI depending on the setting of DF, the
             direction flag (by 1 for bytes and by 2 for words). You may use
             CS:[si], SS:[si] or ES:[si].

                 lodsb
                 lodsw
                 lods BYTE PTR SS:[si]         ; or CS, DS, ES:[si]
                 lods WORD PTR SS:[si]         ; or CS, DS, ES:[si]



             LOOP/LOOPE/LOOPNE are conditional jumps (-128 to + 127 bytes).
             They will jump back to the start of the loop (which is identified
             by a label), under the following conditions:

                 loop      decrement cx ; jump back if cx is not zero
                 loope     decrement cx ; jump back if cx not zero AND zf = 1
                 loopz     decrement cx ; jump back if cx not zero AND zf = 1
                 loopne    decrement cx ; jump back if cx not zero AND zf = 0
                 loopnz    decrement cx ; jump back if cx not zero AND zf = 0

             Here, 'e' stands for equal, 'z' is zero and 'n' is not.

                 loop some_label



             MOV is the general instruction for moving bytes or words on the
             8086. The forms are:

                 reg/mem, reg/mem
                 reg/mem, constant
                 segreg, reg/mem
                 reg/mem, segreg

             Notice that you may not (1) move a constant to a segment
             register, (2) move a segment register to another segment





             The PC Assembler Tutor                                       xxii
             ______________________

             register, or (3) move from memory to memory.



             MOVS moves a byte (or a word) from DS:[si] to ES:[di], and
             increments (or decrements) SI and DI depending on the setting of
             DF, the direction flag (by 1 for bytes and by 2 for words). You
             may use CS:[si], SS:[si] or ES:[si], but you MAY NOT OVERRIDE
             ES:[di].

                 movsb
                 movsw
                 movs BYTE PTR ES:[di], SS:[si]     ;or CS, DS, ES:[si]
                 movs WORD PTR ES:[di], SS:[si]     ;or CS, DS, ES:[si]



             MUL performs unsigned integer multiplication. The multiplicand
             must be in AX (or AL for bytes). After the multiplication, the
             result is in DX:AX (or AH:AX for bytes). If DX (or AH for bytes)
             contains significant information, then CF = 1. If all the
             significant information is in AX (or AL for bytes) then CF = 0.
             Multiplication by a constant is not allowed. The MUL instruction
             does not mention AX (or AL). It is understood.

                 mul  reg/mem



             NEG performs '0 - number' on a number and sets the flags
             accordingly.

                 neg  reg/mem



             NOP (no operation) does absolutely nothing. It can fill up space
             which was previously occupied by a different instruction.



             NOT performs bitwise logical NOT on a word or a byte.

                 not  reg/mem



             OR performs bitwise logical OR on a byte or word

                 or   reg/mem, reg/mem
                 or   reg/mem, constant



             OUT moves a byte (or word) from AL (or AX) to the named port.
             There are two forms:






             Appendix II - The 8086 Instruction Set                      xxiii
             ______________________________________

                 out  port_number, ax
                 out  dx, ax

             where 'port_number' is a CONSTANT which is coded into the machine
             code. The constant may be from 0-255. DX (and it must be DX) may
             hold a port number from 0-65535.



             POP pops a WORD off the stack. Technically, POP takes the word at
             SS:SP and puts it into the named register or memory location,
             then ADDS 2 to SP.

                 pop  mem/reg
                 pop  segreg



             POPF pops a WORD off the top of the stack into the flags
             register. Its technical operation is the same as for POP. 



             PUSH pushes a WORD on the stack from the named register or memory
             location. Technically, PUSH subtracts 2 from SP, then moves the
             word to SS:SP.

                 push reg/mem
                 push segreg



             PUSHF pushes the flags register on the stack. Its technical
             operation is the same as for PUSH.



             RCR (rotate through carry right) and RCL (rotate through carry
             left) rotate the bits of a register or of memory data right and
             left respectively. The bit which is shoved off the register (or
             data) is placed in CF and CF is placed on the other side of the
             register (or data). There are two fixed forms. (1) rotate 1 bit
             and (2) rotate by the number in CL.

                 rcr  reg/mem, 1
                 rcl  reg/mem, cl



             REP. The string instructions may be prefixed by REP/REPE/REPNE
             which will repeat the instructions according to the following
             conditions:

                 rep       decrement cx ; repeat if cx is not zero
                 repe      decrement cx ; repeat if cx not zero AND zf = 1
                 repz      decrement cx ; repeat if cx not zero AND zf = 1
                 repne     decrement cx ; repeat if cx not zero AND zf = 0





             The PC Assembler Tutor                                       xxiv
             ______________________

                 repnz     decrement cx ; repeat if cx not zero AND zf = 0

             Here, 'e' stands for equal, 'z' is zero and 'n' is not. These
             repeat instructions should NEVER be used with a segment override,
             since the 8086 will forget the override if a hardware interrupt
             occurs in the middle of the REP loop. 

                 rep    movsb
                 repe   scasb
                 repne  cmpsw



             RET returns from the subroutine to the calling program. The
             return will be either NEAR or FAR depending on the type of
             procedure it is in. It may take the parameters off the stack (for
             Pascal) or leave them on the stack (for C).

                 ret (6)        ; Pascal - take 6 bytes off the stack
                 ret            ; C - do nothing



             ROR (rotate right) and ROL (rotate left) rotate the bits of a
             register or memory data right and left respectively. The bit
             which is shoved off one end is moved to the other end. CF
             indicates whether the last bit moved from one end to the other
             was a 1 or a 0. There are two fixed forms. (1) rotate 1 bit and
             (2) rotate by the number in CL.

                 ror  reg/mem, 1
                 rol  reg/mem, cl



             SAHF (store AH into flags) puts AH into the low byte of the flags
             register.



             SAL (shift arithmetic left) and SHL (shift logical left) are
             exactly the same instruction. They move bits left. 0s are placed
             in the low bit. Bits are shoved off the register or memory data
             on the left side, and CF indicates whether the last bit shoved
             off was a 1 or a 0. It is used for multiplying an unsigned number
             by powers of 2. There are two fixed forms. (1) shift 1 bit and
             (2) shift by the number in CL.

                 shl  reg/mem, 1
                 sal  reg/mem, cl



             SAR (shift arithmetic right) shifts bits right. The high (sign)
             bit stays the same throughout the operation. Bits are shoved off
             the register or memory location on the right side. CF indicates
             whether the last bit shoved off was a 1 or a 0. It is used (with





             Appendix II - The 8086 Instruction Set                        xxv
             ______________________________________

             difficulty) for dividing a signed number by powers of 2. There
             are two fixed forms. (1) shift 1 bit and (2) shift by the number
             in CL.

                 sar  reg/mem, 1
                 sar  reg/mem, cl



             SBB (subtract with borrow) subtracts one integer from another and
             then subtracts 1 more if CF is set. It works with both signed and
             unsigned numbers and is used for multiple word arithmetic.

                 sbb  reg/mem, reg/mem
                 sbb  reg/mem, constant



             SCAS compares AL (or AX) to the byte (or word) pointed to by
             ES:[di], and increments (or decrements) DI depending on the
             setting of DF, the direction flag (by 1 for bytes and by 2 for
             words).  NO OVERRIDES ARE ALLOWED.

                 scasb
                 scasw
                 scas BYTE PTR ES:[di]    ; no override allowed
                 scas WORD PTR ES:[di]    ; no override allowed



             SHR (shift logical right) does the same thing as SHL but in the
             opposite direction. Bits are shifted right. 0s are placed in the
             high bit. Bits are shoved off the register or memory location on
             the right side and CF indicates whether the last bit shoved off
             was a 0 or a 1. It is used for dividing an unsigned number by
             powers of 2. There are two fixed forms. (1) shift 1 bit and (2)
             shift by the number in CL.

                 shr  reg/mem, 1
                 shr  reg/mem, cl



             STC sets the carry flag (CF = 1).

             STD sets the direction flag (DF = 1, which decrements).

             STI sets the interrupt flag (IEF = 1; interrupts enabled).



             STOS (store to string) moves a byte (or a word) from AL (or AX)
             to ES:[di], and increments (or decrements) DI depending on the
             setting of DF, the direction flag (by 1 for bytes and by 2 for
             words). NO SEGMENT OVERRIDES ARE ALLOWED.

                 stosb





             The PC Assembler Tutor                                       xxvi
             ______________________

                 stosw
                 stos BYTE PTR ES:[di]    ; no override allowed
                 stos WORD PTR ES:[di]    ; no override allowed




             SUB subtracts one integer from another. It works for both signed
             and unsigned numbers.

                 sub  reg/mem, reg/mem
                 sub  reg/mem, constant



             TEST performs logical AND, but does not alter the value of the
             "destination" variable. Its purpose is to set the flags for
             conditional jumps.

                 test reg/mem, reg/mem
                 test reg/mem, constant



             WAIT forces the 8086 to wait until the coprocessor is finished
             with its instruction before the 8086 can go on to the next
             instruction.



             XCHG exchanges the values in two registers or memory locations.

                 xchg reg/mem, reg/mem



             XLAT. If BX contains the address of a 256 byte translation table,
             then XLAT goes to (BX + AL), takes the byte there and puts it
             into AL. DS is the normal segment, but segment overrides are
             allowed.



             XOR performs logical exclusive OR on two numbers.

                 xor  reg/mem, reg/mem
                 xor  reg/mem, constant