68

                                   CHAPTER 9 - JUMPS

             So far we have done almost exclusively sequential programming -
             the order of execution has been from one instruction to the next
             until the very end, where the jump instruction has brought us
             back to the top. This is not the normal way programs work. In
             order to have things like DO loops, FOR loops, WHILE loops, CASE
             constructions and IF-THEN-ELSE constructs, we need to make
             decisions and to be able to go to different blocks of code
             depending on our decisions.

             Intel has provided a wealth of conditional jumps to answer all
             our needs. All of them are listed in a summary at the end of this
             chapter.

             The thing we will do most often is compare the size of two
             numbers. In BASIC code:

                 IF   A < B  THEN

             we need to see if A < B . If that is true, we do one thing, if it
             is false, we do something else. One thing that we need to watch
             out for is whether A and B are signed or unsigned numbers. Let A
             = F523h (signed -2781; unsigned 62755) and B = 59E0h (signed
             +23008; unsigned 23008). If A and B are signed numbers, then A <
             B. However, if they are unsigned numbers, then  A > B. In C and
             PASCAL, the compiler takes care of whether you want signed or
             unsigned numbers (BASIC assumes that it is always signed
             numbers). You are now on the machine level, and must take care of
             this yourself. 

             To compare two numbers, you subtract one from the other, and then
             evaluate the result (less than 0,  0, or more than 0). To compare
             A and B, you do A minus B. To compare AX and BX, you can:

                 sub  ax, bx

             and then evaluate it. Unfortunately, if you do that, you will
             destroy the information in AX. It will have been changed in the
             process. Intel has solved this problem with the CMP (compare)
             instruction. 

                 cmp  ax, bx

             subtracts BX from AX, sets the flags, and throws the answer away.
             CMP is exactly the same as SUB except that AX remains unchanged.
             We probably don't want to save the result anyway. If we do, we
             can always use:

                 sub  ax, bx

             We have subtracted BX from AX. There are now three possibilities.
             (1) AX > BX so the answer is positive, (2) AX = BX so the answer
             is zero, or (3) AX < BX so the answer is negative. But are these

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             Chapter 9 - Jumps                                              69
             _________________

             signed or unsigned numbers? The 8086 uses the same subtract (or
             CMP) instruction for both signed or unsigned numbers. You have to
             tell the 8086 in the following instruction whether you were
             talking about signed or unsigned numbers.

                 cmp  ax, bx
                 ja   some_label

             asks the machine to compare AX and BX. It then says that AX and
             BX were UNSIGNED numbers and the machine should jump to
             "some_label" if AX was above BX.

                 cmp  ax, bx
                 jg   some_label

             asks the machine to compare AX and BX. It then says that AX and
             BX were SIGNED numbers and the machine should jump to
             "some_label" if AX was greater than BX.

             The 8086 makes the decision by looking at the flags. They give it
             complete information about the result. (The decision making rules
             are in the summary).

             In our example on the previous page, we had A = -2781 (unsigned
             62755) and B = +23008 (unsigned 23008). If we put A in AX and B
             in BX, then the instruction JA will execute the jump, while the
             instruction JG will not execute the jump. What happens if the
             8086 doesn't execute the jump? It goes on to the next
             instruction.

             As I said before, the 8086 has LOTS of conditional jumps. I am
             going to give you a list of them now, but be forewarned that the
             mnemonics for these suckers are confusing. Rather than doing
             something sensible like JUG for 'jump unsigned greater' and JSG
             for 'jump signed greater' - things that would be easy to
             distinguish, they have JA for 'jump above' (unsigned) and JG for
             'jump greater' (signed).{1}  Therefore, use the summary at the
             end of the chapter. With enough use, you will remember which is
             which. 

             The arithmetic jump instructions have two forms, a positive one
             and a negative one. For instance:

                 ja        ; jump above
                 jnbe      ; jump not (below or equal)

             are actually the same machine instruction. You use whichever one
             makes the program clearer. We will have examples later to
             illustrate both positive and negative mnemonics. Here are the
             signed and unsigned instructions and their meaning. The
             ____________________

                1 This wierd use of the words above and greater, below and
             less, is so confusing that my copy of the Microsoft assembler
             manual v5.1 has it reversed on one page. It calls the signed
             jumps unsigned and the unsigned jumps signed. And that's the one
             place where it SHOULD be right.





             The PC Assembler Tutor                                         70
             ______________________

             equivalent mnemonics will appear in pairs.

             THESE ARE THE SIGNED JUMP INSTRUCTIONS

                 jg        ; jump if greater
                 jnle      ; jump if not (less or equal){2}

                 jl        ; jump if less
                 jnge      ; jump if not (greater or equal)

                 je        ; jump if equal
                 jz        ; jump if zero 

                 jge       ; jump if greater or equal
                 jnl       ; jump if not less

                 jle       ; jump if less or equal
                 jng       ; jump if not greater

                 jne       ; jump if not equal
                 jnz       ; jump if not zero 

             These are self-explainatory, keeping in mind that these apply
             only to signed numbers.


             THESE ARE THE UNSIGNED JUMP INSTRUCTIONS

                 ja        ; jump if above
                 jnbe      ; jump if not (below or equal) 

                 jb        ; jump if below
                 jnae      ; jump if not (above or equal) 

                 je        ; jump if equal
                 jz        ; jump if zero 

                 jae       ; jump if above or equal
                 jnb       ; jump if not below 

                 jbe       ; jump if below or equal
                 jna       ; jump if not above

                 jne       ; jump if not equal
                 jnz       ; jump if not zero 

             These apply to unsigned numbers, and should be clear. 

             JZ, JNZ, JE and JNE work for both signed and unsigned numbers.
             After all, zero is zero.
             ____________________

                2 I was trying to decide whether or not to put in the
             parentheses. If there are two things after the "not" the "not"
             applies to both of them. By the rules of logic, not (less or
             equal) == not less AND not equal. If you don't understand this,
             try to find someone who can explain it to you. 





             Chapter 9 - Jumps                                              71
             _________________


             Before we get going, there is one more thing you need to know.
             The unconditional jump:

                 jmp  some_label

             can jump anywhere in the current code segment. XXXX is the
             current number in CS, then jmp can go from XXXX offset 0 to XXXX
             offset 65535.

             Conditional jumps are something else entirely. ALL conditional
             jumps (including the loop instruction) are limited range jumps.
             They are from -128 to +127. That is, they can go backward up to
             128 bytes and they can go forward up to 127 bytes.{3} You will
             find that you will get assembler errors because the conditional
             jumps are too far away, but don't worry because we can ALWAYS fix
             them. You will find out later how to deal with them. 


             As in the other arithmetic instructions, there are five forms of
             the CMP instruction.

                 1.   compare two registers
                 2.   compare a register with a variable
                 3.   compare a variable with a register
                 4.   compare a register with a constant
                 5.   compare a variable with a constant

             These look like:

                 cmp  ah, dl
                 cmp  si, memory_data
                 cmp  memory_data, ax
                 cmp  ch, 127
                 cmp  memory_data, 14938


             Here are some decisions we might have to make in programs. 

             (1) We are writing a program to print hex numbers on the screen.
             We have one routine for 0 - 9 and a different one for A - F.
             Sound familiar?

                 cmp  al, 10
                 jb   decimal_routine
                 ; here we are past the jump, so we can start the  A - F
                 ; routine.

             (2) We want to fire everyone over the age of 55 (this is an
             unsigned number since there are no negative ages):
             ____________________

                3 But they don't jump from the beginning of the machine
             instruction, they jump from the END of the machine instruction
             (which is two bytes long). This means that they have an effective
             range of from -126 bytes to +129 bytes from the BEGINNING of the
             instruction.





             The PC Assembler Tutor                                         72
             ______________________


                 cmp  employee_age, 55
                 ja   find_a_reason_for_termination
                 ; start of routine for younger employees here.

             (3) You want to know if you need to go to a loanshark:

                 mov  di, bank_balance
                 cmp  unpaid_bills, di
                 jg   gotta_go_see_Vinnie
                 ; continue normal routine here

             (4) Notice that the last one could have also been written:

                 mov  di, bank_balance
                 cmp  di, unpaid_bills
                 jl   gotta_go_see_Vinnie
                 ; continue normal routine

             though to my eye the first one seems clearer.

             (5) You have the results from two calculations, the first one in
             DI and the second one in CX. You need to go to different routines
             depending on which is larger. If they are the same, you exit:

                 cmp  di, cx
                 jg   routine_one         ; di is greater
                 jl   routine_two         ; cx is greater
                 jmp  exit_label          ; they are equal

             We had two conditional jumps in a row and both of them were able
             to look at the results of the CMP instruction because the first
             jump (JG) did not change any of the flags. This is true of all
             jumps - conditional jumps, the unconditional jump, and LOOP. They
             never change any of the flags, so you can have two jumps in a row
             and be certain that the flags will not be altered.


             (6) Your dad has promised to buy you a Corvette if you don't get
             suspended from school more than three times this semester. Here's
             his decision code:

                 cmp  number_of_suspensions, 3
                 jng  buy_him_the_corvette
                 ; better luck next time



             JUMP OUT OF RANGE

             If the code you are jumping to is more than -128 or +127 bytes
             from the end of a conditional jump, you will get an assembler
             error that the jump is out of range. This can always be fixed.
             Take this code:






             Chapter 9 - Jumps                                              73
             _________________

                      cmp  ax, bx
                      jg   destination_label
                 further_code:
                      ; continue the program 

             If 'destination_label' is out of range, what you need to do is
             jump to 'further_code' with a conditional jump (you are within
             range of 'further_code') and use JMP (which can go anywhere in
             the segment) to go to 'destination_label'. To switch the jump,
             you simply negate the jump condition:

                 jg   ->   jng
                 je   ->   jne
                 jne  ->   je
                 jbe  ->   jnbe

             We use reverse logic. Originally, if the condition was met we
             jumped. If the condition was not met we continued. Now, if the
             condition is NOT met, we jump, and if the condition is NOT not
             met (yes, there are two NOTs) which means it was met, we
             continue, and this sends us to the JMP instruction. Make sure you
             believe this works correctly before going on. The code then looks
             like this:

                      cmp  ax, bx
                      jng  further_code
                      jmp  destination_label
                 further_code:
                      ; continue the program

             This is the standard way of handling the situation.































             The PC Assembler Tutor                                         74
             ______________________

                                        SUMMARY

             CMP
                 CMP performs the same operation as subtraction, but it does
             not change the registers or variables, it only sets the flags. It
             is the cousin of TEST. As usual, there are five possibilities:

                 1.   compare two registers
                 2.   compare a register with a variable
                 3.   compare a variable with a register
                 4.   compare a register with a constant
                 5.   compare a variable with a constant


             THESE ARE THE SIGNED JUMP INSTRUCTIONS

                 jg        ; jump if greater
                 jnle      ; jump if not (less or equal) 

                 jl        ; jump if less
                 jnge      ; jump if not (greater or equal) 

                 je        ; jump if equal
                 jz        ; jump if zero 

                 jge       ; jump if greater or equal
                 jnl       ; jump if not less

                 jle       ; jump if less or equal
                 jng       ; jump if not greater

                 jne       ; jump if not equal
                 jnz       ; jump if not zero 



             THESE ARE THE UNSIGNED JUMP INSTRUCTIONS

                 ja        ; jump if above
                 jnbe      ; jump if not (below or equal) 

                 jb        ; jump if below
                 jnae      ; jump if not (above or equal) 

                 je        ; jump if equal
                 jz        ; jump if zero 

                 jae       ; jump if above or equal
                 jnb       ; jump if not below 

                 jbe       ; jump if below or equal
                 jna       ; jump if not above

                 jne       ; jump if not equal
                 jnz       ; jump if not zero 







             Chapter 9 - Jumps                                              75
             _________________

             THESE JUMPS CHECK A SINGLE FLAG 

             These come in opposite pairs

                 jc        ; jump if the carry flag is set
                 jnc       ; jump if the carry flag is not set

                 jo        ; jump if the overflow flag is set
                 jno       ; jump if the overflow flag is not set

                 jp or jpe ; jump if parity flag is set (parity is even)
                 jnp or jpo  ;jump if parity flag is not set (parity is odd)


                 js        ; jump if the sign flag is set (negative )
                 jns       ; jump if the sign flag is not set (positive or 0)


             THIS CHECKS THE CX REGISTER

                 jcxz      ; jump if cx is zero

             Why do we have this instruction? Remember, the loop instruction
             decrements CX and then checks for 0. If you enter a loop with CX
             set to zero, the loop will repeat 65536 times. Therefore, if you
             don't know what the value of CX will be when you enter the loop,
             you use this instruction just before the loop to skip the loop if
             CX is zero:

                      jcxz after_the_loop

                 loop_start:
                           .
                           .
                           .
                           .
                      loop loop_start
                 after_the_loop:


             INFORMATION ABOUT JUMPS

             The unconditional jump (JMP) can go anywhere in the code segment.
             All other jumps, which are conditional, can only go from -128 to
             +127 bytes from the END of the jump instruction (that's from -126
             to +129 bytes from the beginning of the instruction).

             Jumps have no effect on the 8086 flags.

             How does the 8086 decide whether something is more, less, or the
             same? The rules for unsigned numbers are easy. If you subtract a
             larger number from a smaller, the subtraction will pass through
             zero and will set the carry flag (CF). If they are the same, the
             result will be zero and it will set the zero flag (ZF). If the
             first number is larger, the machine will clear the carry flag and
             the zero flag will be cleared (ZF = 0). Therefore, for unsigned
             numbers, we have:





             The PC Assembler Tutor                                         76
             ______________________


             First number is:
                 above          CF = 0    ZF = 0
                 equal          CF = 0    ZF = 1
                 not equal      CF = ?    ZF = 0
                 below          CF = 1    ZF = 0

             All other unsigned compares are combinations of those three
             things:

                 jae  = ja OR je     (CF = 0 and ZF = 0) or ZF = 1
                 jbe  = jb OR je     CF = 1 or ZF = 1

             When you have a negative condition, it is much easier to look at
             its equivalent positive condition to figure out what is going on:

                 jnae   is the same as    jb   CF = 1
                 jnbe   is the same as    ja   CF = 0    ZF = 0


             SIGNED NUMBERS

             This section is not for the fainthearted. It is not necessary, so
             if you find yourself getting confused, just remember that if you
             see documentation talking about a jump where the overflow flag
             equals the sign flag or the overflow flag doesn't equal the sign
             flag, it is talking about SIGNED numbers.

             Zero is zero, so we won't concern ourselves with it here. It is
             exactly the same.

             If A and B are two signed word sized numbers and we have:

                 cmp  A, B

             then we can have four different cases:

                 1) If A is just a little greater than B  [(A - B) <=
                 +32767],  then the result will be a small positive number,
                 and there will be no overflow. SF = 0, OF = 0.

                 2) If A is much greater than B [+32767 < (A - B)], then the
                 result will be too positive and it will overflow from
                 positive to negative. This will set both the sign flag (it
                 is now negative) and the overflow flag. SF = 1, OF = 1.

                 3) If A is a little less than B [-32768 <= (A - B)], that is
                 if it is only a little negative, then the result is a small
                 negative number, and there is no overflow. SF = 1, OF = 0.

                 4) If A is much less than B [(A - B) < -32768], then the
                 result is a large negative number. It is too negative and
                 overflows into a positive number. SF = 0, OF = 1.

             Recapping, for a positive result:

                 1) SF = 0, OF = 0





             Chapter 9 - Jumps                                              77
             _________________

                 2) SF = 1, OF = 1

             and for a negative result:

                 3) SF = 1, OF = 0
                 4) SF = 0, OF = 1

             For positive results (and zero), SF = OF. For negative results,
             SF is not equal to OF. This, in fact, is how the 8086 decides a
             signed jump. If SF = OF, it's positive, if SF is not equal to OF,
             it's negative. If ZF = 1, then obviously they are equal. Here is
             the list:

                 greater        SF = OF   ZF = 0
                 equal          SF = OF   ZF = 1
                 not equal                ZF = 0
                 less           SF is not equal to OF

             As with the unsigned numbers, if you have a negative condition,
             it is easier to change it into its equivalent positive condition
             and then figure out the requirements. For instance:

                 jnge      same as   jl   SF is not equal to OF
                 jnl       same as   jge  ( SF = OF and ZF = 0 ) or ( ZF = 1)

             If you think about it, this OF = SF stuff does make sense. We are
             subtracting two numbers. If the first one is greater, then the
             answer will be positive. It can either be a little positive as in
             (cmp 0, -1 ) = 1 or it can be very positive, as in (cmp 32767,
             -32768) = 65,535 (same as -1). If it is just a little positive,
             there is no overflow and it has a positive sign (SF = 0, OF = 0).
             If the difference gets large, then the number overflows from + to
             -. At that point OF = 1, but it now has a negative sign, so OF =
             SF. The flags MUST match.

             In the opposite case where the second number is greater, The
             answer is negative. It can either be a little negative as in (cmp
             12, 13)= -1, or it can be very negative (cmp -32768, 32767) =
             -65535 =1. If it is a small difference, the sign is negative, but
             there is no overflow (SF = 1, OF = 0). As the difference gets
             larger, the number overflows from negative to positive so the
             sign flag is now positive, but the overflow flag is set (SF = 0,
             OF = 1). Those flags CAN'T match.