134

                                 CHAPTER 14 - ZOOM


             There are only a couple of reasons for working at the assembler
             level. Perhaps you're curious about how the PC functions at the
             machine level. Maybe you want to optimize a time consuming
             section of code. Maybe you want to work easily with the DOS
             function calls and the BIOS calls (which will be introduced in a
             later chapter). Or maybe you want raw speed. 

             Every time that I enter:

                 >dir /w

             and watch DOS meander its way down the screen at a leisurely
             pace, I think "Can't the computer go any faster?"  Let's find
             out. This is going to be a short chapter. Make a copy of
             template.asm, and we'll call it zoom.asm. This is going to
             overwrite the entire screen 200 times.{1} 

             Before we write to the screen, we need to know where the screen
             is. When IBM designed the structure of the PC, they decided to
             put the memory for the monochrome card in one place and the
             memory for the color card in another place - apparently they
             thought you might want to have both a color monitor and a
             monochrome monitor running at the same time. The color monitor is
             in segment 0B800 at offset 0, and the monochrome monitor is in
             segment 0B000 at offset 0. We need to put the correct number into
             the program, so you need to know whether you have a color card or
             a monochrome card. If one segment number doesn't work, you can
             try the other.

             TEMPLATE.ASM 
             ; - - - - - - - - - -  START CODE BELOW THIS LINE
                    call  show_regs_and_wait  ; {2}
                                              ; we are about to start 
                                              ; this marks the time

                    mov   ax, 0B800h       ; color seg. 0B000h is mono seg
                    mov   es, ax           ; es is at video card segment
                    mov   cx, 2            ; do this whole thing twice
             outer_loop:
             ____________________

                1 It is now time for you to go out and get a book about the
             internal structure and i/o interface of the PC. One good book is
             "The Peter Norton Programmer's Guide To The IBM PC", by guess
             who? It is clearly written and a good introduction. Another
             quality book is "DOS Programmer's Reference" by Terry Dettmann.
             It is very systematically laid out and is more techie oriented.

                2 We need to initialize the video card to make sure it is in
             the right place. This is the easiest way. The registers
             themselves mean nothing to us.

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             Chapter 14 - Zoom                                             135
             _________________

                    push  cx               ; save for outer loop instruction
                    mov   cx, 100          ; 100 repeats ; zoom_loop count
                    mov   al, '0'          ; 100 characters starting at '0' 
                    mov   ah, 07h          ; black background, white letters 
              
             zoom_loop:    ; draw the screen 100 times 
                    push  cx 
                    mov   cx, 2000         ; 80 X 25 screen is 2000 words long
                    mov   si, 0            ; start at offset 0000. 
              
             inner_loop:    ; inner loop - fill the screen - 2000 words
                    mov   es:[si], ax 
                    add   si, 2 
                    loop  inner_loop 
              
                    inc   al               ; next higher ASCII character  
                    pop   cx               ; zoom_loop count
                    loop  zoom_loop 

                    pop   cx               ; outer_loop count
                    loop  outer_loop

                    call  get_continue     ; finished - this is for timing 
             ; - - - - - - - - - - END CODE ABOVE THIS LINE


             Show_regs_and_wait resets the video card, so we use it to make
             sure the video memory is set at offset 0000. It then waits for
             ENTER. At the end, get_continue waits for ENTER.{3} This way you
             can mark the beginning and the end in order to time it. We set
             the ES segment to the video segment. This is different depending
             on whether you have a monochrome card or a color card. The
             monochrome segment is at 0B000h and the color card is at 0B800h.
             You need to know which kind of card you have so you can put the
             right number into ES via AX. 

             Since the normal segment for SI is the DS segment, we need to put
             in a segment override to use SI with the ES segment.

             We start with the ASCII character '0' and then do the next 99
             characters in increasing ASCII sequence. Technically, ASCII
             characters end at 127, but the PC extended characters go up to
             255, so we will start with ASCII 48d and end with ASCII 147d. The
             zoom_loop changes the character 100 different times, and the
             inner_loop fills the screen. That 07h in AH means that we will
             have white characters on a black background. The outer loop has a
             count of 2. This should be adjusted. If you have a medium speed
             machine make it 4 (400 screen fills) and if you have a high speed
             machine make it 8 (800 screen fills).

             ____________________

                3 That is its mission in life. It is there so that you can
             time blocks of code. If you want to find out how long some code
             takes, repeat it 10,000  (or whatever is appropriate) times and
             put  get_continue in front of it and behind it. That way you can
             control the start and mark the finish.





             The PC Assembler Tutor                                        136
             ______________________

             When this is done, the screen will be filled with characters so
             you will need to use the DOS command

                 > cls

             to clear the screen for anything else.

             When it is all assembled and linked, get a cup of coffee and a
             wristwatch with a second hand and we'll time it. Divide by 200
             (or 400 or 800) to find out how long it takes to fill one screen.
             If the characters are not on your screen, you probably have the
             wrong segment address for your video card, so try the other one.
             Are you ready to time it? Then ready, set, go.

             Hmmm. On my machine 200 repeats takes about 4 seconds, while the
             dir command takes about 1 second for one screen. That means that
             zoom.asm is about 50 times faster. That's the difference between
             someone running a 4 minute mile and someone running a 3hr. 20min.
             mile. This is one of the reasons people like to work at the
             assembler level.