Chapter  7

                     Fixed Disk Service (INT 13H)
                     ----------------------------
      
     1.      Introduction
      
      
             1.1     Disk Controller Basic Function
      
             1.2     Standard Disk Interface 
      
                     A.      ST-506/412 Winchester
                     B.      Enhanced Small Device Interface (ESDI)
                     C.      Storage Module Device (SMD)
                     D.      Enhanced SMD
                     E.      Small Computer Systems Interface (SCSI)
                     F.      Intelligent Peripheral Interface (IPI)
                     G.      AT-Bus
      
             1.3     Coding
      
                     A.      Frequency Modulation (FM)
                     B.      Modified Frequency Modulation (MFM)
                     C.      Run Length Limited (RLL)
                     D.      Group Code Recording (GCR)
                     E.      Zone Bit Recording (ZBR)*
      
             1.4     Data Format
      
             1.5     Sector Interleaving
      
             1.6     Disk Formatting
      
                     A.      Physical Format
                     B.      Partitioning
                     C.      Logical Format
      
             1.7     Translative Versus Non-Translative Mode
      
      
     2.      Winchester Disk Controller
      
             2.1     System Configuration for Fixed Disk System

	     2.2     I/O Port Definition

	     2.3     Timing Consideration
      
     3.      Programming Sequence in Fixed Disk Service Program
      
     4.	     SPEC

     5.      Q & A
      
      





     1.1     Basic Function of a Disk Controller

      
             1.      Write data to the disk
             
             2.      Read data from the disk
      
             3.      Serialize and de-serialize data
      
             4.      Control the disk drive (option)
      
             5.      Ensure data integrity
      
             6.      Provide reasonable system interface (option)
      
             7.      Buffer data to/from disk
      
      
      





     1.2     Disk Interface Standard
      
      
      
               ³
         High  ³
               ³
               ³
               ³                                                  . IPI
               ³
               ³                   . SMD           . ESMD
               ³
               ³                                           . SCSI
      COST     ³                                . ESDI
               ³
               ³
               ³
               ³                     . ST-412HP
               ³
               ³          . ST-506/412        . AT Bus
               ³
         Low   ³   . 3.5 Floppy
               ³
               ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ>
                 Low                                            High
                                PERFORMANCE
      
             Fig 1 :    Fixed Disk Interface Versus Market
      
      
     A.      ST-506 412 Winchester Interface
      
      
             1.      Industry standard since 1981
      
             2.      Low capacity Winchester (5 - 150 Mbytes)
      
             3.      small size
      
             4.      Serial data transfer rate of 5 Mbits/second
      
             5.      Cost (not performance) oriented
      
             6.      Simple disk interface (most of the effort is in the 
                     disk controller)




      
     B.      Enhanced Small Device Interface (ESDI)
      
             
             1.      Substantial upgrade to ST-506/412 interface
      
             2.      Oriented towards high-capacity, high speed small
                     winchester
      
             3.      Capable of handling magnetic tapes and optical disks
      
             4.      Serial transfer rate 10 Mbits/second
      
             5.      Simpler controller
      
      
     C.      Storage Module Device (SMD)
      
     D.      Enhanced SMD
      
     E.      Small Computer Systems Interface(SCSI)
      
      
             1.      ANSI defined intelligent, low-cost peripheral interface
      
             2.      Derived from SASI (Shgart Assoc. Systems Interface)
      
             3.      8-bit parallel data transfer, 1.5 to 4 Mbytes/second
      
             4.      Provides device independent software
      
             5.      Function more as a computer interface than a disk 
                     interface
      
             6.      Requires lots of intelligence in the peripheral
             
      
     F.      Intelligent Peripheral Interface (IPI)
      
     G.      AT-Bus
      
      
             1.      Cost dowm
      
             2.      Data transfer rate
      
             3.      One I/O slot for another add-on card
      
             4.      The fixed disk controller is no longer required




      
     1.3     Coding
      
             The following are four different ways of improving the storage
             capacity of disk drives:
             
                 1)  Add more platters
                 2)  Add more tracks per platter
                 3)  Increase BPI (bit per inch)
                 4)  Use better encoding methods
             
             For method 1, it will increase manufacture cost for extra
             platter and extra read/write head set.
      
             For method 2, it will increase control logic complexity for 
             write current precompensation and interfere.
      
             For method 3, it will use better read/write to shorten 
             the length between read/write head and platter.
      
             For method 4, it will increase the encoding/decoding complexity.
      
      
     A.      Frequency Modulation (FM)
      
    
                               1 bit cell
                                ³<----->³
                ÚÄÄÄÄÄÄÄ¿       ÚÄÄÄÄÄÄÄ¿                       ÚÄÄÄÄÄÄÄ¿
                ³   1   ³   0   ³   1   ³    0       0       0  ³   1   ³  0
  NRZ Data    ÄÄÙ       ÀÄÄÄÄÄÄÄÙ       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ       ÀÄÄÄ
   
   
                 c   d   c       c   d   c       c       c       c   d   c
                ÚÄ¿ ÚÄ¿ ÚÄ¿     ÚÄ¿ ÚÄ¿ ÚÄ¿     ÚÄ¿     ÚÄ¿     ÚÄ¿ ÚÄ¿ ÚÄ¿
                ³ ³ ³ ³ ³ ³     ³ ³ ³ ³ ³ ³     ³ ³     ³ ³     ³ ³ ³ ³ ³ ³
  FM Data     ÄÄÙ ÀÄÙ ÀÄÙ ÀÄÄÄÄÄÙ ÀÄÙ ÀÄÙ ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÙ ÀÄÙ ÀÄÙ ÀÄ
   
   
   
                ÚÄÄÄ¿   ÚÄÄÄÄÄÄÄ¿   ÚÄÄÄ¿       ÚÄÄÄÄÄÄÄ¿       ÚÄÄÄ¿   ÚÄÄÄ
  Disk Flux     ³   ³   ³       ³   ³   ³       ³       ³       ³   ³   ³
  Transitions ÄÄÙ   ÀÄÄÄÙ       ÀÄÄÄÙ   ÀÄÄÄÄÄÄÄÙ       ÀÄÄÄÄÄÄÄÙ   ÀÄÄÄÙ  
    


     FM Encoding Rules:
    
       1.      Insert clock pulse for each bit cell
       2.      Insert data pulse when NRZ data is "1"




      
     B.      Modified Frequency Modulation(MFM)
      
      
                               1 bit cell
                                ³<----->³
                ÚÄÄÄÄÄÄÄ¿       ÚÄÄÄÄÄÄÄ¿                       ÚÄÄÄÄÄÄÄ¿
                ³   1   ³   0   ³   1   ³    0       0       0  ³   1   ³  0
  NRZ Data    ÄÄÙ       ÀÄÄÄÄÄÄÄÙ       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ       ÀÄÄÄÄ
   
                                                ÚÄ¿     ÚÄ¿
                                                ³ ³     ³ ³
  Clock       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   
                    ÚÄ¿             ÚÄ¿                             ÚÄ¿
                    ³ ³             ³ ³                             ³ ³
  Data        ÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄ
   
                     d               d           c       c           d    
                    ÚÄ¿             ÚÄ¿         ÚÄ¿     ÚÄ¿         ÚÄ¿    
                    ³ ³             ³ ³         ³ ³     ³ ³         ³ ³    
  MFM Data    ÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÙ ÀÄÄ
   
   
                    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿           ÚÄÄÄÄÄÄÄ¿           ÚÄÄÄÄ
  Disk Flux         ³               ³           ³       ³           ³      
  Transitions ÄÄÄÄÄÄÙ               ÀÄÄÄÄÄÄÄÄÄÄÄÙ       ÀÄÄÄÄÄÄÄÄÄÄÄÙ      
    
   
   
     MFM Encoding Rules :
   
          1. Insert clock in pulse at the beginning of a bit cell only
             if NRZ data = 0 for two consecutive bits.
          2.  If data bit = 1, insert data pulse in the middle of the 
             bit cell.
          3. If data bit = 0, no insertion of data pulses in the bit 
              cell.
   
      




     C.      Run Length Limited (RLL)
      
      
             RLL 2,7 Encoding Rules:
      
             The following table shows encoding/decoding:
      
             ÚÄÄÄÄÄÄÄÄÄÂÄÄÄÄÂÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄ¿
             ³ NRZ Data³10  ³11  ³000   ³010   ³011     ³0010    ³0011    ³
             ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÅÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
             ³ RLL 2,7 ³1000³0100³100100³001000³000100  ³00001000³00100100³
             ÀÄÄÄÄÄÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÙ
      
      
     D.      Group Code Recording( GCR)
      
             4,5 GCR Encoding Rules :
      
             The following table shows encoding/decoding:
      
             ÚÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄ¿
             ³ NRZ Data³0000 ³000 1³0010 ³0011 ³0100 ³0101 ³0110 ³0111 ³
             ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
             ³ 4,5 GCR ³11001³11011³10010³10011³11101³10101³10110³10111³
             ÀÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÙ
      
             ÚÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄ¿
             ³ NRZ Data³1000 ³1001 ³1010 ³1011 ³1100 ³1101 ³1110 ³1111 ³
             ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
             ³ 4,5 GCR ³11010³01001³01010³01011³11110³01101³01110³01111³
             ÀÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÙ
      
      
      
     E.      Zone Bit Recording(ZBR)
      
             
             According to the track number, the fixed disk drive is divided 
             into several zones. The tracks in the same zone have the same 
             format, but the track in different zone may have different 
             format.
                     
      




     1.4     Data Format
      
      
          ÚÄ¿                                                          ÚÄ¿
          ³ ³                                                          ³ ³
   Index ÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄ
    
    
          ÚÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄ¿
          ³Index delay³Sector³Sector³    . . . .     ³Sector³Sector³Final³
          ³  Field    ³  0   ³  1   ³    . . . .     ³  N-1 ³  N   ³ Gap ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÙ
    
                      ³      ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÙ      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ÚÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÂÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³Preamble 1 ³Address³ I.D.   ³EDC³Postamble 1³Sector³Inter sector³
          ³(Synch 1)  ³ Mark  ³(Header)³ECC³           ³Data  ³     Gap    ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÁÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÙ
  
                              ³        ³               ³      ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ        ÀÄÄÄÄÄ¿         ³      ³
          ÚÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄ¿         ³      ³
          ³ID AM³Track³Track³Head³Sector³ ID ³         ³      ³
          ³     ³(MSD)³(LSD)³ #  ³  #   ³Flag³         ³      ³
          ÀÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÙ         ³      ³
                                                       ³      ³
                                                       ³      ³
                           ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ      ÀÄÄÄÄÄÄÄÄÄÄÄÄ¿
                           ÚÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄ¿
                           ³Preamble 2 ³Address³Data³ Data ³EDC³Postamble 2³
                           ³(Synch 2)  ³ Mark  ³Mark³Record³ECC³           ³
                           ÀÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÙ
  
    




    1.5     Sector Interleaving
      
            The initial formatting of a disk determines where sectors are
            located within a track. It is not necessary to allocate sectors
            sequentially around the track. The technique known as sector 
            interleaving optimizes access times when, although sectors are
            accessed sequentially, a small amount of processing must be 
            performed between sector read/write.
      
      
            interleave factor = 3
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
            interleave factor = 2
      
      
      
      
      
      
      
      
      
      
      
      
      
      




      
     1.6     Disk Formatting
      
      
             A.  Physical Format (initialization)
      
                 Initializes the fixed disk with sectors and addresses to
                 access data.
      
             B.  Partitioning
      
                 Assigns a partical amount of disk space to DOS.
      
             C.  Logical Format
      
                 Verifies that the initialization of the fixed disk drive 
                 was successfully completed.
      
      
     1.7     Translative Versus Non-Translative Mode
      
      
             Owing to the use of advanced technique, the new WDD contains 
             more cylinders, heads, and sectors per track. But due to DOS 
             limitation, some DOS  software can't access the extra disk 
             space. So some WDD manufacturer support "Translative mode" to 
             translate the extra disk space into DOS disk space.
      
             Example 1 :
      
             WDD have 1033 cylinders, 2 heads, 33  sectors/track in 
             non-translative mode, but it can have 1002 cylinders, 4 heads,
             and 17 sectors/track in translative mode.
      
               1033 * 2 * 33 = 68178 sectors/drive in non-translative mode
               1002 * 4 * 17 = 68136 sectors/drive in translative mode
      
             About 42 sectors in translative mode will be lost.
      





     2.1     System Configuration for Fixed Disk Subsystem
      


      
                       ÚÄÄÄÄÄÄÄÄ¿                                        
          ÚÄÄÄÄÄÄÄÄÄÄÄÄ´        ³<ÄÄÄÄÄÄÄÄÄÄÄ¿
          ³            ³ 8259A  ³            ³
          ³       ÚÄÄÄ>³        ³            ³                            
          ³       ³    ÀÄÄÄÄÄÄÄÄÙ            ³                 ÚÄÄÄÄÄÄÄÄ¿
          ³ ÚÄÄÄÄÄÁÄÄ¿                   ÚÄÄÄÁÄÄÄÄ¿      Ú---->³ WDD 0  ³
          ³ ³  CPU   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ>³        ³<ÄÄÄÄÄ|ÄÄÂÄ>³        ³
          ³ ³ INT 13H³<----Â-------------³  WDC   ³      |  ³  ÀÄÄÄÄÄÄÄÄÙ
          ³ ³ -------³     |             ³        ³<-----|  ³  ÚÄÄÄÄÄÄÄÄ¿
          À>³ INT 0EH³     |             ÀÄÄÄÄÄÄÄÄÙ      |  ÀÄ>³ WDD 1  ³
            ÀÄÄÄÄÄÄÄÄÙ     |                 ^           À---->³        ³
                           |                 |                 ÀÄÄÄÄÄÄÄÄÙ
                           |                 |                           
                       ÚÄÄÄÁÄÄÄÄ¿            |                           
                       ³ DRAM   ³<-----------Ù                           
                       ÀÄÄÄÄÄÄÄÄÙ                                          
      
      
              Command/Control  ÄÄÄÄÄÄÄÄ
      
              Data/Status      --------
      
      
       Fig :    System Configuration for Fixed Disk System
      
      





     2.2     I/O Port Definition


	     I/O Port Addr	  Read		       Write

	     1F0H/170H		  Data register	       Data register
	     1F1H/171H		  Error register       Write Precomp
	     1F2H/172H		  Sector Count         Sector Count
	     1F3H/173H		  Sector number	       Sector number
	     1F4H/174H		  Cylinder Low	       Cylinder Low
	     1F5H/175H		  Cylinder High	       Cylinder High
	     1F6H/176H		  Drive/Head(SDH)      Drive/Head(SDH)
	     1F7H/177H		  Status register      Command register
	     3F6H		  Alternate Status     Fixed Disk Control
	     3F7H		  Digital Input	


	     A.	 Data Register

	     Transfers through this register are 16 bits wide for all 
             data transfer except ECC byte transfers during read/write 
             long command, which are 8 bits wide.

	     B.	 Error Register

	     There are two mode in all WDC operation: operational mode and
	     diagnostic mode. The controller is set into diagnostic mode 
             upon power on or receiving a diagnostic command. In diagnostic
             mode, the status register contents are invalid and the error 
             register contents reflects a self test completion code. If bit 
             7 of completion code is set, the slave drive will fail.

		Completion Code		Description

		01H/81H			No error
		02H/82H			Winchester Controller
		03H/83H			Sector Buffer Error
		04H/84H			ECC Device Error
		05H/85H			Control Processor Error






          The controller is set into operational mode by issuing any 
          command other than the diagnostic command. While in operational
          mode, the error register is valid only when the error bit in the
          status register is set. The bit definitions for operational mode
          are shown:

		bit 7		Bad Block
		bit 6		Data ECC Error
		bit 5		Reserved
		bit 4		ID Not Found
		bit 3		Reserved
		bit 2		Aborted Command
		bit 1		Track 0 Error
		bit 0		Address Mark Not Found

	     C.  Write Precompensation Register

	     The Write precompensation register holds the value of the 
	     starting  write precompensation cylinder divided by four. The
	     controller may use this value to determine when to turn on the
	     write precompensation logic.

	     D.  Sector Count Register

	     This register holds the number of sector to be transferred
	     during a read or write command, and the number of sectors per
	     per track during a format command. This register is decremented
	     for every sector during a multi-sector operation. Therefore, if
	     an error occurs during a multi-sector operation, this register
	     contains the number of sectors left to be transferred.

	     E.	 Sector Number Register

	     This register holds the starting sector number for any disk 
	     operation. This register is updated as each sector is processed 
	     in a multi-sector operation.






	     F.  Cylinder Number Register

	     The two eight bit cylinder number registers (Low and High) 
	     specify the starting cylinder argument for disk operation.

	     G.  Drive/Head Register(SDH)

	     This register is used to specify the drive and head number 
	     to be operated on during any following disk operation. During 
	     the set parameters commands it is used to specify the maximun
	     number of heads on the drive. The bits are defined as follow:

		bit 7		Reserved
		bit 6		0
		bit 5		1
		bit 4		Drive select
		bit 3		Reserved
		bit 2-0		Head select
		
	     H.  Status Register

	     This register contains the results of the last command executed
	     and the status of the drive. Reading the status register also
	     clears any interrupt request to the host. The bits are defined 
             as follows:

		bit 7		WDC Busy
		bit 6		WDC Ready to accept command
		bit 5		Write Fault
		bit 4		Seek Completed
		bit 3		Data request
		bit 2		Corrected Data
		bit 1		Index 
		bit 0		Non-coverable error
		





	     I.  Command Register

	     This register contains the code for the command to be performed.
	     All other command information should be written to the task 
             file before the command register is loaded. The BUSY bit in 
             the status register will be set when this register is written. 
             Interrupt request to the host is also cleared when this register 
             is written.
	     Valid command formats are as follows:

		Recalibrate 		0 0 0 1 0 0 0 0
		Seek			0 1 1 1 0 0 0 0
		Read Sector		0 0 1 0 0 0 L R
		Write Sector		0 0 1 1 0 0 L R
		Format Track		0 1 0 1 0 0 0 0
		Read Verify		0 1 0 0 0 0 0 R
		Write Verify		0 0 1 1 1 1 0 0
		Diagnostic		1 0 0 1 0 0 0 0
		Read Buffer		1 1 1 0 0 1 0 0
		Write Buffer		1 1 1 0 1 0 0 0
		Set Parameters		1 0 0 1 0 0 0 1

		L : ECC		R : Retry

	     J.  Alternate Status Register

	     This register contains the same information of the status
	     register. However, this register may be read anytime without
	     clearing a pending interrupt.

	     K.	 Fixed Disk Control Register

	     This register contains the software reset bit and the enable
	     bit to enable interrupt requests to the host. The bits are 
             defined as follows:

		bit 7-3		0
		bit 2		Reset(1 for 5 us minimun)
		bit 1		Interrupt enable
		bit 0		0

	     L.	 Digital Input Register

		 This register contains information about the state of the 
	     drive. The bits are defined as follows:

		bit 7		Reserved
		bit 6		Write Gate status(0 - on, 1 - off)
		bit 5-2		Head Select
		bit 1-0		Drive Select
	




     2.3     Timing Consideration

	     A.	  WDD Start Time & Stop Time

	     The WDD will speed up spindle to desired speed when user
             powers on. 
             The time from power on to spindle settling down is called
	     start time. Do not attempt to issue any command during WDD 
             start time, for it will interfere with WDD self test. Generally
             , the WDD start time is approximately 15 seconds. 
	
	     The WDD will speed down spindle until stopped when powered off. 
             The time from power off to spindle halt is called stop time.
	     Generally, the stop time will be approximately 15 seconds.

	     
	     B.	  WDD Access time & Seek Time

	     The performance of WDD is relative to the access time and seek 
	     Time. Generally, the access time and seek time does not affect
	     the  WDD  programming sequence. In some WDD,  it supports
             different seek speed that is set using seek command.
	
	     C.	  WDD  Restart time

	     In some WDD, it will turn off spindle automatically when it
	     detects unstable condition of the power supply, delay some time
             , and turn on the spindle automatically. The time between turn
             off and on of the spindle is called restart time.  The WDD 
             restart time must be  considered in WDD programming sequence 
             when using CONNER WDD.




3.      Programming Sequence in Fixed Disk Service Program
      
     ;++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
     ;Module_Name: read_sector_hd
     ;Calling Sequence:
     ;
     ;        Input :   AH = 02h
     ;                  AH (in stack) = no_error
     ;                  DL = drive no.(not value check)
     ;                  DH = head no.
     ;                  CH = cylinder low
     ;                  CL =  bit 7-6  -- cylinder high
     ;                        bit 5-0  -- sector no.(1 base)
     ;                  AL = no. of sectors to be read
     ;        output :  AH (in stack) = status of operation
     ;
     ;PDL:    IF WDC valid THEN
     ;           prepare task file
     ;           IF WDC ready THEN
     ;              write READ command to WDC
     ;           ENDIF
     ;           DO 
     ;		   IF interrupt occurred THEN
     ;                read one sector from data register
     ;                get result back
     ;		   ELSE 
     ;		      return error code = 80H (timeout)
     ;		   ENDIF
     ;           UNTIL no data to be transferred
     ;        ELSE
     ;           return error code = 01H (invalid function call)
     ;        ENDIF
     ;+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
     page
      
     f02_00:  ; check valid_WDC
      
           call      valid_wdc            ; check valid_wdc
           jc        f02_60               ; goto f02_40 if error occurred
      
     ;     send read command block to WDC
      
           call      write_data           ; Send command
           mov       ah, 021h             ; BX = 021h for read command
           call      out_com              ; out command byte to WDC
           jc        f02_60               ; goto f02_60 if WDC is not ready
           mov       di, [bp-4]           ; DI = offset of transfer address
           call      wait_drq             ;
           jc        f02_60               ;
      
     f02_20:  ; wait DRQ and test 64K boundary
      
           cmp       di, 0fe00h           ; in 64K boundary
           jb        f02_30               ; goto f02_30 if there is no boundary error
           mov       ax, es               ;
           add       ax, 20h              ;
           mov       es, ax               ; adjust ES
           sub       di, 200h             ; adjust DI
     f02_30:
           call      wait_int             ; wait_interrupt
           jc        f02_60               ; goto f02_60 if time out
           mov       dx, hd_port0         ; data register
           mov       cx, 100h             ; count = 256 words
           cld                            ;
           cli                            ;
           rep       insw                 ;
           sti                            ;
      
     ;     get result back
      
           call      get_result           ; get result byte into AL
           jc        f02_60               ;
           dec       byte ptr [bp-2]      ;
           jnz       f02_20               ;
     f02_60:
           jmp       disk_end
      




             5.      Q & A