Interrupts Table of H/W, BASIC, & DOS

Interrupt       Address   Function      Name            BIOS entry
-----------------------------------------------------------------------
    0             0-3     Divide by Zero        D11
    1             4-7     Single Step           D11
    2             8-B     Nonmaskable           NMI INT
    3             C-F     Breakpoint            D11
    4            10-13    Overflow              D11
    5            14-17    Print Screen          PRINT_SCREEN
    6            18-1B    Reserved              D11
    7            1C-1F    Reserved              D11
    8            20-23    Time of Day           TIMER_INT (IRQ 0) 
    9            24-27    Keyboard              KB_INT    (IRQ 1)
    A            28-2B    Reserved              D11       (IRQ 2)
    B            2C-2F    Communications        D11       (IRQ 3)
    C            30-33    Communications        D11       (IRQ 4)
    D            34-37    Alternate Printer     D11       (IRQ 5)
    E            38-3B    Diskette              DISK_INT  (IRQ 6)
    F            3C-3F    Printer               D11       (IRQ 7)
   10            40-43    Video                 VIDEO_IO
   11            44-47    Equipment Check       EQUIPMENT
   12            48-4B    Memory                MEMORY_SIZE_DETERMINE
   13            4C-4F    Diskette/Disk         DISKETTE_IO
   14            50-53    Communication         RS232_IO
   15            54-57    Cassette              CASETTE_IO/System Extensions
   16            58-5B    Keyboard Service      KEYBOARD_IO
   17            5C-5F    Printer               PRINTER_IO
   18            60-63    Resident BASIC        F600:0000
   19            64-67    Bootstrap             BOOTSTRAP
   1A            68-6B    Time of Day           TIME_OF_DAY
   1B            6C-6F    Keyboard Break        DUMMY_RETURN
   1C            70-73    Timer Tick            DUMMY_RETURN
   1D            74-77    Video Parameters      VIDEO_PARMS
   1E            78-7B    Diskette Parameters   DISK_BASE
   1F            7C-7F    Video Graphics Chars  O
   20            80-83    DOS program terminate
   21            84-87    DOS function call
   22            88-8B    DOS terminate address
   23            8C-8F    DOS Ctrl Break exit address
   24            90-93    DOS fatal error vector
   25            94-97    DOS absolute disk read
   26            98-9B    DOS absolute disk write
   27            9C-9F    DOS terminate, fix in storage
  28-3F          A0-FF    Reserved for DOS
  40-5F         100-17F   Reserved for BIOS
  60-67         180-19F   Reserved for user program interrupts
  68-6F         1A0-1BF   Not used
   70           1C0-1C3   Realtime Clock INT    RTC INT   (IRQ 8)
   71           1C4-1C7   Redirect to INT 0Ah   RE_DIRECT (IRQ 9)
   72           1C8-1CB   Reserved              D11       (IRQ 10)
   73           1CC-1CF   Reserved              D11       (IRQ 11)
   74           1D0-1D3   Reserved              D11       (IRQ 12)
   75           1D4-1D7   Redirect to NMI int.  INT_287   (IRQ 13)
   76           1D8-1DB   Disk hardware INT     HD_INT    (IRQ 14)
   77           1DC-1DF   Reserved              D11       (IRQ 15)
  78-7F         1E0-1FF   Not used
  80-85         200-217   Reserved for BASIC
  86-F0         218-3C3   Used by BASIC interpreter while BASIC is running
  F1-FF         3C4-3FF   Not used