INT 12 - MEMORY_SIZE_DET_I
        MEMORY SIZE DETERMINE 
        This routine returns the amount of memory in the system as determined
        by the POST routine. (Up to 640K)
        Note that the system may not be able to use I/O memory unless there
        is a full complement of 512K bytes on the planar.
INPUT -
        No registers
        The @MEMORY_SIZE variable is set during power in diagnostics 
        according to the following assumptions :

        1. Configuration record in non-volatile memory equals the actual
           memory size installed.

        2. All installed memory is functional. If the memory test during
           POST indicates less, then this value becomes the default.
           If non-volatile memory is not valid (not initialized or battery
           failure) then actual memory determined becomes the default.

        3. All memory from 0 to 640K must be contiguous.