POST - INITIAL RELIABILITY TESTS

TEST.01
        80286 PROCESSOR TEST (REAL MODE)
Description
        Verify Flags, Registers, and Conditional Jumps.
        Check for Processor ShutDown (0 to A)
        SHUT0:

TEST.02
        ROM CHECKSUM TEST 1
Description
        A Checksum is done for the 32K ROM modules (two) 
        containing POST, BASIC and BIOS.

TEST.03
        VERIFY CMOS SHUTDOWN BYTE
Description
        Rolling Bit Written and Verified at Shutdown address.

TEST.04
        8254 CHECK TIMER 1 ALL BITS ON
Description
        Set Timer Count
        Check that Timer 1 all bits on

TEST.05
        8254 CHECK TIMER 1 ALL BITS OFF
Description
        Set Timer Count
        Check that Timer 1 all bits off.

TEST.06
        8237 DMA 0 INITIALIZATION
        CHANNEL REGISTER TEST
Description
        Disable the 8237 DMA Controller 0.
        Write/Read the current DMA 0 address and Word Count Redisters
        for all channels.

TEST.07
        8237 DMA 1 INITIALIZATION
        CHANNEL REGISTER TEST
Description
        Disable the 8237 DMA Controller 1.
        Write/Read the current DMA 1 address and Word Count Redisters
        for all channels.

TSET.08
        DMA PAGE REGISTER TEST
Description
        Write/Read all Page Registers.

TSET.09
        STORAGE REFRESH TEST
Description
        Verify Refresh is occurring.

TEST.10
        8042 INTERFACE TEST
        READ CONFIGURATION JUMPERS
Description
        Isuue a self test to the 8042.
        Insure a 55H is received.
        Read Manufacturing and Display Jumpers and Save in MFG_TEST.

TEST.11
        BASE 64K READ/WRITE MEMORY TEST
Description
        Write/Read/Verify data patterns AA, 55, FF, 01, and 00 
        to 1st 64K of storage. Verify storage Addressability.

TEST.11A
        VERIFY 286 LGDT/SGDT/LIDT/SIDT INSTRUCTIONS
Description
        Load GDT and IDT Registers with AA, 55, 00 and Verify correct.

TEST.12
        VERIFY CMOS CHECKSUM/BATTERY OK
Description
        Determine if Config Record can be used for initialization.

TEST.13
        PROTECTED MODE TEST AND MEMORY SIZE DETERMINE (0 --> 640K)
Description
        This Routine runs in Protected Mode in order to address all of
        storage. It checks the Machine Status Word (MSW) for Protected Mode
        and the Base Memory Size is determined and saved. Bit 4 of the CMOS
        Diagnostic Status Byte is set if 512K --> 640K memory is installed.
        During a Power Up sequence the Memory Size determine is done with
        Plannar and I/O Parity Checks Disabled. During a Soft RESET the 
        Memory Size Determine will check for Parity Errors.
        SHUT8:

TEST.13A
        PROTECTED MODE TEST AND MEMORY SIZE DETERMINE (ABOVE 1024K)
Description
        This routine runs in Protected Mode to address above 1M.
        The Memory Size is Determined and Saved in CMOS.
        During a Power Up sequence the Memory Size determine is done with
        Plannar and I/O Parity Checks Disabled. During a Soft RESET the 
        Memory Size Determine will check for Parity Errors.
        SHUT1:

TEST.14
        INITIALIZE AND START CRT CONTROLLER (6845)
        TEST VIDEO READ/WRITE STORAGE
Description
        Reset the Video Enable Signal.
        Select Alphanumeric Mode, 40 * 25, B & W.
        Read/Write Data Patterns to memory. Check Storage Addressability.
ERROR = 1 Long and 2 Short Beeps

TEST.15
        SETUP VIDEO DATA ON SCREEN FOR VIDEO LINE TEST
Description
        Enable Video Signal and Set Mode, Display a horizontal bar on screen.

TEST.16
        CRT INTERFACE LINES TEST
Description
        Sense ON/OFF Transition of the Video Enable and  
        Horizontal SYNC Lines.

TEST.17
        8259 INTERRUPT CONTROLLER TEST
Description
        Read/Write the Interrupt Mask Register (IMR) with all ones and zeros.
        Enable System Interrupt. Mask Device Interrupts Off. 
        Check for Hot Interrupts (Unexpected).

TEST.18
        8254 TIMER CHECKOUT
Description
        Verify that the System Timer (0) doesn't count too fast or too slow.

TEST.19
        ADDITIONAL READ/WRITE STORAGE TEST (MUST RUN IN PROTECTED MODE)
Description
        Write/Read Data Patterns to any Read/Write Storage after the 1st 64K.
        Storage Addressability is checked.

        SHUT3: Memory Error Reporting (R/W Memroy or Parity Errors)

TEST.20
        ADDITIONAL PROTECTED (VIRTUAL MODE) TEST
Description
        The Processor is put in Protected Mode and the following functions
        are verified

        1.Verify Protected Mode
          The Machine Status is check for Virtual Mode.
        2.Programmed Interrupt Test
          An Programmed Interrupt 32 is issued and verified.
        3.Exception Interrupt 13 Test
          A Descriptor Segment Limit is set to zero and a write to that
          Segment is attempted and Exception 13 is expected and verified.
        4.LDT/SDT LTR/STR Test
          Load LDT Register and Verify correct.
          Load TASK Register and Verify correct.
          They are verified via the STORE Instruction.
        5.The Control Flags of the 286 for Direction are verified via the
          STD and CLD Commands in Protected Mode.
        6.BOUND Instruction Test (Exception INT 5)
          Create a Signed Array Index within and outside the limits.
          Check that no EXC INT if within limit and that and EXC INT 5 occurs
          if outside the limits.
        7.PUSH ALL POP ALL Test
          Set General Purpose Registers to different values, issue a PUSH ALL,
          Clear the Rigisters then issue a POP ALL and verify correct.
        8.Check the VERR/VERW Instructions
          The Access Byte is set to Read Only then to a Write Only and the
          VERR/VERW Instructions are verified.
        9.Cause an Interrupt 13 via a Write to a Read Only Segment
       10.Verify the ARPL Instruction Functions 
          Set the RPL Field of a Selector RPL and verify that current Selector
          RPL is set correctly.
       11.Verify the LAR Instruction Functions
       12.Verify the LSL Instruction Functions
       13.Low MEG Chip Select Test

        SHUT2:
        SHUT7:
        SHUT6:

TEST.21
        KEYBOARD TEST
Description
        Reset the Keyboard and Check that Scan Code "AA" is Returned to the
        Processor. Check for Stuck Keys.

TSET.22
        CHECK FOR OPTIONAL ROM FROM C800->E000 in 2K BLOCKS
Description
        A Valid Module has "55AA" in the first 2 locations, Length Indicator
        (Length/512) in the 3rd location, and Test/Initial Code Starting in
        the 4th location.
<NOTE:> this routine is after the TEST.23.

TEST.23
        DISKETTE ATTACHMENT TEST
Description
        Check if IPL Diskette Drive is attached to System. If attached, verify
        Status of NEC FDC and check Status. Complete System Initialization
        then Pass Control to the Boot Loader Program.

BOOTSTRAP - INT 19H
        BOOT STRAP LOADER
Description
        Track 0, Sector 1 is Read into the Boot Location (0:7C00) and 
        Controll is Transferred there.
        If there is a Hardware Error, Control is Transferred to the
        ROM BASIC entry point.
FLOW:
        1.Reset the Disk Parameter Table Vector (INT 1EH)
        2.Clear @BOOT_LOCN (0:7C00)
        3.Load System From Diskette -- CX has Retry Count 4
        4.If read successful and Boot Record is valid,
          then go to @BOOT_LOCN (0:7C00),
          else loop 3.
        5.Attempt Bootstrap from Fixed Disk -- CX has Retry Count 3
        6.If read successful and Boot Record is valid,
          then go to @BOOT_LOCN (0:7C00),
          else loop 5.
        7.INT 18H -- Go to RESIDENT BASIC