AIDS

 Virus Name:  AIDS
 Aliases:     Hahaha, Taunt, VGA2CGA, Burger.Pascal
 V Status:    Endangered
 Discovery:   1989
 Symptoms:    Message; .COM file corruption
 Origin:     
 Eff Length:  N/A
 Type Code:   ONA - Overwriting Non-Resident .COM & .EXE Infector
 Detection Method:  ViruScan, VirexPC, AVTK, F-Prot, CPAV, NAV, Sweep,
                    UTScan, AllSafe, ViruSafe, IBM Scan, VBuster 3.92+,
                    Trend, VNet, Panda
 Removal Instructions:  Delete infected .COM files

 General Comments:
       The AIDS virus, also known as the Hahaha virus in Europe and
       referred to as the Taunt virus by IBM, is a generic .COM and
       .EXE file infector.  When the virus activates, it displays the
       message "Your computer now has AIDS", with AIDS covering about
       half of the screen.  The system is then halted, and must be
       powered down and rebooted to restart it.  Since this virus
       overwrites the first 13,952 bytes of the executable program, the
       files must be deleted and replaced with clean copies in order to
       remove the virus.  It is not possible to recover the overwritten
       portion of the program.

       Note: this is NOT the Aids Info Disk/PC Cyborg Trojan.

       Known variant(s) of AIDS are:
       AIDS B: Very similar to the original AIDS virus, this variant is
               also 13,952 bytes in length.  Unlike the original virus, it
               will only infect .COM files, as well as COMMAND.COM, and
               does not activate as the original virus did.  Instead, this
               variant will occasionally issue the following error message:
               "I/O error 99, PC=2EFD Program aborted". This variant was
               received in January, 1991, origin unknown.
       AIDS-1992: Isolated at several locations in the United States in
               May, 1992, this variant of the AIDS virus has been altered to
               avoid detection by anti-viral utilities.  Among the changes
               to the virus are that it will not infect files if there are
               less than two subdirectories on the current drive.  System
               hangs may occur when infected programs are executed, as well
               as the system video mode may be switched to 25 x 40 Black &
               White from color mode.
               Origin:  United States  May, 1992.

       See:   Number One