***************************************************************************
*   Instructions for using "medplayer.library" V2, by Teijo Kinnunen      *
***************************************************************************

"medplayer.library" is a shared library, which can be used to load and play
MED/OctaMED  4-channel modules You can call its functions from any language
which supports library calls (C, Assembler, Basic...)
(Note:  All functions must be called by the same task that opened the
	library (using GetPlayer()). The library uses the task pointer
	to keep track of the current user of the library.)

First  you  must  install  "medplayer.library" to your LIBS:  drawer (click
Install_Libraries  to  do that).  You can also load it with ARP's "loadlib"
command.

The main advantage of using medplayer.library instead of modplayer.a player
routine  is  that you won't have to modify your program when new MED player
routines   are   released.    The   user   will   just   have   to  replace
medplayer.library  and  ZAP...   (sorry,  ZAP ;-) your program will support
HexaMED  V63.132  (or  whatever  :-)  modules...   At the moment of writing
(1.1.1992)  I  have been working on OctaMED Professional, which will have a
new  module  format  incompatible  with  MMD0  (it'll be MMD1).  If you use
medplayer.library, your programs will be compatible with MMD1s.

There's  a  header  file  'libproto.h'  that  contains  the  prototypes and
#pragmas for use with SAS/Lattice C V5.

Here's  the  complete  list of the functions in "medplayer.library" (in RKM
autodoc-style):

---------------------------------------------------------------------------
---------------------------------------------------------------------------

GetPlayer

NAME
	GetPlayer -- get and initialize the player routine

SYNOPSIS
	error = GetPlayer(midi)
	D0                D0

FUNCTION
	This routine allocates the audio channels and CIAB timer A/B
	and prepares the interrupt. If "midi" is nonzero, serial
	port is allocated and initialized. You should call this
	routine when your programs starts up.

INPUTS
	midi =  0 no midi, 1 set up midi. When you use a song that
		has only Amiga samples, there's no reason to allocate
		the serial port. Then set midi to 0.

RESULT
	If everything is OK, GetPlayer() returns zero. If initialization
	failed or somebody else is currently using the library, then
	GetPlayer() returns nonzero value.
	NOTE: Even if GetPlayer() returned an error, you can still call
	      the library functions without making harm. They just won't
	      work (except LoadModule(), UnLoadModule(), RelocModule()
	      and GetCurrentModule(), which always work).

SEE ALSO
	FreePlayer

---------------------------------------------------------------------------
---------------------------------------------------------------------------

FreePlayer

NAME
	FreePlayer -- free the resources allocated by GetPlayer()

SYNOPSIS
	FreePlayer()

FUNCTION
	This routine frees all resources allocated by GetPlayer().
	Remember always call this routine before your program
	exits. It doesn't harm to call this if GetPlayer() failed.
	If you don't call this function during exit, audio channels,
	timer etc. will remain allocated until reboot.

SEE ALSO
	GetPlayer

---------------------------------------------------------------------------
---------------------------------------------------------------------------

PlayModule

NAME
	PlayModule -- play module from the beginning

SYNOPSIS
	PlayModule(module)
		   A0

FUNCTION
	This routine starts to play the module from the beginning.
	The module can be obtained by calling LoadModule() or it can
	be incorporated directly into your program. The module has to
	be relocated before calling PlayModule()!

INPUTS
	module = pointer to the module.

SEE ALSO
	ContModule, StopPlayer

---------------------------------------------------------------------------
---------------------------------------------------------------------------

ContModule

NAME
	ContModule -- continue playing the module from where it stopped

SYNOPSIS
	ContModule(module)
		   A0

FUNCTION
	ContModule() functions just like PlayModule() except if you
	have stopped playing with StopPlayer(), the playing will
	continue where it stopped. When you play the module first
	time, you should use PlayModule().

INPUTS
	module = pointer to module.

SEE ALSO
	PlayModule, StopPlayer

---------------------------------------------------------------------------
---------------------------------------------------------------------------

StopPlayer

NAME
	StopPlayer -- stops playing immediately

SYNOPSIS
	StopPlayer()

FUNCTION
	Stop.

SEE ALSO
	PlayModule, ContModule

---------------------------------------------------------------------------
---------------------------------------------------------------------------

DimOffPlayer

NOTE
	This is an obsolete function! It was removed in V2 of the library,
	and it now just does StopPlayer()!

---------------------------------------------------------------------------
---------------------------------------------------------------------------

SetTempo

NAME
	SetTempo -- modify the playing speed

SYNOPSIS
	SetTempo(tempo)
		 D0

FUNCTION
	If you want to modify the playback speed, you can call this one.
	The tempo value should be 1 - 240. Note that tempos 1 - 10 are
	recognized as SoundTracker tempos. This function usually has no
	use.

INPUTS
	tempo = new tempo

---------------------------------------------------------------------------
---------------------------------------------------------------------------

LoadModule

NAME
	LoadModule -- load a MED module from disk and relocate it

SYNOPSIS
	module = LoadModule(name)
	D0                  A0

FUNCTION
	When you want to load a module from disk, call this function.
	The function loads only MED modules (MMD0). It doesn't load
	Tracker-modules, MED songs or object files. Only MMD0's
	(MMD0 is the identification word at the beginning of the file).
	Because the module contains many pointers, they must be
	relocated. This function relocates the module automatically.
	If you include the module as a binary file converted with
	Objconv, YOU must relocate it. This is an easy thing to do.
	Just call RelocModule().

INPUTS
	name = pointer to file name (null-terminated)

RESULT
	module = pointer to module. If failed to load for some reason
		 (disk error, out of memory, not a module), zero will
		  be returned.

SEE ALSO
	UnLoadModule

---------------------------------------------------------------------------
---------------------------------------------------------------------------

UnLoadModule

NAME
	UnLoadModule -- frees the module from memory

SYNOPSIS
	UnLoadModule(module)
		     A0
FUNCTION
	When you don't need the module anymore, you MUST free the
	memory it has used. Use this routine for it. Remember to
	stop the player before unloading the module it is playing.

	NOTE: unload only those modules which are loaded with
	LoadModule(). If you attempt to free module which is a part
	of the program, you will cause guru 81000009/81000005.

INPUTS
	module = pointer to module. If zero, nothing happens.

SEE ALSO
	LoadModule

---------------------------------------------------------------------------
---------------------------------------------------------------------------

GetCurrentModule

NAME
	GetCurrentModule -- returns the address of module currently playing

SYNOPSIS
	module = GetCurrentModule()
	D0

FUNCTION
	Simply returns the pointer of the module, which is currently
	playing (or if player is stopped, which was played last). This
	works also if some other task is currently playing. In this case,
	because of multitasking, you should have no use for the value
	(the module can be already unloaded). You may ask what use this
	function has. Well, I'm not sure, but because this function
	takes only 2 machine language instructions (8 bytes of memory)
	there's not much harm of it.

RESULT
	module = pointer to current module

---------------------------------------------------------------------------
---------------------------------------------------------------------------

ResetMIDI

NAME
	ResetMIDI -- reset all pitchbenders and modulation wheels and
		     ask player to resend the preset values

SYNOPSIS
	ResetMIDI()

FUNCTION
	This function resets pitchbenders and modulation wheels on all
	MIDI channels. It also asks the player to send again the
	preset change requests for all instruments, so that the presets
	will be correct if the user has changed them. It performs the
	same function as MED's Ctrl-Space.

---------------------------------------------------------------------------
---------------------------------------------------------------------------
NOTE: THE FOLLOWING FUNCTIONS ARE ONLY AVAILABLE IN MEDPLAYER.LIBRARY V2
OR LATER, BE SURE THAT YOU'RE REALLY USING V2 OF THE LIBRARY
e.g.  MEDPlayerBase = OpenLibrary("medplayer.library",2);
---------------------------------------------------------------------------
---------------------------------------------------------------------------

SetModnum

NAME
	SetModnum -- select the number of the song (in multi-module)

SYNOPSIS
	SetModnum(modnum)
		  D0

FUNCTION
	Use this function to set the number of song you want to play.
	Call this before PlayModule(). 0 is the first song, 1 is the
	second, and so on. If the module is not a multi-module, this
	function has no affection.

---------------------------------------------------------------------------
---------------------------------------------------------------------------

RelocModule

NAME
	RelocModule -- relocate module

SYNOPSIS
	RelocModule(module)
		    A0

FUNCTION
	This function relocates the module. It should be used if you've
	incorporated the module with Objconv program before using the
	module. Note that LoadModule() automatically relocs everything.

---------------------------------------------------------------------------
***************************************************************************